## Slide 1: Lecture Learn Docs and Takeoff

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Explain the Autodesk Construction Cloud (ACC) ecosystem.
Navigate the ACC web interface efficiently.
Open and explore models and sheets in Docs.
Leverage the Model Browser and Properties panels.
Detect and communicate design changes.
Create and manage Issues.
Set up Takeoff Packages.
Define and duplicate 2D and 3D Takeoff Types.
Analyze and export quantity results.

## Slide 3: Common terms
  Model Browser – A hierarchical tree that lets you filter, isolate, and select elements by level, category, family, or type.
  Type Properties – Shared parameters that apply to every instance of a given family/type (e.g., size, material).
  Instance Properties – Element-specific parameters (e.g., Mark) that differ from one placed element to another.
  Classification System – A coding framework used to tag quantities so they stay organized and comparable.
  Version Comparison – A color‑coded diff view that highlights added, removed, or modified elements between file versions.
  Markups – Graphic annotations (clouds, arrows, notes) used to visually call out issues or clarifications on sheets/views.
  Issues – Trackable tickets pinned to a location that log a problem or question, its status, assignee, and supporting files.
  Package (Takeoff Package) – A scoped container that holds quantification types, individual measurements, and revision history for a trade or task.
  Takeoff Type – A reusable template that defines what is being counted or measured (tool, outputs, classification) so quantities calculate consistently.
  Inventory Pane – The roll‑up view that aggregates all quantities in order to regroup or export them for reporting.

## Slide 4: Why Autodesk Construction Cloud?
Single source of truth for every project, from design through handover on one data platform.
Cloud-native collaboration from any device, anywhere.
Streamlines end-to-end construction workflows: design, coordination, field, and turnover.
Trusted by thousands of contractors, designers, and owners worldwide.

## Slide 5: The ACC product line-up
Product | Core Function | Typical Users
Docs | Centralized file management, version control, mark-ups, issues | Entire project team
Build | Package-based model exchange, timeline tracking, and change visualization across disciplines | Architects, engineers, BIM leads, VDC managers
Takeoff | Automated clash detection and issue tracking directly in the browser | VDC coordinators, BIM managers
Design Collaboration | Unified 2D & 3D quantity takeoff with classification mapping and live inventory | Estimators, pre-construction teams
Model Coordination | Field execution tools: RFIs, submittals, daily logs, cost & schedule tracking | PMs, supervisors, foremen, field engineers
Insight | Dashboards, analytics, and machine-learning–driven risk indicators across projects | Project executives, PMs, quality & safety leads

## Slide 6: Autodesk Docs User Interface
Product Picker: Allows you to navigate between ACC modules (Docs, Takeoff, Build, Design Collaboration, Model Coordination, Insight).
Project Selector: Lists every project you’re a member of; switch context in one click.
Folders Pane: Shows the folder tree for the current project. Right-click the three dots ( ⋮ ) to add sub-folders or adjust permissions.
Upload Files: Drag-and-drop or browse to add PDFs, RVTs, DWGs, IFCs, etc. Versions auto-stack when you upload a file with the same name.
File Table: Displays every file in the selected folder, with indicators for mark-ups, versions, and reviews.
User Menu: Access profile settings, notifications, help, and Sign Out.

## Slide 7: Autodesk Docs: What it solves
Automated versioning & change history.
Markup import from AutoCAD & PDF, rich 3D issue call-outs.
Granular folder-level permissions.
Integrated issues list that feeds Build & Model Coordination.
Approval workflows for submittals & design packages.

## Slide 8: Autodesk Docs: Working with 2D sheets
Left toolbar: Use these icons to jump between sheets or 3D views, filter the model by category or level, review all mark-ups, track open issues, and locate tagged assets. Everything you need for navigation and coordination lives here.
Top-left version selector: Click the file name drop-down to switch between published versions of the sheet.
Bottom viewer toolbar: Pan, zoom, fit-to-view, measure distances or areas, and open the Properties panel; think of it as your toolkit for interacting with and inspecting the drawing itself.
Right toolbar: Create markups (rectangles, clouds, callouts) or drop an issue pin to capture feedback.
Compare tool: Use the compare tool (upper-right) to overlay or side-by-side two sheet versions, with added, removed, and modified elements auto-highlighted so design changes are crystal-clear.

## Slide 9: Autodesk Docs: Working with 3D models
Model Browser: Navigate the entire Revit model tree, filter by level, category, or discipline, and isolate specific elements; selecting an item here highlights it in the viewer for focused inspection.
Bottom Viewer toolbar: Access core view controls (pan, orbit, zoom), activate section analysis to slice the model, launch measurement tools, and toggle the Properties pane. All the interaction tools for 3D exploration in one strip.
Properties panel: Displays type and instance data for any selected object: dimensions, materials, phase, and custom parameters, so you can verify design intent or gather quantities directly from model metadata.
ViewCube: Click or drag this cube to snap to orthographic views, orbit freely, or reorient to any face, making it easy to understand spatial relationships from multiple angles.
Compare tool: Use the compare tool (upper-right) to overlay or side-by-side two model versions, with added, removed, and modified elements auto-highlighted so design changes are crystal-clear.

## Slide 10: Autodesk Takeoff
Single quantification workspace: combine 2D drawings and 3D models in one tab.
Shared classification system for cost codes (e.g., UniClass, Uniformat).
Live inventory pane aggregates quantities by type, location, or CSI code.
Export clean spreadsheets for Excel or cost platforms.

## Slide 11: ACC Takeoff workflow
Create Package
Set measurement & classification system
Publish Drawings/Model
From Docs
Define Takeoff Types
Count, linear, area, BIM
Measure & Assign
Review Inventory, Export

## Slide 12: ACC Takeoff toolbar
Create a Takeoff package, assign classification and measurement systems
Access your files in Docs or browse locally to publish sheets & models to Takeoff
Publishes and lists every 2D sheet and 3D model that will be measured.
Generates pre-built and custom quantity outputs.
Project-wide configuration
Project team management

## Slide 13: Autodesk Takeoff: User Interface
Takeoff Types panel: Displays every takeoff type you have already defined, organized by package and classification, so you can quickly select, edit, or filter quantities for measurement.
New Takeoff Type (+): Click the plus icon to create a new takeoff type; you’ll choose its name, output, measurement method (linear, area, count, etc.), color, and classification before it appears in the list.
Inventory pane: Open the inventory icon at the bottom-left to view live totals for every takeoff object. The pane groups quantities by classification, takeoff type, or location, and updates instantly as you add or edit measurements: perfect for spot-checking counts before exporting.
Bottom toolbar: Houses viewer controls (orbit, pan, zoom, fit-to-view), measurement tools, section-analysis toggles, and shortcuts to open/close the Model Browser and Properties panels.
Properties panel: Reveals detailed metadata for the selected element (type mark, family, size, material, manufacturer, URL, and more), helping you verify that you’re quantifying the correct components.

## Slide 14: Autodesk Takeoff: Create a Takeoff type
Primary Output:
Fill output name (what the quantity represents, e.g., area, length, EA).
Unit of Measure (LF, CY, m2, etc.)
Cost: Enter unit cost if desired.
Classification
Formula: optional expression if the output is derived.
Name: A clear, descriptive label for the Takeoff type
Pick the measurement tool:
For 2D takeoffs, use Count, Linear, or Area.
For 3D takeoffs, use BIM.
Additional Outputs: capture secondary metrics from the same measurement, such as count, area, length, or weight. Each extra output opens the same output detail panel so you can define its name, unit, cost, and classification.
Hit Save to finish, or Start Takeoff to activate the chosen measurement and begin quantifying

## Slide 15: Takeoff Type Tools: When to use what
Area: For surfaces you outline (e.g., slab foundations, floor finishes); captures area and can drive secondary outputs like volume with a specified thickness.
Linear: For length-based elements you trace along a path (e.g., wall footings, curbs, piping); outputs can include length plus calculated volume if depth/width are defined.
Count: For discrete items on 2D sheets (e.g., columns, fixtures); click each symbol once and totals update automatically.
BIM: For 3D takeoff: selects model elements and pulls quantities (count, volume, area, etc.) directly from their Revit properties, with no tracing required.

## Slide 16: Autodesk Takeoff: Inventory
Totals list: Shows aggregated quantities; click any line to expand and reveal its individual instances.
Instance panel: Displays each measured object; select one to zoom/highlight it in the model or delete if it was placed incorrectly.
“Group By” menu: Regroup totals by Classification, Takeoff Type, Location, or Document to see quantities from different perspectives.
Export: Downloads the current inventory to a CSV spreadsheet for reporting or further analysis.
Pop-out window: Opens the Inventory in a separate, resizable window so you can keep totals visible while working elsewhere.