## Slide 1
Developing existing conditions lecture

## Slide 2: Sections in this lecture
Establish existing conditions
Create site limits and constraints

## Slide 3
Establish existing conditions

## Slide 4: Learning objectives
After completing this lecture, you’ll be able to:
Edit objects in the base and a proposal and recognize the differences between them.
Revise context to match form and height of adjacent buildings.
Create and size trees in a project.
Create a collaborative workspace to accelerate matching existing conditions with a team.

## Slide 5: Edit Base model
Open the 311 Mcdaniel project.
Double-click on any of the geometry on the base to edit.
Left-click to select a building, right-click on the selection and select Delete.
Notes: Start by double clicking on any of the building forms to the south of the site. This will allow you to edit the base model. If you have not yet deleted the row of buildings to the south of our site, go ahead and do that now, by selecting the building objects, right clicking, and choosing delete, or using the delete button on your keyboard.

## Slide 6: Verify existing conditions
Verify height from source material such as:
  Google Earth
  Site visit
  ARC GIS
  Open Street Map
  City maps
Notes: Use Google Earth for site verification, so you can switch to that now. However, you could also use data collected from a site visit, data from ARC GIS or Open Street Map, or even researching heights through local city maps. The key thing here, is getting familiar with the site – and while nothing is better than visiting the site in person, Google Earth will get everyone not in Springfield on the same block. In Google Earth, hover over the edge of a building and then then the edge of the ground plane – subtract the values (these will be height above sea level) to get the height of the building, tree, or other contextual element.

## Slide 7: Model existing conditions
Select Generic Volume from the Design toolbar.
Trace the footprint of the building to be modeled.
Wherever possible and applicable, use right angles.
Right-click to finish base.
Pay attention to topography!
Notes: Trace the overall perimeter of the building by selecting Generic Volume from the Design toolbar, then with the pen tool selected, left click of the mouse, while drawing, as most buildings in this project will be square, make sure you are seeing the snap symbol that represents a 90 degree relationship to the previous line.

## Slide 8: Input height of existing building
Input height from source material (such as Google Earth) and click enter.
Repeat this process to quickly generate the existing context of any buildings or site context that will be relevant to simulations and the site layout.
Notes: Input height from source material.

## Slide 9: Add trees and adjust tree parameters
Add trees with either the Tree line or Area with tree tools in the Design Toolbar.
Adjust tree parameters in the analyze tab, with variables for height and spacing.
Notes: Input height from source material.

## Slide 10: Create a collaborative workspace
Select the collaboration tool in the top-right corner.
Add emails and set work parameters (Manager, Editor, or Viewer).
Notes: At the top right, click the icon with the three people in the small football huddle. The person that has started the project is the manager by default. Click the plus icon, add emails and each members roles - most likely that of an editor, to a team so you can work through the existing conditions of the site. Make sure everyone is working in the base layer, that the block by block work is neatly organized, and the entire site will be completed in less than an afternoon.

## Slide 11
Create site limits and constraints

## Slide 12: Learning objectives
After completing this lecture, you’ll be able to:
Create site limits and constraints.
Determine a proposal’s impact on adjacent site elements and buildings.
Run a solar hours analysis.

## Slide 13: Establish constraints
Select Constraint from the Design Toolbar.
Select existing site limit.
Set Height to 100’ (30 meters).
Notes: To set up a 3d constraint – make sure you are editing the base, go to the design tool bar top and center, and select constraint. Because you have already drawn your perimeter, you can select the trace existing shape tool, select the site limit, and then enter 100’ (30 meters) into the dialog box to create the vertical constraint.

## Slide 14: Create a Basic building model to test sun hours
Create new proposal.
Select Basic building from the Design Toolbar.
Trace out a building footprint the approximate size of the site.
Set the Height to 100’ (30 meters).
See next slide for overall form…
Notes: Along the northern edge of the property, create a basic building and make it 100’ (30 meters) tall – the maximum height allowed.

## Slide 15: Create a Basic building model to test sun hours
Completed building proposal.
  Form along north edge of site.
  100’ (30 meters) tall.

## Slide 16: Analyze sun hours for the summer solstice
On the Analyze Panel, Select Sun hours.
Verify that Entire model is selected to run the simulation on.
Set the date to June 21.
Click Run analysis.
Notes: On the analyze panel, select sun hours, verify that the analysis area is set to the entire model, set the date to the summer solstice – June 21, and let’s run a daylight hours simulation.

## Slide 17: View sun hours analysis results
Select View Results once the simulation is completed.
Use the Inspect tool to label results on the buildings adjacent, and to the north of our site.
Notes: Observe that most surfaces with windows are still receiving 7 or more hours of sunlight per day. Note that this is the summer solstice – the sun is the highest in the sky relative to the site, and it is the longest day of the year in the northern hemisphere.

## Slide 18: Run sun hours analysis for winter solstice
Rerun the Sun hours simulation for the winter solstice – December 21.
Select Run analysis.
Select view results once completed.
Notes: Rerun the Sun hours simulation but this time for the winter solstice, Dec 21. View the results once completed

## Slide 19: View sun hours analysis results
Use the Inspect tool to label the south walls of the buildings to the north of our site.
Note the difference in sun hours between the winter and summer solstice.
Notes: Opening this analysis from the history, you can note that this is kind of a disaster. The majority of the south facing surfaces on the adjacent building with windows receive no sun light at all.