## Slide 1
Create mass models of design proposals lecture

## Slide 2: Sections in this lecture
Design basic mass models
Model a building with 3D sketch

## Slide 3
Design basic mass models

## Slide 4: Learning objectives
After completing this lecture, you’ll be able to
Create basic buildings in Forma Site Design.
Create floor levels.
Create specific functions in levels, varying form and function.

## Slide 5: Building Program
Lower Level
  10,000 sqft (930 sq m) leasable commercial space with café and outdoor seating, including two commercial office spaces. Parking is adjacent in garage across the street to the south.
Upper Levels (4)
  Circulation (+/- 20%) 8000 sqft (740 sq m)
  4x small studio apartments (500 sqft each) – 2000 sqft total (185 m sq)
  10x One Bedroom Units (750 sqft each) – 7500 sqft total (700 m sq)
  6x Two Bedroom Units (1250 sqft each) – 7500 sqft total (700 m sq)
  Community Kitchen and Roof Deck – Upper Level – 1000 sqft (90 m sq)
  Workout Room – 500 sqft (50 m sq)
  Laundry – 250 sqft (25 m sq)
  Mail/Common Room on Lower Level – 500 sqft (50 m sq)

## Slide 6: Create building footprint in Proposal 1
Select Proposal 1, and remove any existing geometry.
Select Basic building in the Design toolbar.

## Slide 7: Create the L shape footprint
On the west side of the site, create the building base with dimensions as noted on the image to the right:
Press Enter to complete the footprint and create a single level.
120’
90’
40’
60’
100’
30’

## Slide 8: Set Building function
Set the function of the single story to Commercial.

## Slide 9: Modify floor-to-floor height
Set the floor-to-floor height to 16’ (5 m) to match existing storefront context in the area.

## Slide 10: Add levels
Set levels to 3.
Modify floor-to-floor height for levels 2 and 3 to 12’ (3.5 m) each.

## Slide 11: Add second floor terrace
Select the southeast face of both floor 2 and floor 3, and move west 20’ (6 m) to create roof terrace

## Slide 12: Add levels four and five
Change the number of levels to five.

## Slide 13: Create fifth floor roof terrace
Select the northeast face of the fifth floor and move it to the west 30’ (9 m) to create a roof terrace for the fifth floor.

## Slide 14: Change function
Select floors 2-5 and set their function to Residential.

## Slide 15: Edit floor plans
Select the first floor and left-click on floor plan.
This will allow you to divide the lower level into more than one type of function.

## Slide 16: Edit floor plans
Select the line tool.
Draw a line from north to south to divide the lower-level plan into two sections.

## Slide 17: Change functions on a single level
Select the entire east side by drawing a lasso around the space.
Select Function, then Create new function.

## Slide 18: Create new function
Click the plus sign to add a new function.
Name the function café.
Set the color to pink(ish).
Select the back arrow in the top left to go back to the 3D canvas view.

## Slide 19: Back to 3D view
You can now see the functional spaces represented by a change in color.
You will also be able to see a break down of the spaces and area in the Analyze panel under metrics.

## Slide 20
Model a building with 3D sketch

## Slide 21: Learning objectives
After completing this lecture, you’ll be able to:
Describe when additional formal complexity will shape simulation data.
Draw outside of the plane view on the Forma canvas.
Modify a basic building massing form by drawing and using sketch lines and advanced modeling tools.

## Slide 22: Add proposal 2
Create a new proposal, and name it Proposal 2, or delete the geometry from your existing Proposal 2 to start with a clean canvas.

## Slide 23: Create a terrain pad
Click the Terrain Pad tool from the Design Toolbar top and center.
This will help level out the eastern portion of the site.

## Slide 24: Establishing cut and fill
Using the Terrain Pad tool, click at around the middle of site at an approximate elevation of 1312’ above sea level.
Left-click to place points at: north-center, northeast corner, southeast corner, and south-center of the site. Press Enter to complete the terrain pad.

## Slide 25: 3d Sketch building tool
Select the 3d Sketch building tool from Design toolbar.
3d Sketch building differs from the Basic building tool in the following ways:
  Open ended
  Freeform modeling
  Less automation
Notes:   Open ended – you can start the process from a line, a cube, or a set of 2d lines
  Freeform modeling – you can push pull and carve forms
  Less automation – metrics are not automated, and floor plans need to be generated based on volumes

## Slide 26: Create a cuboid base
Select the Cuboid tool.
Draw an 80’ (24m) by 180’ (55 m) box.
Set the height to 16’ (5m).

## Slide 27: Carve the cube
Draw a three-point arc along the southwest edge on the roof plane.
Select the triangle shaped polygon along the arc.
Push that shape down to subtract the form, leaving a curved edge.

## Slide 28: Subdivide the west wall
Draw a vertical line along the western elevation. This line subdivides the geometry on the west into two pieces.
Select the northern part of the west elevation.

## Slide 29: Push a wall to modify form
With the north west face selected, inset the surface by pushing it east 20’ (6m).

## Slide 30: Subdivide roof surface
Draw a line across the roof surface to subdivide it into east and west surfaces.

## Slide 31: Extrude roof for levels 2 and 3
Select the east side roof polygon.
Pull this section of the roof up 24’ (7m).

## Slide 32: Subdivide roof with spline
Subdivide the newly formed roof with the spline tool.
This will create a second roof top exterior space on the third floor of the residential spaces.

## Slide 33: Extrude roof for levels 4 and 5
Pull the eastern side of the roof up 24’ (7m).
This will create a curvilinear wall that faces an exterior roof common space for tenants.

## Slide 34: Push roof surface to create private roof deck
Use either the line tools, or the rectangle tool to draw a 20’ x 30’ (6m x 9m) rectangle on the roof.
Push the rectangle down 12’ (3.5m) to form a private roof deck for an upper level residential space.

## Slide 35: Add floors to 3d Sketch
With the overall form selected (make sure you are still editing the 3D Sketch) set floors to 5.
Set level one to 16’ (5m), and levels 2-5 to 12’ (3.5m).
Notes: If the floor tools are not available, you likely need to select the building massing form, right click, and select Edit in 3d Sketch

## Slide 36: Edit floor plan 1
Select Floor plan 1 to edit the entry level plan.

## Slide 37: Divide floor plan
Draw a line from north to south to divide level one into an east and west side for two different functions.

## Slide 38: Set entry level functions
Draw a line from north to south to divide level one into an east and west side for two different functions.
Left-click and drag a lasso around the west side.
Select function, and set the west side to café.

## Slide 39: Second level plan functions
Select the 2nd Floor plan.
Draw a line that divides the plan into east and west sides close to the west edge.
Lasso select the west side of the second floor.
Set the function to café.

## Slide 40: Second level plan functions
Lasso-select the east side of the second floor plan.
Select Function, and set it to Residential.

## Slide 41: Exit floor plan editing
Click the top left back button to exit the floor plan editing screen.

## Slide 42: Set function for levels 3, 4 and 5
Select levels 3, 4, and 5.
Set their Function to Residential.