## Slide 1
Create core analysis simulations lecture

## Slide 2: Sections in this lecture
Perform a sun analysis
Run a daylight potential simulation
Perform a wind analysis
Run a microclimate simulation

## Slide 3
Perform a sun analysis

## Slide 4: Learning objectives
After completing this lecture, you’ll be able to:
Run the sun hours simulation and label measurable results.
Describe what the sun hour values represent.
Study the impact of a design proposal on surroundings.
Explain how sun hours impact future design decisions.

## Slide 5: Insights from the Sun hours analysis
Notes: Sun Hours:
We do this first, for human health and comfort. Natural daylight has been shown many times over to promote health, wellbeing, and productivity.
We can leverage the solar envelope to help with building energy efficiency – both in terms of interior illumination, and for leveraging solar heat gain, and solar shading.
This data will help determine building location on the site, orientation, the size of the windows as well as the overhangs and shading at building openings, and the ability to control contrast and glare.

## Slide 6: Sun hours analysis
Run sun hours analysis. Data will show hours of sunlight on a surface

## Slide 7: Set parameters for sun hours analysis simulation
Set sun hours simulation parameters by selecting either:
  Entire model will run sun hours on every surface (other than the ground plane)
  Site limit will run sun hours only on objects in the site limit.
Notes: This simulation

## Slide 8: Set date for sun hours simulation
Set sun hours simulation parameters by selecting a date, a good starting point would be:
  Summer Solstice - June 21.
  Winter Solstice – December 21.
  Equinox – September 22 or March 20.
Notes: Summer solstice for the northern hemisphere will provide the longest day of the year, and potentially the highest value of sun hours during the hottest time of the year, with the sun the highest in the sky (shorter shadows). The winter solstice will provide the hours over the shortest day of the year in the northern hemisphere with the sun lowest in the sky. Either equinox date is your average.

## Slide 9: Run analysis
Select Run analysis.
This simulation will should take a few seconds, perhaps just over a minute to run

## Slide 10: View analysis result
Select View Result.
This will open up a new window, with the sun hours data mapped onto the 3D geometry in the canvas

## Slide 11: View analysis results
In the results:
  Note the date, results can change drastically based on the date.
  Review the Highlights for an overview of all surfaces, including the ground plane
  The graph at the bottom shows the color relating to hours of sunlight on a surface

## Slide 12: Compare proposals in side-by-side view
Close the results window, and move to a side-by-side comparison view. Click Forma Site Design in the upper-right corner and click Compare.

## Slide 13: Compare proposals in side-by-side view
Inside of Compare, close the Area Metrics view by clicking the “x”.

## Slide 14: Compare proposals in side-by-side view
Under Proposal 1 and Proposal 2, select the latest version of Sun hours.
This side-by-side comparison will work for different proposals, and date variations of the same proposal, allowing for studies of summer versus winter sun.

## Slide 15: Compare proposals in side-by-side view
Use the Label tool to tag specific locations within your model for precise read outs of Sun hours.

## Slide 16
Run a daylight potential simulation

## Slide 17: Learning objectives
After the lecture, you’ll be able to:
Perform Daylight potential simulations.
Label the measurable results.
Describe the definitions and values of daylight potential.
Explain the impact on the interior spaces and envelope systems in your design.

## Slide 18: Daylight potential
Notes: There are definite crossovers between sun hours and daylight potential, but there are also fundamental differences in the type of data created that are important to understand. First, Sun hours are counted through a direct connection between a surface and the solar envelop. Sun hours do not account for indirect or ambient light as part of their solution. Daylight potential assumes an overcast sky, and is calculating direct, indirect (or light bounces), and ambient light.
Daylight potential helps anticipate the quality of interior light by looking at the VSC (Vertical Sky Component) score on a surface. Early in the design phase this number helps establish the type of programmatic functions adjacent to exterior walls. The configuration of window systems (glass specifications, size, and constructed elements like light shelves to help with interior illumination). Understanding the balance between artificial light and daylight. And similar to sun hours, this can also help establish the building location on the site, and building orientation in relationship to the sun.

## Slide 19: Daylight Potential analysis
Select Daylight potential analysis.
  Data created will show access to daylight on facades
  The simulation is run on a date close to the spring equinox, using an overcast sky for balanced data
Notes: This simulation

## Slide 20: Set the site limit
Verify that the simulation will be run on the site only
  This will limit the data to the building massing in the site limit
Notes: This simulation

## Slide 21: Run sun hours analysis
Select Run analysis to launch the simulation
  This should be a fast process – just a few minutes
Notes: This simulation

## Slide 22: Set up comparison view
Select Compare
  While not necessary for every Daylight potential analysis, Compare allows a side by side evaluation of different proposals
Notes: This simulation

## Slide 23: Select simulations for analysis
Select multiple versions of the latest Daylight potential analysis.
The data displayed is the is based on the Vertical Sky Component (VSC), which is the amount of illumination on a vertical surface
Use the Inspect tool for precise labels
Notes: This simulation

## Slide 24: Observe the Daylight potential analysis
Greater than a 27% score suggests that standard windows will provide adequate interior daylighting
15-27% requires design attention to improve interior daylight
Less than 15% will likely not provide adequate interior daylight illumination
Notes: This simulation

## Slide 25
Perform a wind analysis

## Slide 26: Learning objectives
After this lecture, you’ll be able to:
Run both rapid and detailed wind simulations and describe the differences between each approach.
Label the measurable results.
Work with wind roses and apply seasonal thinking.
Visualize wind flow in early design concepts.
Apply wind analysis to inform site layout design strategies.

## Slide 27: Wind analysis
Notes: There are three key categories to consider regarding wind simulation and design strategies: Safety, comfort, and energy.
Safety: understanding both lateral loads and potential lift from the Bernoulli Effect on structures and building materials, as well as dead zones that may create snow drifts on both buildings and the site.
Comfort: how wind will impact the comfort of pedestrians around the site, how wind will impact perceived temperatures on the site, and how wind breaks may be created for both comfort, shelter, and mitigating the impact of wind on the interior to exterior threshold.
Energy: understanding wind direction and speed can help design cross ventilation through a building, inform the building shape, and establish the potential for wind energy creation on site designs

## Slide 28: Wind analysis
Select Wind analysis. There are two types of wind analysis process available:
  Rapid uses AI to quickly provide insights across the site ground plane.
  Detailed takes longer, and provides a volumetric analysis
Notes: This simulation

## Slide 29: Establish simulation area
Set radius.
This determines the area of the simulations and includes surrounding buildings, trees, topography, and context
Notes: This simulation

## Slide 30: Study the comfort results
The Comfort results displayed are based on Lawson Wind Comfort Scale
  Uncomfortable conditions are in red
  Light green for sitting
  Green to yellows for standing and walking
Notes: This simulation

## Slide 31: Study the direction results
Set the Rapid analysis to Direction.
Set the direction based on the wind rose
  Larger pedals convey a higher percentage of wind coming from the direction.
  The gradient displays wind speeds.
Notes: This simulation

## Slide 32: Run the Detailed analysis
Select Analyze under the Detailed panel.
  The Detailed analysis runs volumetric wind simulations using CFD (Computational Fluid Dynamics)
  The simulation runs in the cloud, and may take up to an hour to complete
Notes: This simulation

## Slide 33: Study the detailed analysis results
Select view results once the detailed analysis once completed
  Note that results are now shown on all horizontal surfaces in the simulation area.
  The gradient displayed conveys wind speed.
Notes: This simulation

## Slide 34: Study the detailed analysis results
Use the Label tool to tag show precise speeds at exact locations across the site layout
  Note that simple changes in location and elevation may have drastic impacts on wind speed
Notes: This simulation

## Slide 35: Turn on Streamlines
Unhiding streamlines shows a visualization of wind “streams” over the site.
  Note that a higher compression of the streamlines typically means higher wind speeds
Notes: This simulation

## Slide 36
Run a microclimate simulation

## Slide 37: Learning objectives
After completing this lecture, you’ll be able to:
Run the microclimate simulation.
Label the measurable results.
Explain how Microclimate combines sun, daylight, wind, and local weather data to estimate thermal comfort.
Apply the baseline data from the microclimate simulation to generate design ideas centered around human comfort and experience.

## Slide 38
Notes: The microclimate analysis introduces human context, specifically – the perception of temperature – as a key element. The simulation includes data from sun (including the impact of local context), daylight, wind, and local weather conditions to compute perceived temperatures on a site. The measurement is defined by the UTCI index (Universal Thermal Climate Index) to create the “feels like” temperature. For a designer, this impacts at least three different areas of design thinking:
Comfort and Health: Understanding the “feels like” temperature allows the designer to position key design elements in optimum locations – building entries, exterior parks, and site amenities can all further improved by understanding these temperatures. By optimizing shade where humans move across the site, and working with the prevailing winds, the site layout can mitigate temperature extremes and improve the human health.
Materiality: Knowing the temperatures of exact locations on the site helps designers apply materials in a thoughtful way. Highly reflective materials close to extremely high on site temperatures will further amplify the intensity. Darker materials (asphalt) may absorb more light energy and increase heat, which could be a positive or negative depending on the site context.
Energy: Knowing the temperatures around the building, and on building surfaces (like the roof) helps the design team know the best methods, materials, and mechanical processes to optimize building performance. In the same way that a human senses temperature beyond the ambient measure, a building surface may perform differently given wind, shade, and daylight.

## Slide 39: Run Microclimate analysis
Select Microclimate analysis.
  This process simulation will provide perceived or “feels like” temperature
  Uses UTCI (Universal Thermal Climate Index)

## Slide 40: Select analysis area
The analysis can be run either within the site limits, or the selection area.
  Typically, the selection area (a circle with a defined radius) is preferred to provide data around and within the site.
Notes: This simulation

## Slide 41: View the simulation data
When complete, select View results
Notes: This simulation

## Slide 42: Establish month and time of day
Set the date and time.
You can also select the predominate wind direction on the wind rose, and modify wind speed on the curve below the wind rose
Notes: This simulation

## Slide 43: Label locations in the site layout
Select the Label tool.
  Left-click to label an exact location.
  Sun, shade, daylight, ambient temperature and wind are all significant variables in the analysis.
Notes: This simulation