## Slide 1
Develop variables and proposals lecture

## Slide 2: Sections in this lecture
Integrate Forma Site Design into BIM workflows
Add site elements
Develop multiverse proposals

## Slide 3
Integrate Forma Site Design into BIM Workflows

## Slide 4: Learning objectives
After completing this lecture, you’ll be able to:
Adapt Forma Site Design to your specific workflow.
Import a sketch to develop a site layout proposal.
Import OBJ files from Rhino, Revit and SketchUp to develop the site layout in Forma Site Design

## Slide 5: Move a project across different Forma Sites
Select your geometry, right-click, and select Add to Library.
This will move the file to the cloud storage for your Site.
Notes: This simulation

## Slide 6: Copy geometry to Hub
Once in your Library, you can right-click and copy the massing model to the Hub.
This will move the file to the cloud storage for your Project, and will be accessible to all sites in your Project.
Notes: This simulation

## Slide 7: Open geometry from the Hub
In a different Site, open your Library, Hub, and then you can click to place the geometry from the hub into a Proposal.
Using this method, you can move models across multiple Forma Sites.
Notes: This simulation

## Slide 8: Export from Revit to Forma Site Design
To study a Revit file in Forma Site, isolate the object, select: Export, CAD Formats, OBJ, and accept all of the defaults, except for “leave temp. hide and isolate”.
For early design simulations, keep the massing and form simple.
Notes: This simulation

## Slide 9: Upload geometry to Forma Site Design
Click the Library button and then click Import.
This starts the process of uploading your file to your Forma Library for your Site.
Notes: This simulation

## Slide 10: Upload OBJ file from your computer
Click the Import button to navigate to the files on your computer to upload to Forma Site Design.
Notes: This simulation

## Slide 11: Establish OBJ Import Settings
Set the base units to Feet.
Select Rotate.
  OBJ uses an XYZ axis with XZ on the ground plane, Rotate will align XZ on the ground plane, Y as vertical.
Select Save and close to load the object into the Site Library.
Notes: This simulation

## Slide 12: Upload geometry to Forma Site Design
Left-click your object in the Library
Left-click where you want the object to be placed in the site proposal.
NOTE: This same process will work with OBJ files from most any platform!
Notes: This simulation

## Slide 13
Add site elements

## Slide 14: Learning objectives
After completing this lecture, you’ll be able to:
Develop imagery to convey how a human will experience the site.
Use the Surface tool to communicate site elements like green spaces, parks, water retention, etc.
Use the Surface Parking tool.

## Slide 15: Add a surface for spatial evaluation
Select Generic – Surface. This tool will allow you to create custom spaces on the ground plane for:
  Data metrics
  Visualization
  Spatial programming
Notes: This simulation

## Slide 16: Create a generic surface
Trace surface shape with left clicks. Click enter on your keyboard to close the surface shape.
Surface area and function will be displayed under Area metrics on the right panel.
Notes: This simulation

## Slide 17: Modify a surface
Select Unspecified by Surface function.
Click the plus sign in Settings to add a new function.
Name the function.
Select Apply changes.
Modify the color and transparency of the generic surface in the right side panel.
Notes: This simulation

## Slide 18: Add parking to a site
Select the Surface Parking tool.
The Surface Parking tool will provide area, spaces, and options to vary the parking spot configurations.
Notes: This simulation

## Slide 19: Save a camera position
You can save the location and settings of a view in Forma Site Design by selecting the Camera button, and then + Save camera position.
Provide a descriptive name with date and time (the sun settings) for quick reference later.
Notes: This simulation

## Slide 20
Develop multiverse proposals

## Slide 21: Learning objectives
After this lecture, you’ll be able to:
Create collaborative files in Forma Site Design to build depth in proposal options.
Document observable variables across multiple options to develop outcome-based design solutions.

## Slide 22
Notes: Why run multiple design options:
Creativity: Curation is a skill necessary to all designers, develop it (especially as AI tools continue to evolve). More options push our creativity, and increase value proposition to our clients. Developing multiple solutions allows for further understanding on problem solving as the design options are refined into a single solution.
Cost and Analysis: Developing a series of options helps clarify the analysis by ensuring design performance data is not an anomaly, and clarifies the designer’s understanding of the site layout.
Evolution of Parameters: It takes a series of tests, or design options, to begin understanding the site opportunities, parameters, problems and shortcomings regarding the potential of a site and site layout. Multiple options allows for the understanding of a trend, versus anomaly, and quite simply is part of a solid scientific process of investigation.
Innovation: Even if the first idea is the best idea, it still should be measured, understood, and evaluated not only with a measurable performance database (as is required by code), but also against the other formal configurations on the same site. Design is a balance of many factors including context, form, performance, function, community, connection, efficiency….and many more, that sometimes work together, and at times pull the design in different directions. The process takes discernment and balance found through an iterative design process that builds innovative solutions.

## Slide 23: Share a site for collaboration
Select the “football huddle” in the top right.
Enter email address for invitation to the site.
Set user access to either: Viewer (cannot edit), Editor (can make changes), or Manager (can add new users).
Notes: This simulation

## Slide 24: Evaluation across multiverse proposals…
Building multiple proposals allows for an understanding of trends.
For instance:
  Daylighting on west elevation, if the building is on the west side of the site will consistently perform poorly for interior illumination.
Notes: This simulation

## Slide 25: Evaluation across multiverse proposals…
Building multiple proposals allows for an understanding of trends.
For instance:
  The middle of the site has increased wind speeds due to the buildings south of our site.
Notes: This simulation

## Slide 26: Evaluation across multiverse proposals…
Building multiple proposals allows for an understanding of trends.
For instance:
  Exterior perceived temperatures on the west side are significantly more favorable than the east.
Notes: This simulation