## Slide 1
Extending performance analyses lecture

## Slide 2: Sections in this lecture
Analyze the site for sound
Evaluate solar energy

## Slide 3
Analyze the site for sound

## Slide 4: Learning objectives
After completing this lecture, you’ll be able to:
Define the input parameters and values for analyzing sound.
Apply traffic data to road centerlines.
Use the data to inform design decisions.
Develop sound mitigation strategies.

## Slide 5
Notes: Health – Understanding how to mitigate noise is a serious concern for human health, as high level of noise have been linked to increase levels of stress, anxiety, cardiovascular disease, blood pressure, and a decrease in productivity.
Code – Most locations have designated noise ordinances to ensure that prolonged sounds need to stay under 50-70 decibels because of the health hazard that this level of sound presents. However, this does not include sound generated by traffic – so it often becomes the responsibility of the designer to develop strategies to reduce noise while designing a site layout.
Cost – Developing the correct set of materials with the appropriate STC (Sound Transmission Class) value helps ensure that interior spaces, and the type of interior spaces are both appropriate to potential noise problems, and that sound passing through the assembly is mitigated.

## Slide 6: Analyze noise on a site layout
Select the road to the south of the site, and select edit base.
The roads are part of the base of the model, editing the base send the information to all proposals.
Notes: This simulation

## Slide 7: Find values for traffic data
You will need to add vehicular speed, and ADT (Average Daily Traffic) to the road.
These values, or similar road conditions, can typically be found on department of transportation websites.
Notes: This simulation

## Slide 8: Assign traffic data to road
Input the values from the Traffic Volume Map onto the appropriate road(s) in Forma Site Design.
This site has a speed limit of 30 mph with 2500 vehicles per day.
Notes: This simulation

## Slide 9: Run the Noise analysis
Select Noise analysis from the panel on the top right.
Note the gradient on the ground plane showing sound in decibels:
  < 50 dB is ambient
  < 70 dB is safe
  > 85 dB is the start of damage
Notes: This simulation

## Slide 10: Detailed noise analysis
To run a more detailed, three-dimensional noise analysis, select Analyze under DETAILED, and then View result when completed.
Notes: This simulation

## Slide 11: Detailed noise analysis results
This analysis presents noise levels in decibels on all surfaces within the defined parameters of the simulation.
Use the Label tool to select surfaces for a precise dB value.
Notes: This simulation

## Slide 12
Evaluate solar energy

## Slide 13: Learning objectives
After completing this lesson, you’ll be able to:
Set up the solar energy simulation for the roof area and additional surface areas.
Describe potential energy use for a building.
Evaluate potential solar energy creation for an area (like the roof) on a site.
Evaluate solar energy payback.

## Slide 14
Notes: Solar Power:
Economic value:
Installing solar power reduces the buildings strain on the power grid, lowering the owner cost on utilities, increasing the return on the building investment, and building resilience against fluctuating (usually rising) utility costs. Solar panels have been shown to increase a buildings value. Generating even a portion of a building’s power needs by using solar decreases building downtime from power loss and creates independence from blackouts.
Multifunctional materiality:
When integrated into a building design, solar panels can also create additional shade for a building decreasing solar heat gain. When integrated into a site design, solar panels can create additional shade for parking areas and parks. Several advancements in solar panel materials have integrated power generation into creating BIPVs (Building Integrated Photovoltaics) such as roofing material, wall enclosure systems, and glazing.
Inherent good:
Working toward building level energy independence is a step in the direction for environmental good: Reduction of greenhouse gases, reduction of global warming, and the overall improved health of our planet.

## Slide 15: Create a solar energy analysis
Select Solar energy analysis.
Set the Analysis area to the Site limit.
This will ensure that the only surfaces evaluated will be within the site

## Slide 16: Create a solar energy analysis
Select Run analysis.
When completed, click on View result.

## Slide 17: Study the analysis results
Select the Label tool.
Select surfaces to see values for the potential power generation in Kilowatt Hours per Square foot.
In the right panel at the bottom are overall values for the surfaces assuming panel type and surface coverage.

## Slide 18: Apply and refine results to a single surface
By selecting a single surface you can see specific values that can be adjusted with sliders to dial in both panel efficiency and surface coverage to match either solar panels, or BPIVs.

## Slide 19: Create a PV cost payback analysis
Apartments:
9.6 kWh per square foot
Apartment square footage: 28,000
Apartment power: 9.6 x 28,000 = 268,800 kWh per year
Apartment power cost: $0.12 x 268,800 per kWh = $32,256
Commercial Space:
15 kWh per square foot
Commercial space square footage: 6,400
Commercial space power: 15 x 6,400 = 96,000 kWh per year
Commercial space Power Cost: $.0942 x 96,000 = $9,043
Notes: Develop an understanding of power…

## Slide 20: Energy Calculations
Restaurant:
40 kWh per square foot
Restaurant square footage: 4,800
Restaurant power: 40 x 4,800 = 192,000 kWh per year
Restaurant Power Cost: $0.0942 x 192,000 per kWh = $18,086
Total Costs:
Apartments: $32,256
Commercial: $9,043
Restaurant: $18,086
Total: $59,385 (round up) $60,000 annually for power.
Notes: Develop total costs

## Slide 21: Energy Calculations
Solar Panel Potential:
Total Energy annually: 556,800 kWh
Potential Energy Output on Upper Roof: 59,700 kWh
59,700 / 556,800 = 10.7% (round down to 10%)
$60,000 x .10 = $6,000 savings on utilities per year
Solar Panel Costs:
59,700 kWh x 1000 W = 59,700,000 Wh
59,700,000 Wh / 8760 hours per year = 6815 Watts
Cost per Watt installed solar panels: $2.48
$2.48 x 6815 = $16,901 for the cost of solar panels on the upper roof
At a savings of $6,000 per year, pay back is in approximately 3 years.
Notes: Apply potential power creation, apply cost potential offset