## Slide 1: Lecture: Introduction to BIM for the AECO industry

## Slide 2: Learning objectives
After completing this project, you’ll be able to:
Describe how the Building Information Modelling (BIM) process brings efficiency and savings to a project.
Link two-dimensional (2D) drawings into Revit.
Convert two-dimensional (2D) drawings into three-dimensional (3D) information models.
Explain why a Common Data Environment (CDE) is central to a BIM project workflow and multidiscipline collaboration.
Use a Common Data Environment (CDE) to host and share 3D Revit models.
Explain how standardized processes like file naming make it easier for different teams to work collaboratively.
Combine (federate) multidiscipline 3D models to find design and other coordination issues.
Use outcome-based BIM to meet sustainability and other goals.
Read and extract key information from BIM documentation such as the BIM Execution Plan (BEP) and Asset Information Requirements (AIR).
Apply maintainable asset information from BIM documentation to a 3D model.
Export maintainable asset information from a 3D model and share with the wider stakeholders

## Slide 3: Common terms
  AECO – Architecture, Engineering, Construction, and Operations – the industries that design, build, and manage buildings and infrastructure.
  AIR (Asset Information Requirements) – A list of all the information needed to manage a building or asset properly.
  Asset – A building, road, or equipment, usually called this when handed over to the client and called project before this.
  BEP (BIM Execution Plan) – A guide that explains how BIM will be used on a project.
  BIM (Building Information Modeling) – A standardized process that allows all team members to work together.
  CDE (Common Data Environment) – A shared online space where all project files and information are stored.
  Clash Detection – Using software to find mistakes where parts of a building might overlap or interfere.
  COBie (Construction-Operations Building Information Exchange) – A format for organizing important building data to help with maintenance after construction.
  Collaborate – Different teams working together to complete a project successfully.
  Status Code – A label showing the current stage of a project or file, like "In Progress" or "Approved“ and whether it can be used by other teams to help them design their model.

## Slide 4: BIM for AECO
What is BIM?

## Slide 5: What is BIM?
Building Information Modeling (BIM) is the PROCESS of delivering and operating built assets using well organized digital information collaboratively.
This standardization is what allows different teams to work together.
The process follows standards such as the ISO19650 suite.
Notes: At the heart of BIM is the 3D model, a visual representation of the project. But it's not just any 3D model. Each element within the model is packed with data, dimensions, material, and more. This information is crucial for creating accurate construction drawings, reducing errors and keeping the project on track. So how does all this digital information translate in the real-world construction process?

## Slide 6: BIM: During the planning stage
It is important to set the client’s goals and needs at the earliest stages of the project. This is achieved by creating early documentation such as:
  Organizational Information Requirements (OIR)
  Asset Information Requirements (AIR)
  Project Information Requirements (PIR)
  Exchange Information Requirements (EIR)
  Master Information Delivery Plan (MIDP)

## Slide 7: BIM: During the design stage
Early in the project cycle, concept models are created and can be used for early analysis and communication of design intent.
Later in the design stage, as decisions are reached on layout and systems, more technical and complete 3D information rich models are created.
Documentation produced during this stage include construction drawings and schedules such as project progress and costs.
Both the model geometry and information continue to include more detail such as asset supplier contact information and service / warranty information.

## Slide 8: BIM: During the construction stage
During construction, the 3D model can be updated with any changes that happen on site, such as an asset being installed in a slightly different location.
Schedules and costs are also kept up to date if there are any changes.

## Slide 9: BIM: During the handover stage
After construction, the 3D model and all of the information gathered can be shared with the client so they can operate and maintain the built asset.
Documents handed over like the Operation and Maintenance Manual contain all the information the facilities management team need for every maintainable asset in the building, such as the boiler manufacturer and contact details for the company, product number, service requirements, room number etc.

## Slide 10: BIM for AECO
Shift from a 2D to 3D workflow

## Slide 11: Shift from 2D to 3D
BIM transforms the design process by shifting from traditional 2D drafting to intelligent, data-rich 3D models.
2D drawings created in programs such as AutoCAD consist of 2D lines that have little information.
3D models are better for communicating design intent and can host information such as an element’s manufacturer, product or serial number.
This parametric workflow saves significant time compared to 2D drafting. It reduces errors and ensures consistency and version history across all documentation.

## Slide 12: Convert 2D drawings to 3D information models
Revit tools allow you to link 2D drawings into the project.
Linking is good practice as it keeps the information up to date if the original file is changed.
Any 3D elements created automatically appear in all views, such as plans, elevations and 3D.
For efficiency, Revit tools allow you to Pick Lines and automatically converts them to walls.

## Slide 13: Use 2D plans to create 3D multistory models
As Revit models are 3D, 2D plans can be linked to multistory floor levels.
Walls have base and top “constraint” properties, allowing you to create walls on any level.

## Slide 14: Navigate and enhance 3D views
Revit's 3D views provide a comprehensive perspective that goes beyond flat 2D drawings, enabling you to visualize your model in real-world context.
You can use Orbit tools to look around your model, as well as change the view to display shadows, materials, add some perspective or separate elements for a better understanding of construction.

## Slide 15: Generate documentation from a 3D model
Revit transforms project documentation by automating the creation of views and schedules directly from the 3D model, ensuring consistency and reducing errors.
Revit also enhances design communication with features like annotations, tags, exploded views, and 3D details, improving clarity and collaboration.
Editing an element like the door position, automatically moves the door in every view, drawing sheet or if removed, updates the schedule to reflect any changes.

## Slide 16: BIM for AECO
Shift from 2D to 3D workflow: Revit User Interface

## Slide 17: The Revit Home
The Revit Home is where you can access existing Revit project models or begin new ones.
Use the Home to:
Access existing models and families.
Create new models and families.
Access recent models or models saved in the Autodesk Construction Cloud.

## Slide 18: The Revit User Interface
Ribbon: The ribbon displays when you create or open a file. It provides all the tools necessary to create a project or family.
To save space, the Ribbon organizes tools in tabs and panels, and depending on the tool or the element selected, what is displayed on the Ribbon will be context related, meaning you will always have easy access to the tools you need.
u

## Slide 19: The Revit User Interface
Ribbon: The ribbon displays when you create or open a file. It provides all the tools necessary to create a project or family.
Ribbon tabs: Contains tools specific to that tab, e.g. architecture or annotation tools.
Click to look through the tabs. Now imagine all of those tools were presented at once. There would be very little screen space left to work in.
v

## Slide 20: The Revit User Interface
Ribbon: The ribbon displays when you create or open a file. It provides all the tools necessary to create a project or family.
Ribbon tabs: Contains tools specific to that tab, e.g. architecture or annotation tools.
Quick Access Toolbar: The Quick Access Toolbar contains a set of default tools. You can customize this toolbar to display the tools that you use most often.
You can customize this with the tools that you use most often.
w

## Slide 21: The Revit User Interface
Ribbon: The ribbon displays when you create or open a file. It provides all the tools necessary to create a project or family.
Ribbon tabs: Contains tools specific to that tab, e.g. architecture or annotation tools.
Quick Access Toolbar: The Quick Access Toolbar contains a set of default tools. You can customize this toolbar to display the tools that you use most often.
Properties palette: View and modify instance properties on elements in your model.
If you edit the properties of a door in the Properties palette, only that instance is affected. That means you can add unique properties like serial number to a specific door.
Click Edit Type to open the Type properties of all of the doors of that type, for example the internal door. Editing properties in the Type dialog edits all of the doors of that type, for example cost.
x

## Slide 22: The Revit User Interface
Ribbon: The ribbon displays when you create or open a file. It provides all the tools necessary to create a project or family.
Ribbon tabs: Contains tools specific to that tab, e.g. architecture or annotation tools.
Quick Access Toolbar: The Quick Access Toolbar contains a set of default tools. You can customize this toolbar to display the tools that you use most often.
Properties palette: View and modify instance properties on elements in your model.
Project Browser: The Project Browser shows a logical hierarchy for all views, schedules, sheets, groups, and other parts of the current project.
You can open the floor plan view by double clicking on Floor Plans > Base Level. You can duplicate views by right clicking on the view and selecting Duplicate > Duplicate With Detailing.
y

## Slide 23: The Revit User Interface
Navigation bar: Provides access to navigation tools, including the ViewCube and SteeringWheels.
You can drag the ViewCube to rotate the model in 3D view, or click on a face to view from that direction. You can also press and hold Shift on your keyboard, click the middle wheel button on your mouse, and move the mouse to 3D orbit the model.
z

## Slide 24: The Revit User Interface
Navigation bar: Provides access to navigation tools, including the ViewCube and SteeringWheels.
Context menu: A menu of options that changes based on the current context or selection.
Selecting an object such as a wall provides you with the opportunity to change the orientation or select other walls. General tools like Zoom in/out are available no matter what is selected.
{

## Slide 25: The Revit User Interface
Navigation Bar: Provides access to navigation tools, including the ViewCube and SteeringWheels.
Context menu: A menu of options that changes based on the current context or selection.
Drawing area: The drawing area (canvas) displays views (and sheets and schedules) of the current model. Each time you open a view in a model, the view displays in the drawing area.
The drawing area may be a Floor Plan view, Elevation, 3D, Schedule or Drawing Sheet.
|

## Slide 26: The Revit User Interface
Navigation bar: Provides access to navigation tools, including the ViewCube and SteeringWheels.
Context menu: A menu of options that changes based on the current context or selection.
Drawing area: The drawing area (canvas) displays views (and sheets and schedules) of the current model. Each time you open a view in a model, the view displays in the drawing area.
View Control Bar: The View Control Bar provides quick access to functions that affect the current view.
You can modify the view properties including scale, detail level, and visual style such as shading or hidden line and whether shadows are turned on or off.
}

## Slide 27: The Revit User Interface
Navigation bar: Provides access to navigation tools, including the ViewCube and SteeringWheels.
Context menu: A menu of options that changes based on the current context or selection.
Drawing area: The drawing area (canvas) displays views (and sheets and schedules) of the current model. Each time you open a view in a model, the view displays in the drawing area.
View Control Bar: The View Control Bar provides quick access to functions that affect the current view.
Status bar: The status bar provides tips or hints on what to do. When you highlight an element or component, the status bar displays the name of the family and type.
For new users to Revit, the Status bar is a very helpful aid. It steps you through tools, instructing you through the creation of elements like “Click to enter the start point” or “Click to enter Move end point.”
~

## Slide 28: How to use the Ribbon
The ribbon provides all the tools necessary to create a project or family.
Use the ribbon to:
Create 3D elements like walls, doors and windows.
Add annotation like dimensions and text.
Modify elements using the modify tools.
Collaborate with others using Interoperability Tools.

## Slide 29: How to use the Ribbon
When you use certain tools or select elements:
A contextual ribbon tab displays tools that relate to the context of that tool or element. In this example, the tools you need to create or modify a wall.
The tab closes when you exit the tool or clear the selection.

## Slide 30: Expanded panels
To save space, some panels can be expanded to reveal more tools.
An arrow next to a panel title indicates that you can expand the panel to display related tools and controls
By default, an expanded panel closes automatically when you click outside the panel.
Click the push pin icon to keep the panel expanded.

## Slide 31: Dialog launcher
Some panels allow you to open a dialog to define related settings.
Click the dialog launcher on the bottom of a panel to open a dialog.

## Slide 32: How to use the Project Browser
The Project Browser acts as a table of contents for your project.
Use the Project Browser to:
Navigate and open views of the model.
Double-click any view to open it.
Scroll to find all existing views, such as floor plans, elevations, 3D, schedules, and drawings.
Organize, sort, and filter to support your workflow.

## Slide 33: How to use the Properties palette
The Properties palette lets you view and modify parameters for selected elements.
Use the Properties palette to:
View and modify parameters for selected elements like walls and doors.
Edit the type such as External or Internal wall.
Edit properties such as the base and top of a wall.
If no element is selected, you can modify the View properties, such as the visibility of elements.

## Slide 34: What are some common modeling tools?
1 Wall: Creates a wall in the project.
2 Door: Adds doors to the building model.
3 Window: Adds windows to the building model.
4 Roof: Creates a roof in the project model.
5 Ceiling: Creates a ceiling in the project model.
6 Floor: Creates a floor in the project model.
u
v
w
x
y
z
u
v
w
x
y
z

## Slide 35: Creating walls
Once the Wall tool is activated or a wall is selected, the Ribbon displays the tools available to create or edit walls.
Walls can be created manually using the Line option u or automatically using the Pick Lines option v.
Using the Line option, click to select the start w, then the end x of the wall.
Using the Pick Lines option, click to select the existing 2D line y to convert it to a 3D wall.
v
u
w
x
y

## Slide 36: Adding a door
Hovering the cursor over a wall indicates the position and orientation of a door if it is placed there.
Moving your cursor to the outside 1 / inside 2 face of the wall changes the door “facing,” and pressing space changes the “hand” 3.
A door facing refers to the direction a door opens (into the room or outwards). A door hand refers to which side the hinges are located on when a person is standing in front of the door.
Click the left mouse button to place the door 4.
v
u
w
x

## Slide 37: BIM for AECO
Collaborating with other disciplines

## Slide 38: The Common Data Environment (CDE)
Communicating with other teams and disciplines on a traditional construction project can be messy and confusing.
  Where are files saved?
  Should they be emailed?
  How is communication to be achieved?

## Slide 39: The Common Data Environment (CDE)
With a CDE, such as Autodesk Docs within the Autodesk Construction Cloud, all communication and file sharing takes place in a cloud shared space.

## Slide 40: Set up Autodesk Construction Cloud (ACC)
A new ACC Project is created for every construction project, keeping the information separate and available to only those who need access.
All of the information saved to the project relate only to this project, including models, drawings and report.

## Slide 41: Folders in ACC
Teams work in their own company dedicated space.
A model can be stored in a Work in Progress (WIP) folder for the individual or team members.
When complete or ready to be shared externally with other teams, it can be shared using ACC tools to package it into a shared area on the CDE.

## Slide 42: Assign permissions in ACC
When it comes to assigning permissions in a CDE, it’s not just about giving people the right access to the right files, it may be a contractual or even legal requirement.
By making sure team members only access the information they need for their roles, you’re not only keeping data secure but also avoiding accidental changes to critical files.
ACC makes this process more efficient by allowing you to assign permission to individual people, role or company , ensuring that every team member has the appropriate access to the right information at the right time.

## Slide 43: Create attributes and meta data
The name of the file communicates what it is, such as a model, drawing or a report. Metadata such as classification communicates what the content of the file is in more detail, such as the environmental impact report.
Other metadata such as Status Code communicate the status of the file. Is it…
  Work in Progress : S0
  Shared for Coordination : S1
  Shared for Information: S2
  Etc.

## Slide 44: Naming standards: ISO 19650
Standardized processes like naming files makes it easier for people to find and use the information quickly.
The project in this course uses the U.K. national annex for ISO19650 to show how the global ISO standard template in ACC can be adjusted for your project’s needs.
The file name structure for this course’s project should be:
  Project
  Originator
  Functional Breakdown
  Spatial Breakdown
  Form
  Discipline
  Number

## Slide 45: Naming standards: ISO 19650
Names of files can only be made from the list as shown in the BEP.
PRJ001-ADSK-ZZ-ZZ-M3-A-0001
PRJ001: The unique code for this project
ADSK: This file was created by Autodesk company
ZZ: Contains all / multiple volumes of the project
ZZ: Contains all/ multiple levels
M3: Native 3D model (such as Revit project model)
A: The file relates to the architecture (walls, windows doors etc.)
0001: First time the preceding 6 fields have been used in a name

## Slide 46: Naming standards: ISO 19650
Names of files can only be made from the list as shown in the BEP.
PRJ001-STR-01-00-DG-S-0002
PRJ001: The unique code for this project
STR: This file was created by Structural Company
01: Contains information relating to volume 01
00: Contains information relating to the base level
DG: the file is a drawing
S: The file relates to the Structure (columns, beams, slabs etc)
0002: Second time the preceding 6 fields have been used in a name (the base level is so big, it needs to be split over two drawings)

## Slide 47: Collaborate to the CDE
Revit Collaborate tools permit you to create a cloud shared model on the CDE so you can work with others in your company/team.
This is achieved by clicking Collaborate and selecting the In the cloud option.
Remember to select the WIP folder until you are ready to share externally.

## Slide 48: Create and manage coordination in ACC
WIP is where you and your team work to create your 3D model in privacy.
You can use other 3D models shared with you in your WIP folder to help you design a model that is free from coordination errors (such as the window placed where a column is).

## Slide 49: Create a shared coordination space in ACC
Once your team has completed their work package, or a date has arrived where you need to share the work done so far, each team shares their 3D model and other documentation such as drawings to the Shared area of Autodesk Docs.
A nominated team take each model and run coordination checks such as Clash Detection.
Finding issues in models at the design stage saves money later in the project as issues don’t need to be found and resolved on site.

## Slide 50: Sharing a project model with other disciplines
ACC Design Collaboration allows teams to create a Package, containing all of the files they wish to share.
A Package appears on the Timeline so other disciplines know it is available to use if they wish.

## Slide 51: Consume a package and link shared Revit model
A package appears as a white circle on the Timeline.
To use a Package, teams “consume” it, bringing it into their company area on the CDE.
Once consumed, the circle is filled blue.
From here, teams can Link the file into their own 3D Revit model and use it for coordination of their own design.

## Slide 52: BIM for AECO
Outcome-based BIM

## Slide 53: Integrate outcome-based BIM
Buildings can exist for many years and operating costs can have a high impact on financial and environmental outcomes.
3D models and tools allow designers to measure alignment to client goals and outcomes such as sustainability, carbon footprint, and energy use.

## Slide 54: Use Forma for outcome-based BIM
During early concept stages, design intent models can be used in Forma to analyze outcomes like environmental impact though:
  Sun hours
  Daylight potential
  Wind speeds and comfort
  Noise
  Solar panel potential

## Slide 55: Use Autodesk Insight to analyze carbon
During later design stages, a more detailed 3D model can be analyzed to aid the selection of different structure and envelope systems such as walls.
Teams can analyze exactly where the greatest carbon impacts can be achieved.
Notice how the Operational Carbon is the greatest contributor to the Total Carbon value.

## Slide 56: BIM for AECO
BIM Information Requirements

## Slide 57: Use BIM Information Requirements
Q: Why do we need Information?
A: So everyone knows what to do, how to do it, and when it needs to be done. This is explained in the Information Requirements documentation such as:
  Organizational Information Requirements (OIR)
  Asset Information Requirements (AIR)
  Project Information Requirements (PIR)
  Exchange Information Requirements (EIR)
  Master Information Delivery Plan (MIDP)

## Slide 58: Read and extract information from the BEP
The BEP is the “rulebook.”
It provides a description of the standardized way of working together, such as:
  File naming
  Coordinates and address
  Project number and other information
  Software versions and file formats
  If and how the project is split into volumes

## Slide 59: Apply information from the BEP to a Revit model
In Revit, information from the BEP such as project name, site name, and location can all be added via Manage > Project Information

## Slide 60: Read and extract information from the AIR
The AIR specifies the information the facilities management team need to operate and maintain the building.
  Maintenance: lighting, heating etc.
  Maintenance schedules
  Digital records of where everything is
  Who looks after it

## Slide 61: Apply information from the AIR to a Revit model
This AIR appendix displays the information as Uniclass 2015 codes that can be applied to the elements in the Revit model via: Interoperability Tools> Standardized Data> Assign classification.
In stage 3, the following codes should be applied:
Foundations
  Ss_20_05_15
Structural Steel
  Ss_20_10
Structural Concrete
  Ss_20_10_75_15
Curtain Walling
  Ss_25_10_20
Wall Partitions
  Ss_25_10_30

## Slide 62: Export information from a Revit project model
To share the information stored in the Revit model with other teams, it can be exported.
Other teams like Quantity Surveying may wish to use this for costings.
The client/ facilities management may want to use it to run and maintain the building.
Structured formats like COBie allow teams to share and use data in other disciplines.
The system importing the information knows what data it is and the order.

## Slide 63: BIM for AECO
BIM dimensions

## Slide 64: BIM dimensions
In design tools like AutoCAD and Revit, dimensions are used to describe the storing of information.
Two dimensions (2D) could be used to identify the start of this line using X and Y cartesian coordinate data.
10,0
x,y
0,0
x,y

## Slide 65: BIM dimensions
3 Dimensions (3D) could be used to identify the length, width, and height of this box.
The Revit project model when saved, saves this information, and when the file is opened, the information is used to recreate the model.

## Slide 66: BIM dimensions
Think of these, saved as a piece of information.
With each piece of information stored individually as a “dimension.”
X
Y
Z
1
2
3

## Slide 67: BIM dimensions
Revit projects can also save other information such as the cost of an air conditioning unit, when it should arrive on site and maintenance information like warranty etc.
Saving these pieces of information in a project results in a project being described as a 4D, 5D, 6D etc. model.
There is no real consensus on what number of dimension these models can be identified as, however the following is generally accepted.

## Slide 68: BIM dimensions (general consensus)
4D Time / scheduling information such as construction sequencing.
5D Cost information such as the cost of a door.
6D Sustainability information such as sustainability goals or energy performance of a window.
7D Facilities management / maintenance information such as warranty information.
8D Health and safety information such as risks throughout the model.

## Slide 69: BIM dimensions
Think of these, saved as a piece of information.
With each piece of information stored individually called a “dimension.”
X
Y
Z
1
2
3
Time
Cost
Sustainability
4
5
6

## Slide 70: BIM for AECO
BIM maturity model

## Slide 71: BIM maturity levels
The BIM (Building Information Modeling) Maturity Model is a framework that categorizes an organization's BIM capabilities and adoption, providing a roadmap for improvement and guiding organizations towards more advanced BIM practices.
It helps organizations understand their current BIM capabilities and plan their journey towards more advanced stages of BIM implementation.
Think of it like a plan for your company to adopt BIM if it doesn’t already.
It lets everyone know the stage of BIM you should be working to on a project.

## Slide 72: BIM maturity levels
BIM Stage 1
  Use 2D CAD and 3D models, meeting national regulatory requirements.
BIM Stage 2
  3D information models created by the individual disciplines (architectural, structural, MEP, etc.), stored separately and federated when required. Models meet international standards such as ISO 19650.
BIM Stage 3
  All disciplines work together in a single structured platform that combines the models automatically (no need to federate individual discipline models).

## Slide 73: BIM for AECO
BIM Level of Information Need

## Slide 74: BIM level of detail / information
It would be unreasonable to expect at the beginning of a conceptual design that the team would have a final idea of the exact specification and design of every element in the project.
Level of Information, Level of Detail and Level of Information Need are terms that describe the various levels of information and detail required through all stages of the design and construction of a building.
As you would expect, at the beginning (concept design), the level of complexity or detail in the model would be low, as would the level of information, such as door and window manufacturer and product numbers.
To allow the project to progress, detail is increased and information added as decisions are made, such as what heating system the client requires.

## Slide 75: BIM level of detail / information
LOD (Level of Detail/Development): Defines how detailed or developed a BIM model element is at each stage of a project.
LOI (Level of Information): Specifies the amount and quality of information embedded within BIM model elements.
Together, they help manage project expectations, improve collaboration, and support accurate decision-making.

## Slide 76: BIM level of detail / information
BIM documentation such as the BIM execution plan specifies the levels of detail and information at the various stages through the project such as:
  LOD 100 (Conceptual): Basic form, size, and location of elements.
  LOD 200 (Approximate): General geometry, approximate size, shape, location.
  LOD 300 (Precise): Accurate dimensions, geometry, and orientation.
  LOD 400 (Fabrication): Detailed enough for fabrication and assembly.
  LOD 500 (As-Built): Represents exact built conditions, suitable for facility management.

## Slide 77: Level of Information Need
What is Level of Information Need?
A structured approach defining exactly what, why, and when specific information is required at each project stage.
Goes beyond just detailing (LOD) and information content (LOI), focusing explicitly on information purpose and user requirements.

## Slide 78: Level of Information Need
Relationship to LOD and LOI:
  LOIN clearly defines the necessary depth (LOD) and type (LOI) of information.
  Ensures information generated is relevant, purposeful, and aligned with stakeholders' specific needs (e.g., procurement, construction planning, and facility management).
Why Use LOIN?
  Prevents overproduction or underproduction of BIM information.
  Enhances efficiency by tailoring information precisely to stakeholder requirements.
  Supports informed decision-making at every stage of the project lifecycle