## Slide 1: Introduction to BIM for Construction Management

## Slide 2: Learning objectives
After completing this course, you’ll be able to:
Model to match construction methods and use parts to improve model accuracy.
Create and manage callouts and views
Create a federated model.
Use LIDAR for construction.
Create and manage 4D simulations in Navisworks.
Segment elements to model location for scheduling tasks.
Use 4D simulations for materials planning and management.
Run clash tests, create clash reports, and retest.
Create quantity takeoffs.
Use the BIM model to add maintainable asset data.

## Slide 3: Common terms
Notes: Building Information Modeling is revolutionizing the way we approach construction projects from the smallest homes to the largest international airports. At its core is the digital process that helps all parties involved, from architects to contractors, to work smarter and more efficiently and with a clearer vision of what's ahead. BIM provides a framework for managing the digital information of a built asset, whether it's a small residential home, a bridge or something as complex as a sports stadium.

## Slide 4: Common terms
Notes: The beauty of BIM lies in its ability to facilitate collaboration and streamline information sharing across every stage of the building's lifecycle, from design through to construction, through to operation. To ensure that everyone involved in the process is working towards a unified goal. The ISO 19650 standard sets a comprehensive framework. This standard covers all aspects of the building's lifecycle, ensuring consistency and quality in every phase from conceptualization to completion.

## Slide 5: What’s at the heart of BIM?
Each element within the model is packed with data, dimensions, material, and more. This information is crucial for creating accurate construction drawings, reducing errors and keeping the project on track.
Notes: At the heart of BIM and a 3D model is a visual representation of the project. But it's not just any 3D model. Each element within the model is packed with data, dimensions, material, and more. This information is crucial for creating accurate construction drawings, reducing errors and keeping the project on track. So how does all this digital information translate in the real world construction process?

## Slide 6: Project Organization
Notes: That's where contractors come in. Contractors are hired by the client to bring the plans to life, carrying out the actual construction work. For small projects, a single contractor might handle everything. But for large, complex builds, contractors tend to work with subcontractors and appoint specialized teams to tackle specific parts of the project, such as steel fabrication, electrical installation, or facade construction.
For large and complex projects, the principal or tier one contractor takes the lead. This contractor manages the overall construction and coordinates with the various specialists and subcontractors. The key to ensuring everything runs smoothly is effective collaboration, especially when it comes to sharing BIM models. These models created by architects, engineers and specialists, are shared across platforms like the Autodesk Construction Cloud, allowing everyone to stay aligned and on the same page.

## Slide 7
Project and Cost Management
Project Closeout
And Handover
Safety Management
Operation
Quality Management
Bid Management
Qualification
Autodesk Confidential & Proprietary Information - Please do not post, copy or distribute without authorization.​
Strategic
Definition
Model Coordination
Design Collaboration
Model Conditioning
BIM Project Cycle
Cost Estimating
Takeoff
Proposal Generation
Notes: Once the design stage is complete, pre-construction begins. By now, the architecture and engineering teams have finalized the designs and the detailed BIM models are handed over to the contractors. Even though the designs are nearly complete, changes can still happen, often due to budgetary concerns or unforeseen issues.

## Slide 8
Operation
Project and Cost Management
Project Closeout
And Handover
Safety Management
Quality Management
Bid Management
Qualification
Autodesk Confidential & Proprietary Information - Please do not post, copy or distribute without authorization.​
Strategic
Definition
Model Coordination
Design Collaboration
Model Conditioning
Preparation
Cost Estimating
Takeoff
Proposal Generation
Design
Construction
Handover
Notes: Once the design stage is complete, pre-construction begins. By now, the architecture and engineering teams have finalized the designs and the detailed BIM models are handed over to the contractors. Even though the designs are nearly complete, changes can still happen, often due to budgetary concerns or unforeseen issues.

## Slide 9: Modeling to Match Construction Methods
Learning objectives:
Prepare a model with a higher level of development that is suitable for construction planning.
Divide parts to add construction detail and assign material to parts.
Use material property overrides and create parts schedules.
Add 3D details for design communication, adding annotations, text, and tags.

## Slide 10: Modeling to Match Construction Methods
When you design a structural model, the structural connections for elements depend on many factors beyond their purpose of joining elements. These factors often include the standards of the contracted engineer, the contractor, or the fabricator. Even the type of structure will influence the type of connection.
The purpose of Revit structural connections is to exchange information about the designed connection between engineers, detailers, and fabricators.

## Slide 11: Modeling to Match Construction Methods
Precast
The precast tools provide a simple, user-friendly working environment for creating 3D structural models from which shop drawings and CAM files are created.
Using the tools in the Precast ribbon tab you set-up rules for segmentation, reinforcement, shop drawings and CAM files, which are then used to automatically drive each stage.

## Slide 12: Modeling to Match Construction Methods
Join Geometry
Use the Join Geometry tool to create clean joins between 2 or more host elements that share a common face, such as walls and floors.

## Slide 13: Parts and Parts Schedules
Learning objectives:
Add details to architectural elements, including floor and wall finishes.
Divide parts to add construction detail and assign material to parts.
Use material property overrides and create a parts schedule to a structural foundation.

## Slide 14: Parts and Parts Schedules
Exclude Parts
You can exclude parts from the project so that they will not be included in material takeoffs, schedules, and other lists or calculations.
An excluded part is visible only when highlighted under the cursor or selected. An excluded part can be restored to the model as needed.

## Slide 15: Parts and Parts Schedules
Divide Parts
After an element has been designated as a part, that part can be divided into smaller parts, either by sketching division lines or by selecting reference elements that intersect the part.

## Slide 16: Design Communication
Learning objectives:
Prepare detailed construction details from design models. Use 3D details to assist with fabrication, assembly, and construction.
Use displaced elements to create 3D exploded views and details. Override graphics to highlight important components in the construction process.
Work with sheets and export pdf documents named according to ISO 19650.

## Slide 17: Design Communication
Callouts and Keynotes
Use a detail callout when you want to provide details about a part of the building model. The detail callout provides more granular information than the parent view. You can add details and annotations to the detail callout. These details do not display in the parent view.
Use keynotes to tag elements or materials with standard CSI keynotes or custom keynotes.

## Slide 18: Design Communication
Displaced Views
Displaced views can be used to illustrate the relationship that model elements have to the model as a whole.
Displaced views are similar to exploded views, but provide flexibility by allowing the displacement of selected elements or all elements. This tools is available in a 3D or perspective model, when you select one or more model elements.

## Slide 19: Design Communication
Export PDF
When batch-exporting multiple PDF files, you can create naming rules for the files. Select parameters from the views and sheets to establish the naming rules, and save the rules to your export setup.

## Slide 20: LIDAR for Construction
Learning objectives:
Describe LiDAR and how it can be used in construction workflows
Link RCP files into Revit.
Work with point clouds in Revit.

## Slide 21: LIDAR for Construction
LiDAR is a tool for capturing highly accurate models for existing buildings and landscapes.
Point clouds can be processed in Recap Pro and imported into Revit, allowing designers to take accurate measurements without taking multiple visits to the site.

## Slide 22: Cost Estimation and Quantity Takeoff
Learning objectives:
Use architectural massing and mass floor to quantify model elements.
Use formulas in schedules and material takeoffs.

## Slide 23: Cost Estimation and Quantity Takeoff
Typical construction projects are complex in nature and providing an accurate cost estimate can take a lot of time and effort.
In Revit, you can create early cost estimates by considering the mass model, You can create schedules and use them for estimating costs.
You can set up the model for quantification and perform both constructive and destructive takeoffs.

## Slide 24: Cost Estimation and Quantity Takeoff
Architectural Massing
You can use massing studies to perform a variety of tasks:
Create in-place or family-based mass instances that are specific to individual design options.
Create mass families that represent the forms associated with often-used building volumes.
Vary materials, forms, and relations between masses that represent major components of a building or development using design options.
Abstractly represent phases of a project.
Study zoning compliance, both visually and numerically, by relating a proposed building mass to the zoning envelope and floor area ratio.

## Slide 25: Cost Estimation and Quantity Takeoff
Schedules
A schedule is a tabular display of information, extracted from the properties of the elements in a project.
A schedule can list every instance of the type of element you are scheduling, or it can collapse multiple instances onto a single row, based on the schedule's grouping criteria.
You can create a schedule at any point in the design process. As you make changes to the model that affect the schedule, it automatically updates to reflect those changes. You can add a schedule to a drawing sheet.
You can export a schedule to another software program, such as a spreadsheet program.

## Slide 26: Construction Planning and Simulation in Navisworks
Learning objectives:
Create a federated model in Navisworks and adjust project origin and orientation values.
Create and manage viewpoints for the model, allowing you to set camera positions that are best for the project and for teams.
Create and manage search sets in preparation for running 4D simulations.
Associate model elements to tasks and refine construction elements in Revit to achieve a more realistic and accurate construction simulation.

## Slide 27: Construction Planning and Simulation in Navisworks
File Types
NWC files are compressed versions of the project model which update when changes are made to the source file, making for easier and quicker project workflows.
An NWF file contains links to the NWC files together with Navisworks-specific data, such as review markups. No model geometry is saved with this file format; this makes an NWF considerably smaller in size than an NWD.
An NWD file contains all model geometry together with Navisworks-specific data, such as review markups. You can think of an NWD file as a snapshot of the current state of the model.

## Slide 28: Construction Planning and Simulation in Navisworks
Viewpoints
Viewpoints are an important feature of Navisworks. They allow you to save and recall different settings related to the view and navigation of the model.
Viewpoints are snapshots taken of the model as it is displayed in the Scene View.

## Slide 29: Construction Planning and Simulation in Navisworks
Find Items
The Find Items window allows you to search for items having a common property or combination of properties.
The left pane contains the Find Selection Tree with a drop-down list at the top and enables you to select the level of item to start searching at; this can be a file, a layer, an instance, a selection set, and so on.
The right pane enables you to add the search statements (or conditions). And the buttons enable you to find the qualifying items in your scene.

## Slide 30: Construction Planning and Simulation in Navisworks
TimeLiner
The TimeLiner window enables you to attach items in the model to project tasks and simulate project schedules.

## Slide 31: Model Coordination in ACC
Learning objectives:
Define a coordination space and then create a view of combined models with specific model categories visible to act as a clash set.
View models, filter categories, and save views to manage clash tests.
Create clash test reports in preparation for distribution to project delivery teams, manage clash testing in updated models, and rerun clash tests.

## Slide 32: Model Coordination in ACC
Coordination Space and Saved Views
Clash Detection makes it easy for the entire project team, from architects and engineers to the seasoned BIM manager, to catch, clear and resolve clashes before they become a problem.
In a coordination space, you can create a federated model and decide whether to allow for automatic clash detection or not.
The Model Browser allows you to use filters to isolate building elements to be used in clash tests.
The saved view can be applied as a filter in the main clash detection results table.

## Slide 33: Model Coordination in ACC
Clash Groups and Object Exclusions
Clashes are automatically grouped to facilitate the review process and help you identify of issues.
Object exclusions can be created to exclude elements from the clash detection results.

## Slide 34: Model Coordination in ACC
Issues
Issues should be created for clashes that need attention. Issues can be assigned to team members on ACC.
These issues get updated every time a new version of the model is uploaded to the coordination space.

## Slide 35: Takeoffs in ACC
Learning objectives:
Set up classification systems
Create packages
Create takeoffs from a 3D model.

## Slide 36: Takeoffs in ACC
Quantity takeoffs are essential in estimating costs accurately in the construction industry.
To get started in ACC Takeoff, you should:
  Define a measurement system and classification systems.
  Upload 2D and 3D files in Sheets and Models to use during takeoff.
  Create takeoff packages to organize your scopes of works.

## Slide 37: Takeoffs in ACC
To start takeoff exercises, you create takeoff types and assign one or multiple outputs.
The inventory keeps track of all your takeoffs, showing the instances taken off, their associated costs, and classifications.
The inventory data can be organized and then exported to external files.

## Slide 38: Assets in ACC
Learning objectives:
Track and visualize construction components across a project's lifecycle from design through commissioning and handover using the Assets tool.

## Slide 39: Assets in ACC
Asset categories can be set up to map organize your project’s assets, map their properties, and assign status sets.
An asset status can be modified from 2D plans, 3D models, either through the ACC website, or on the mobile app.