## Slide 1: Lecture Introduction to BIM for Structural Design and Engineering

## Slide 2: Learning objectives
After completing this course, you’ll be able to:
Describe Building Information Modeling (BIM) and its role in structural engineering.
Create a new project using an architectural model.
Create structural foundations.
Model structural steel systems.
Place structural floors and slabs.
Add structural reinforcing.
Create and manage views, sections, and callouts.
Query the model to create documentation and schedules.
Use Civil 3D to place a project using shared coordinates.
Workshare Revit models to the cloud.

## Slide 3: Common terms
Notes: Building Information Modeling is revolutionizing the way we approach construction projects from the smallest homes to the largest international airports. At its core is the digital process that helps all parties involved, from architects to contractors, to work smarter and more efficiently and with a clearer vision of what's ahead. BIM provides a framework for managing the digital information of a built asset, whether it's a small residential home, a bridge or something as complex as a sports stadium.

## Slide 4: What’s at the heart of BIM?
Each element within the model is packed with data, dimensions, material, and more. This information is crucial for creating accurate construction drawings, reducing errors and keeping the project on track.
Notes: At the heart of BIM and a 3D model is a visual representation of the project. But it's not just any 3D model. Each element within the model is packed with data, dimensions, material, and more. This information is crucial for creating accurate construction drawings, reducing errors and keeping the project on track. So how does all this digital information translate in the real world construction process?

## Slide 5
Project and Cost Management
Project Closeout
And Handover
Safety Management
Operation
Quality Management
Bid Management
Qualification
Autodesk Confidential & Proprietary Information - Please do not post, copy or distribute without authorization.​
Strategic
Definition
Model Coordination
Design Collaboration
Model Conditioning
BIM Project Cycle
Cost Estimating
Takeoff
Proposal Generation
Notes: Once the design stage is complete, pre-construction begins. By now, the architecture and engineering teams have finalized the designs and the detailed BIM models are handed over to the contractors. Even though the designs are nearly complete, changes can still happen, often due to budgetary concerns or unforeseen issues.

## Slide 6: Intro to BIM for structures
What role does BIM plays in design and construction?
Navigate and review the multidisciplinary model.

## Slide 7: Project creation
A typical design project can take 1 to 5 years to design. It is imperative that it is set up properly from the start. All trades must be accounted for, and models must be set up properly using the correct templates.
A company will have a standard template that they have developed over years of trial and error. This course uses the default structural template in Revit and is provided.

## Slide 8: Project creation
Starting a new model using a structural template ensures structural settings such as visibility graphics are properly set.
A structural template also provides the correct content you need to perform structural modeling.

## Slide 9: Project creation
Linking an architectural model has several advantages. One is that you know where to start your model. Another is that the entire project will be based on the project internal origin.

## Slide 10: Project creation
Adding levels that report the top of steel elevations are coordinated with the architectural finish floor levels.
These levels can be then be monitored based on the architect’s modifications. You will receive an alert if a monitored level changes.

## Slide 11: Project creation
Adding structural grids not only gives the structural engineer the ability to layout their building but provides accurate guidelines for the entire design team.

## Slide 12: Structural foundations
Foundation design is based on many factors: the capacity and composition of the soil, the type of building, the size of the building, and the site where the building is actually being built.
Using BIM workflows and Revit, the structural engineer can relay their foundation design and coordinate with other trades.

## Slide 13: Structural foundations
Foundation walls can be added when the structural engineer knows what shape and type the building will be.
With the foundation wall sized properly, structural wall footings (known as strip or continuous) can be added to the footprint.
This ensures the loads from the foundation walls are spread into the earth covering a wider square foot area.

## Slide 14: Structural foundations
Piers and pilasters are added to a foundation to absorb the point loads from the structural columns that bear upon them.
A pier is a stand-alone vertical support member that transfers the load to a thickened spread footing. Picture a traditional pier that extends into the ocean.
A pilaster is cast against or integrated into a structural wall. This allows the point load to be transferred into the walls as well as into the footing below.
Pilasters
Piers

## Slide 15: Structural foundations
When a site is not flat, and there are valleys and hills, the footings must maintain a specific depth keeping the footings under a frost line.
Footings cannot be angled or on a slope. They need to be stepped into the hill or valley maintaining a consistent top of footing elevation.

## Slide 16: Structural steel systems
Steel systems start with adding columns at grid locations. Because the building has been carefully laid out, the columns have preset points in the model called grid intersections.
Grid intersections can be used as reference points for placing elements such as columns and beams, and help to organize and structure the module.

## Slide 17: Structural steel systems
In a typical structure, you will see beams along gridlines that frame from column to column. You will also see beams that could be bent or fabricated on a radius.
It takes careful consideration what size and shape beam you use at each location. Not only is the structural integrity impacted, but also the cost.

## Slide 18: Structural steel systems
Steel connections can be added in Revit for a basis of design but are generally detailed by the fabricator.
You will design a connection and then approve what is called a shop drawing. In most cases, the shop drawings will be modeled in a structural modeling application that sizes and creates fabrication drawings.
Use these connections sparingly in Revit for a basis of design.

## Slide 19: Structural floors and slabs
Floors are shared between architects and structural engineers. The architect depends on the structural engineer to design the thickness of the structural floor to determine their finish floor elevation.
Revit and a BIM workflow allows this coordination to take place in real-time.

## Slide 20: Structural floors and slabs
When a floor is designed in Revit not only is the concrete considered, but the structural decking is considered as well.
As the structural desk interacts with the edges that bear on framing, the decking needs to stop at the beam centerline, while the concrete cantilevers to the outside of the flange.

## Slide 21: Structural floors and slabs
If a structural slab or floor needs to pitch to a drain, or the element needs to be sloped, Revit makes this condition possible.
By setting a variable thickness to a layer, spot coordinates can be placed, allowing the floor’s thickness to be adjusted at precisely the point needed.

## Slide 22: Structural floors and slabs
Circulation such as elevator shafts and stairs need to be accommodated for in the structural model.
For a multi-level project, simply adding a hole in each floor is tedious and can lead to errors. Using a shaft opening will create a 3D void in which floors, ceilings and roofs will be cut.
The top and bottom level can be specified. This allows for one time editing and forces consistency.

## Slide 23: Structural reinforcing
When designing a foundation or any concrete element, reinforcing is the key to structural stability.
Revit comes with many rebar shapes and methods to place reinforcing into your structure. Old techniques of 2D dimensional layout are left behind by Revit’s ability to configure and design structural reinforcing.

## Slide 24: Structural reinforcing
It is important to specify how deep into the concrete the reinforcing needs to be. Rebar cover (or concrete cover) is the minimum thickness of concrete that must surround reinforcing steel within a concrete structure
  If the steel rebar is too shallow in the member, it can cause the concrete to spawl, thus exposing the rebar. The rebar will quickly rust and deteriorate.
  If the rebar is too deep, it will diminish the effectiveness of the rebar.

## Slide 25: Views sections and callouts
Revit is a 3D BIM application, and the way the 3D model is viewed is what sets it apart from most applications.
By setting up and configuring views of the model, you can quickly go from an elevation to a section or a plan to a 3D view.
Each view has a purpose and a visibility graphic controller to make the 3D model understandable.

## Slide 26: Views sections and callouts
Callouts in a model add clear, concise information focusing on crucial areas of the design.
The addition of specific views to a project allows the ability to display the model in ways that suit a variety of needs.

## Slide 27: Views sections and callouts
Sections in a model allow for an instant vertical view.
Every view created does not have to be on a sheet. Working in a 3D model lends itself to having multiple views.

## Slide 28: Documentation and data
If a tree falls in the woods, and nobody hears it did it really happen?
If you create a beautiful model and there are no printed sheets nobody will know where to find the information.

## Slide 29: Documentation and data
Creating well-organized sheets is an age-old artform. Revit allows you to create drawing sheets right in the Project Browser along with the model you carefully constructed.
You can simply drag your view to be added and after placement, you can adjust them on the sheet as required.

## Slide 30: Documentation and data
Each item you place in a model is a component with a specific designation. This designation allows you to perform a query on the model as you would do in a database.
Revit provides allows you to create schedules to categorize model elements based on sorting rules and filters.

## Slide 31: Structural analysis
Built into Revit are analytical tools used to aid in structural analysis.
By associating structural elements with analytical forces, you can prepare your model to be brought into a structural analysis application.

## Slide 32: Structural analysis
You can assign:
  Load case combinations
  Boundary condition settings
  You can also look at Loads Scaling Displays.

## Slide 33: Civil 3D data in Revit
Many projects depend on geo-locating a model. To do that, coordination with the civil engineer on the project is needed.
The ability to acquire coordinates and work between AutoCAD, Civil 3D, and Revit involves a specific workflow.

## Slide 34: Civil 3D data in Revit
Linking a version of Civil 3D Into revit is an accepted solution. To do this, you need to create a separate model in which to link both Revit and a Civil 3D drawing.
From there, you acquire and publish the coordinates from one model to another.

## Slide 35: Cloud worksharing
Revit Cloud Worksharing allows architects, engineers, and contractors to collaborate on Revit models, leading to accelerated timelines and a more efficient project workflow.
You can co-author cloud models, centralize all project design data, and improve communication and collaboration across the entire team.

## Slide 36: Cloud worksharing
Revit Cloud Worksharing requirements:
  A subscription to Revit
  A subscription to Autodesk BIM Collaborate
  Access to the Revit Cloud Worksharing service
  An Autodesk Docs account
  An invitation to at least one Autodesk Docs project
  A folder permission level that includes the ability to Edit a Autodesk Docs folder