## Slide 1: Assembly modeling

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Understand intent-driven assembly modeling in Fusion.
Describe the use of joints and constrain components.
Understand internal and external references.
Identify bodies and components in a hybrid assembly model.
Notes: Video production guidance
Use fade in/out when using these slates in video format.
Opening and closing slides should last no more than 3 seconds.
Practice-based module tutorial videos don't include music;
Tutorial videos are generally 2-10 minutes long. (After 10 there is a drop of student engagement)
See video production guidelines: https://wiki.autodesk.com/pages/viewpage.action?pageId=623205469
Language style guidance
DO use sentence case for module titles.
DO use sentence case for learning objectives.
DO use consistent punctuation at the end of each learning objective.
DO: If it’s necessary to add context by describing the content type, use the word “video”. For example, “Here’s what you’ll be able to do after this video.”
DON’T: As of 2021, we no longer use the word “lesson”.
DON’T: If possible, don’t refer to the content type in video voiceover. If you have to refer to the content type, please use "module".
DON’T include helper text above the learning objectives list.

## Slide 3: What is an assembly?
Assemblies contain multiple components that make up a larger design.
Components can be internal or external to a hybrid assembly, or external only in a standard assembly.
Components can include joints or relationships that allow for constrained motion.
Components are containers for bodies, sketches, features, coordinate systems and more.
Position 2
Position 1

## Slide 4: What is intent-driven design?
Intent-driven design allows for a clear definition of what makes a part and what makes an assembly.
Parts are single component designs.
Assemblies are created by inserting external parts.
Assembly context and relationships can be added to externally referenced parts.
Hybrid Design can be a part or assembly with internal or external components.

## Slide 5: Bodies and components
Bodies represent solid model geometry in a design or assembly.
Components represent a container for bodies that include a unique origin and other design elements such as features and sketches.
Multiple components can be nested as a sub-assembly which will be represented by a different icon.
Internal components exist only in the current design and may be grounded to the parent component or pinned in place.
External components exist as independent designs and can be referenced in multiple assemblies.
Component
Body
Group of Components
Top Level Component

## Slide 6: Common assembly tools
Insert Component – Insert an external component into the current assembly.
Insert Fastener – Insert hardware.
Add To Assembly – Add the current assembly to a new or existing assembly.
New Component – Create a new external part or assembly.
Constrain Components – Remove degrees of freedom for a component.
Joint – Define all degrees of freedom for a component.
Rigid Group – Lock multiple components together.

## Slide 7: What are joints and constraints?
Joints – Allows a user to select positions on two components, position them relative to the selection, and define their degrees of freedom.
As-Built Joint – Allows a user to define degrees of freedom between components using their current assembly position.
Constrain Components – Allows a user to position two ore more components relative to each other, reduce degrees of freedom in the assembly, and create a Constraint Relationship between the components.

## Slide 8: What are assembly references?
References
  Internal – Components are created directly in a design (Hybrid or Part). They are saved in the design and only exist in the design. Commonly referred to as Top-Down Design.
  External – Components are saved externally in their own design and are referenced or linked in an assembly. External components have a chain link icon in the browser. Commonly referred to as Bottom-Up Design.
Part – Single component design.
Assembly – Design that contains externally referenced components.
Hybrid – Design can contain internal and external components.
Derived Design – Component that is saved externally and references back to an assembly. Derived designs don’t carry any feature history but do maintain a link to the parent design.
External
Derive
Internal

## Slide 9: Which assembly method is best?
There is no correct answer to which modeling approach you should take, but there are a few key differences that may push you one way or the other.
  Externally referenced components can be reused in other designs easily.
  Externally referenced components or sub-assemblies can be worked on by other users without reserving a design.
  Derived components can be used to design fixturing or packaging for manufacture without affecting the original design.
  Hybrid Designs offer a flexible approach to the design process that often is used in single-designer workflows or smaller teams that don’t rely on collaboration.

## Slide 10: Conclusion
Assemblies are groups of components that make up a larger design.
Components are containers for bodies, sketches, features, origins, and more.
Hybrid Designs can have internal and external references.
Assembly Designs can have external references only.
Assemblies use joints or constraint relationships define the degrees of freedom between components for motion.