## Slide 1: CAM lathe

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Understand CAM turning in Fusion.
Describe the need for a tool library.
Describe toolpath creation and validation.
Identify key steps in the CAM process.
Notes: Video production guidance
Use fade in/out when using these slates in video format.
Opening and closing slides should last no more than 3 seconds.
Practice-based module tutorial videos don't include music;
Tutorial videos are generally 2-10 minutes long. (After 10 there is a drop of student engagement)
See video production guidelines: https://wiki.autodesk.com/pages/viewpage.action?pageId=623205469
Language style guidance
DO use sentence case for module titles.
DO use sentence case for learning objectives.
DO use consistent punctuation at the end of each learning objective.
DO: If it’s necessary to add context by describing the content type, use the word “video”. For example, “Here’s what you’ll be able to do after this video.”
DON’T: As of 2021, we no longer use the word “lesson”.
DON’T: If possible, don’t refer to the content type in video voiceover. If you have to refer to the content type, please use "module".
DON’T include helper text above the learning objectives list.

## Slide 3: What is CAM?
CAM stands for Computer Aided Manufacturing.
CAM is a tool used to help program CNC machines to perform complex operations.
CAM can be used to program CNC mills, lathes, waterjet machines, laser cutters, plasma cutters, 3D printers and more.
CAM tools are available in the Manufacturing workspace in Fusion.
turned part

## Slide 4: What is the CAM workflow?
In the Manufacture workspace in Fusion there are a few key elements to the workflow for CAM turning.
These are the basic steps required:
  Tool Library – A digital library used to replicate physical tools.
  Setup – Critical properties such as which machine is being used, where the coordinate system and chuck are located, and how big the stock is.
  Toolpaths – The path that a tool will take to remove material from stock. For turning the stock will rotate while the tool moves in various axes.
  Simulate – Validate toolpaths for efficient and complete stock removal.
  NC Program – The NC Program compiles machine post processor, settings, toolpaths to include as well as program number and comment.
  Setup Sheet – A document that is created to convey information about a program such as WCS location, required tools, and machine time.
  G-Code – Machine readable code that is generated by converting toolpaths to a set of instructions for a specific machine.

## Slide 5: Tool library
A tool library is a digital representation of physical tools that will be used to machine a part.
Data about the tool is stored and selected during toolpath creation.
Data contained in a tool library includes holder orientation, insert type and size, feedrate, and number.
Tool data must match a physical tool being used to avoid potential collisions and incorrect parts.
CNC machines will reference tool numbers and retrieve the tool during operation.

## Slide 6: Setup
A CAM setup contains critical information about the stock, coordinate system, and machine used.
A CAM setup identifies the chuck location for a CNC lathe.
A setup will define the safe Z location for retraction moves.
The work coordinate system location and orientation definition is stored in a setup.
Common parameters such as a program number and WCS reference are in a setup.

## Slide 7: Toolpath creation
Toolpaths are routines used to define tool motion based on geometry.
Turning toolpaths generally require the selection of geometry directly or provide an area in which to focus based on a set of planes.
Turning toolpaths contain various options for extension, offset, and suppression of specific features.
Toolpath settings will dictate the area to machine, how to machine it, and how to enter and exit the cut.

## Slide 8: Toolpath validation
Toolpath validation is critical before any program is used on a CNC machine.
Toolpaths can be validated by using in-process stock which displays a generated preview of the model after the toolpath has been run.
Simulation and Machine Simulation are used to learn more about the toolpath.
Simulations show if too much material has been removed, if a collision has happened, or if material has been left behind.
Simulations are animations that allow you to watch a sped up version of the machining.

## Slide 9: Toolpath documentation
Toolpath documentation is the last step before setting up and testing a set of toolpaths on a machine.
NC Programs are containers of information about which machine to use, which settings for that machine, and which toolpaths are going to be posted.
Posting a toolpath is a method of converting the created toolpaths in CAM to code a machine can understand.
Setup sheets are also created from an NC Program and provide a machine operator critical setup information to ensure the proper stock, tools, and coordinate system are used.

## Slide 10: Conclusion
CAM is used to create a digital tool library and toolpaths to control tool motion to manufacture parts.
Toolpath definitions in CAM are converted to machine readable code for a specified machine.
Documentation is created to provide machine operators the instructions needed to set up a new set of toolpaths.
Validation is used to verify toolpaths before any physical parts are made.