## Slide 1: Lecture Learn Fusion for CAD in 90 minutes

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Define common terminology used in Fusion.
Describe the sections of the Fusion user interface.
Identify the tools used to make solids from sketch geometry.
Describe how 2D sketches are created and used.
Identify geometric constraints in sketches.
Distinguish between bodies and components and between top-down and bottom-up modeling approaches.
Project previously created geometry to a new work plane.
Recognize how the Extrude tool adds depth to sketch profiles.
Distinguish between different joint types.
Describe the Drawing and Render workspaces.
Prepare files for 3D printing.

## Slide 3: Common terms
  2D Sketch – A 2D feature that contains geometry that may include points, lines, arcs, polygons, text, and dimensions.
  Body – A solid feature that maintains its position in cartesian space according to the location of its parent geometry.
  Component – A solid feature that moves freely in cartesian space until joints or other constraints are applied.
  Feature – Any entity that can be populated in the timeline, including sketches, arrangements, joints, patterns, etc.
  Face – A surface that constitutes all or part of a solid, mesh body, origin plane, or construction plane.
  Parent / Child relationship – When a dependency is created when geometry is consumed to create new features.
  Activate Component – When a component is activated, the subsequent features belong only the active component.
  Sub-assembly – A component that has other components nested within itself.
  Top-down modeling – A method of creating a design in which parts are designed in their natural position in an assembly
  Bottom-up modeling – A method of designing in which parts are created separately from one another and assembled afterwards.

## Slide 4: The User Interface
Data Panel: import, organize, and visualize data from various sources.
Application Bar: contains the data panel, file menu, undo and redo buttons, and tabs for open files.
Toolbar: allows workspace selection, create, modify, and analyze 3D designs.
Browser: provides an organized and hierarchical view of components, sketches, features, and assemblies within the design.
Canvas: digital workspace where models, sketches, and assemblies are created and edited.
ViewCube: provides an interactive way to orient and navigate within the workspace.
Marking Menu: provides quick access to a range of commands and tools based on the user’s current selection or context.
Navigation Bar: allows user to orbit, pan, zoom, change grid settings, and visualization settings.
Timeline: a visual representation showing the sequence of actions taken throughout a design.

## Slide 5: How to use the Browser
The browser organizes data related to the elements within the workspace.
Use the Browser to:
Edit and adjust document settings, custom views, and exportable files.
Control visibility of sketches, bodies, components, canvases, and many other types of entities.
Select and modify entities using a rich context menu.
Track and manage nesting of subassemblies, components, bodies, and more.

## Slide 6: Using the Timeline
The Timeline is a unique part of Fusion where sketches and design features are recorded in chronological order as they are created.
Select and edit features easily:
The accumulation of features in the Timeline keeps the Browser less busy than other design applications.
The controls provide a means to quickly view the steps taken to create a design and a way to quickly revert without deleting or using undo.
Selecting features for patterns and other operations can be done easily. Items can be selected and edited from here as well.

## Slide 7: Common tools for 3D solids
Sketches and sketch geometry are the basis for solid features in parametric CAD.
Extrude
Sweep
Revolve
Loft
Hole
Extrude from text

## Slide 8: What are some common 3D Solids?
Extrusions
Revolutions
Shells

## Slide 9: 2D sketches and how they are used
Sketches are the foundation from which you create solids, surfaces and T-Spline bodies. Sketch entities include lines, rectangles, circles, arcs, polygons, ellipses, slots, splines, conic curves, points, and text.
Sketches are parametrically defined by dimensions, constraints, and references to other geometry.
Sketches can be 2D or 3D and used to build geometry, trim or split solids, and even contain CNC toolpaths.
Solid
Surface
T-Spline
Sketch

## Slide 10: Sketch element identification
Fully defined
Under defined
Dimension
Constraint
Construction

## Slide 11: Where can you create a 2D sketch?
Default Plane
Construction Plane
Planar Face

## Slide 12: What are some sketch entities?
Line
Rectangle
Circle
Arc
Polygon
Slot
Spline
Text

## Slide 13: Dimensions and constraints in sketches
Dimensions – Provide numerical input for the length and location of sketch entities.
Constraints – Define the relationship of a sketch entity relative to other geometry or the construction planes and origin.

## Slide 14: Creating a fully defined sketch
Fully defined means a sketch has all its dimensions and geometric constraints specified in a way that the shape and size of the sketch all have values.
In the sketch to the right, dimensions are defined with the exception of the angled line. However, the angled line is connected to the end of two defined dimensions.

## Slide 15: What display options are available?
During sketch editing the Sketch palette provides options for features or sketch visualization.
Linetype toggle to change a sketch entity to a construction entity.
Look At to view the sketch plane from a Normal direction.
Grid and display options.
3D Sketch toggle.

## Slide 16: What is 3D sketching?
Creating a sketch in 3D allows users to generate complex curves for use with surface creation, sweep paths, or general geometry creating.
3D sketches can be used for some feature creation but not all feature creation. For example, a closed profile is required to create a solid extrude.
3D sketching is considered a more advanced workflow.

## Slide 17: Understanding line colors
Colors of sketch entities have meaning in Fusion.

## Slide 18: Bodies vs. Components
A body is a solid or surface created by various modeling operations such as extrusions, sweeps, etc.
A component is a collection of bodies and/or other components. It is a separate and functional part of a design that can interact with other components.
Body
Component

## Slide 19: The bottom-up approach
The geometry of one part is not typically influencing other surrounding parts because they are designed separately.
Careful planning is required before design work begins. It can be more difficult to communicate the design and ensure that the entire assembly fits together correctly.
Bottom-up design is a design method in which you create components separately from the rest and the focus is on individual parts that make up an assembly.

## Slide 20: The top-down approach
Individual parts are sketched and modeled together.
Critical features can be referenced between neighboring parts.
Top-down design is a design method in which you create your components in the same design. Top-down design makes it easy to create and manage relationships in parts.
An advantage of top-down assemblies is that the user can project geometry and create components based off other components already created in the design. This assures the creator that components should geometrically fit.

## Slide 21: Bodies in top-down modeling
A body is a single container for a contiguous 3D shape and bodies are contained within components.
Bodies
Bodies are located in 3D (cartesian) space by the position of the 2D profiles from which they were created.
Bodies cannot be moved freely so that there is no chance of misalignment as modifications are made that are meant to effect multiple bodies.
Bodies are quickly modeled and updated in reference to one another. If you need to create joints and motion between bodies, they must reside in separate components.

## Slide 22: Components in top-down modeling
A component is a container for design elements such as sketches, construction geometry, bodies, joints, origins, and even other components.
Components
Converting bodies to components allows for joints and other motions to be applied to parts that must interact and move to accomplish their purpose.
Each component is capable of motion and has its own unique origin, coordinate system, timeline, name, number, and description.
A Fusion assembly is created when a group of two or more components is joined together within a design.

## Slide 23: Combining top-down and bottom-up approaches
The Fusion environment encourages top-down modeling practices and provides elements that make this approach easy. However, you can use either method or a combination of design methods according to project needs.
Importing components
Some components are ready made and available via several third-party services.
Inserting and joining components into assemblies is an example of designing efficiently using a blend of top-down and bottom-up strategies.

## Slide 24: Projecting geometry
Projecting geometry allows the user to include points, lines, arc, circles, and other 2D geometry to a current sketch plane.
After creating a new sketch plane, you can project geometry and it will be projected into the current plane, further simplifying the design process.

## Slide 25: Creating a sweep
A sweep allows a 2D sketch to serve as the cross-sectional shape to “sweep” or continue along a path
The shape is combined with a path, which is usually a series of lines, both curved and straight.

## Slide 26: Thin Extrude
The Extrude tool adds depth to sketch profiles or faces. Thin Extrude is an excellent way to make a wall or flange from sketch geometry as you can specify wall thickness with it.
Wall thickness and position
Thin extrude provides a simple method for creating a wall and controlling its thickness without having to edit a sketch.
Thin extrude is a good alternative to shell when varied for wall thicknesses are needed.

## Slide 27: Thin Extrude
Adjusting the width of the cut
Thin extrusions as cuts may provide more options for modifying outcomes than Emboss.
“Wall Thickness” provides an easy way to increase or decrease the width of the cut along the selected profile, allowing for easy modification.

## Slide 28: Joints
Joints are placed between components to model both positioning as well as motion.
There are 7 types of joints available in Fusion: Rigid, Revolute, Slider, Cylindrical, Pin-Slot, Planar, and Ball.

## Slide 29: As-built joints in top-down modeling
As-built joints allows you define the relative motion between components without repositioning them in Fusion.
As-built joints
Use for components that are already in position and need to be joined.
This method of applying joints only requires a joint type and joint origin snap point be selected.

## Slide 30: Drawing workspace
Create a dimensioned drawing with multiple views in the Drawing workspace.
Multiview drawings are a method in which the designer can send design assemblies, animations, and necessary dimensions to fabricators and machinists.

## Slide 31: Render workspace
The rendering environment allows you to see the design in a more realistic environment.
You can:
  Add materials and textures
  Change the lighting
  Change camera angles
  Change/create environments
  See the design in a “marketing” environment

## Slide 32: Sharing a design
There are multiple ways to share a design:
  Link
  Exporting
  3D Printing

## Slide 33: 3D printing
3D printing a design allows the creator to see a physical prototype. It is important to note, many 3D printing materials are not food-safe. In the Tumbler lesson, material choice is critical if used for food consumption. Select an FDA-approved food safe material such as PETG. There is a lesson in the practice exercises in which a drink coaster was designed and can be printed in other material choices.
Right-click a component in the Browser and select Save As Mesh. In the dialog, select the desired units and save the mesh to the computer.