## Slide 1
Step-by-step guide
Create a fully constrained sketch
Begin a design by sketching a tumbler cup. You’ll create the sketch and then learn about geometric constraints and how they are used to make the process easier. Add and edit dimensions to the sketch.
Learning objectives:
Create a 2-dimensional sketch.
Apply dimensions and constraints.
Add geometric constraints to a sketch.
Create a fully constrained sketch.
The completed exercise

## Slide 2
1. Before you begin sketching, set your units of measure to inches. From the Browser, expand Document Settings. Click Change Active Units and select the desired units.
Save the design by clicking Save in the Application Bar and name the design MyTumbler.
Figure 1. Expanding Document Settings to adjust active
units in the sketch.
2. To create a 2-dimensional sketch, in the Create group, click Create Sketch.
Figure 2. Clicking Create Sketch to access the sketch
tools.

## Slide 3
3. To enter sketching mode, click a plane to begin. There are 3 planes to choose from in the canvas area. To begin creating the profile of the tumbler cup, choose the X-Y plane.
Figure 3. Selecting a work plane will allow you to begin
sketching.
4. Sketch tools are now available in the toolbar.
Click the Line tool or press L to begin the profile. Once the 2-dimensional sketch is fully-defined, you’ll create a revolve. This object is symmetrical, so you will only need to sketch half of the object.
Figure 4. Selecting the Line tool will allow you to begin
creating the profile of the tumbler.

## Slide 4
5. It is best practice to begin a sketch at the origin. This will assist you later when you apply dimensional and geometrical constraints.
Figure 5. Starting at the origin makes it easier to fully
define a sketch.
6. Select the origin point. As you do, notice the start of the line snaps into place. Moving the pointer away from the origin will allow the line to extend and you will notice two- dimension inputs.
Figure 6. Two options for dimensioning: one is the length of the line and the other is the angle from the X
axis.

## Slide 5
7. To define the height of the tumbler cup, draw a vertical line 9" by typing
9. Make sure the angle is 90 degrees and press Enter.
NOTE: Typing measurements in the box and pressing Tab allows you to toggle between the length and angular dimensions
Figure 7. Defining the height of the tumbler.
8. After placing the line, press the Escape key to begin another line at the origin. Create a 2" line extending to the right.
Figure 8. Beginning a line from the origin that extends
to the right a distance of 2".

## Slide 6
9. Create a line coming from the top of the 9" vertical line, to the right 3". Then, click at the end of the 3" line and draw a line down 1".
Figure 9. Creating the lines for the top of the tumbler.
10. Connect the end points. You will notice the shape turns blue. The blue shading indicates the shape is fully constrained. Click Finish Sketch and save the file
Figure 10. Finishing the profile.