## Slide 1
Step-by-step guide
Create features from 2D sketches
Create a 3D body from a 2D sketch. You’ll learn how to extrude and revolve a profile first and then how to hollow bodies using the Shell command. You’ll also use the Fillet tool to create rounded edges for aesthetics and functionality.
Learning objectives:
Create features and a solid body from 2D sketches.
Extrude and revolve a profile.
Hollow a body by using the Shell tool.
Create round edges using the Fillet tool.
The completed exercise

## Slide 2
1. Open the Data Panel and then open the MyTumbler sketch you created in the previous video.
NOTE: You can also use the supplied
Module2-01.f3d file in the course downloads.
Figure 1. The Tumbler sketch.
2. One of the most commonly used tools in 3D modeling is the Extrude tool. In the Create group, click Extrude.
Figure 2. The Extrude tool.

## Slide 3
3. Click the fully strained sketch. Set the distance to 1" and press Enter.
TIP: Use the Orbit tool to move the sketch and view the extrusion.
Since the extrusion does not give the desired result for the tumbler design that you are building, click Undo in the Application Bar and return to your original sketch.
Figure 3. Setting the Extrude distance to 1”.
4. For this project, you’ll use the Revolve tool. In the Create group, click Revolve. You’ll be prompted to choose a Profile and then an Axis to revolve around. It is possible that your profile will already be selected. If so, your profile will be blue.
The profile will be the first vertical line you drew in the sketch. The axis will be the 9” line. After clicking the axis, Fusion will provide a preview.
In the Operation drop-down list, click New Component. Click OK and the outside shape of the tumbler will be created in 3D.
Figure 4. Selecting the profile and axis.

## Slide 4
5. In the Browser, click Component to rename it. Type Tumbler in the field.
Figure 5. Renaming the component Tumbler.
6. Now you’ll hollow out the tumbler by creating a shell. In the Modify group, click Shell. Then click the area you wish to shell. In this case, click the top planar face of the Tumbler. Drag the arrow and set the shell distance to .125". Click OK.
Figure 5. Shelling the Tumbler.
7. Orbit the tumbler to the bottom edge. In the Modify group, click Fillet and apply a .125" fillet to the bottom of the tumbler. Click OK and then save the file.
Figure 6. Applying a fillet to the bottom edge of
the tumbler.