## Slide 1
Step-by-step guide
Create new components in top-down assemblies
Learn about bodies and components and how they are used to create assemblies as you begin creating additional components to your tumbler design. You’ll discover key differences between top-down and bottom-up assemblies and gain a better understanding of workflows in Fusion.
Learning objectives:
Distinguish between bodies and components.
Define top-down and bottom-up assemblies.
Create a new component in an assembly file.
The completed exercise

## Slide 2
1. Open the MyTumbler file you created in the previous video. Before creating the next component, make sure the radio button to the right of the design file is selected.
NOTE: You can also use the Module4- 01.f3d file in the course downloads.
Figure 1. Open the Tumbler.
2. In the Assemble group, click New Component. Name the component Gasket.
Figure 2. You will need to select the Create Sketch icon to
access the sketch tools.
3. Two components are listed in the Browser.
Figure 3. Multiple components.

## Slide 3
4. The Tumbler is now translucent because it is not the activated component. The active component is the Gasket.
Figure 4. Confirming the active component.
5. Now you’ll create an extrusion for the gasket.
Make sure the Gasket is the active component. In the Create group, click Extrude. Click between the inner and outer circle of your Tumbler at the top. Extrude the gasket .125" up from the cup. Click OK to finish the extrusion and save the file with the description of added gasket.
Figure 5. Creating the gasket.