## Slide 1
Exercise duration: ~15 minutes
Use existing geometry
Learn how to take existing geometry and use it again to create new components. You’ll also create an extrusion and further modify the design by using the Shell tool and Hole tool.
Learning objectives:
Use existing geometry to create new components.
Extrude the design.
Use the Shell tool and Hole tool to modify the design.
The completed exercise
Step-by-step guide: Use existing geometry
Page 1

## Slide 2
1. Open the MyTumbler project you created previously. In the Browser, click the radio button to the right of the MyTumbler project.
Figure 1. Activating the entire assembly.
2. In the Assembly tab, click New Component. Name it Lid. Click OK.
In the Browser, you will notice the radio to the right of the Lid is now selected.
Figure 2. Creating the Lid component.

## Slide 3
3. Select the new sketch and click on the top planar face of the gasket. Extrude the inside circle into the cup
-1".
Figure 3. Creating the inside extrusion of the Lid.
4. In the Browser, expand the Sketches folder under the Lid component and click on the eye icon to the left of Sketch1. This will allow you to reuse the original sketch.
Figure 4. Reusing a sketch.

## Slide 4
5. Click the top planar level of the tumbler. In the Create group, click Create Sketch. Draw a circle on the top of the lid that is concentric with the outer circle (it should be 6"). Click Finish Sketch.
Figure 5. Drawing circle that is concentric with the
exterior circle of the lid.

## Slide 5
6. Select the outside circular ring and the inside (extrusion you created previously). Extrude both the inside and outside circular profiles upward a distance of .1875" and click OK.
Figure 5. Extruding the top of the lid.
7. To account for overflow, create a new sketch on the top planar face of the lid. Create a circle with a diameter of 5". Create an extrusion that is a distance of -.063".
Figure 6. Creating an inner circle.

## Slide 6
8.
Now you’ll create the shell to hollow out the lid. Turn off the visibility of the Tumbler to access the Lid. In the Modify group, click the Shell tool. Select the bottom planar face of the lid.
Change the thickness to
.125" and click OK.
Figure 8. Creating the shell.
9. You’ll use the Hole tool to create a hole in the top of the lid for the straw.
Turn the visibility of the Tumbler back on. In the Create group, click the Hole tool. Click the top of the Lid. Drag the center of the hole to match the origin of the lid. Change the diameter of the hole to .375" and depth of the hold to .1875".
Turn the visibility of the entire assembly on and save the file.
Figure 9. Creating a hole.