## Slide 1
Step-by-step guide
Create a sweep feature
The Sweet tool is used to extrude a profile along a path to create a solid body. Learn to create a sweep for the drinking straw and discover how the bottom-up approach to design can be used.
Learning objectives:
Create a sweep.
Use the Measure tool to determine select dimensions of modeled parts.
Insert a design file into an assembly using the bottom-up approach.
The completed exercise

## Slide 2
1. Open the full, completed assembly that is included in the provided datasets, Autodesk_Tumbler.f3z.
You’ll use the file as a reference to determine the measurement of the hole on the lid that allows for the straw to move through it.
Figure 1a. Accessing the Autodesk_Tumbler
Turn off the visibility of the Tumbler, Gasket, and the Autodesk_Tumbler_Straw by clicking the eye icons next to their
names in the Browser.
assembly in the Data Panel.
Figure 2b. Turning off visibility of components.
2. In the Inspect group, click Measure to measure the hole on the Lid. Note the measurements in the Measure dialog indicates a diameter of .375 in. Click Close. Turn the visibility of the components back on and click Home next to the ViewCube to return to the default view.
Figure 2. Using the Measure tool to determine
diameter for the straw hole.
3. In the next steps, you’ll create the straw design file as a separate design and then insert it into your MyTumbler design.
Figure 3. Creating a New Design..

## Slide 3
Create a new design file by clicking New Design (the + icon) on the Application Bar. Save it with the name MyTumbler_Straw.
4. Create a sketch and draw a .35" circle on the origin. Using the Offset tool located in the Modify group of the sketch environment, select the .35" circle and drag a circle inside -.02". This will be referred to as the sketch profile. Click Finish Sketch.
Figure 4. Creating the sketch profile.

## Slide 4
5. Now you’ll create a sketch for the path. In the Browser, click the eye icon next to Origin. Select a plane that is perpendicular to the originally selected plane for the profile and click New Sketch. You can also right-click the plane and select Create Sketch.
Use the Line tool and start on the origin. Create a line 1.25" going in the right direction from the origin. Continue with the Line tool and draw a line upwards and to the right at an angle. Type in a length of 10" for this line. Press the Tab key and type 60 to set the angle to 60 degrees.
This will be known as the pathway.
Figure 5. Create the path sketch.

## Slide 5
6. Add a .75" fillet where the 1.25" and 10" lines come together. (The angle is 120 degrees at the intersections of the lines.)
In the Modify group, click Fillet. Fusion will automatically select the intersection of the lines as the point to create the fillet.
Type .75 for the fillet and press Enter. Click Finish Sketch.
Figure 6. Adding a fillet in sketch mode.
7. Now you’ll create the sweep.
Click the Home icon on the ViewCube to return to the default view. In the Create group, click Sweep.
Figure 7. Creating a sweep feature.

## Slide 6
8. Be sure Profile is selected in the Sweep box and then click the space in between the inner and outer circle of the first sketch.
Figure 6. Selecting the profile sketch.
9. Click the Path box and then click the line you made for the path. The sweep has been created.
In the Browser, turn the visibility of Origin off. Click OK and save the file.
Figure 7. Choosing the path..

## Slide 7
10. Now you’ll create a bottom-up assembly and insert the straw into the tumbler design.
In the Data Panel, open the latest version of the MyTumbler assembly.
You should also see MyTumbler_Straw file in the Data Panel. On Windows computers, you can drag the file into the assembly. On Windows and Mac computers, you can right-click on the Straw file and click Insert into Current Design.
Figure 8. Open your Tumbler Assembly and Drag the Straw
in From Data Panel.
11. Use the move tools to position the straw in order to see the bottom of it. Click OK to exit the Move/Copy dialog.
Figure 9. Getting a useful orientation.

## Slide 8
12. In the Assemble group, click Joint
Figure 10. Choosing Joint from the Assemble group.
13. Zoom in to the bottom of the straw and choose the snap point. Click the bottom of the straw and then the click the hole on the lid for the second snap point. You might need to click the Flip button in the Position tab of the Joint dialog if the straw goes in upside down.
Figure 13. Positioning the straw.

## Slide 9
14. To add motion to the straw, click the Motion tab. Then choose Slider in the Type drop-down list. For Joint Motion Limits, set the Maximum to 8. Click the Play button to preview the motion.
Click OK. Save the file.
Figure 14. Adding a slider motion.