## Slide 1
Exercise duration: ~15 minutes
Create dimensioned drawings
When you create a drawing from the modeling environment, the system generates a 2D projection of the components you select. The drawing view that is generated is a 2D projection of the components you selected. This is referred to as a base view and once you place the view in the drawing, you can generate orthogonal and isometric projected views from it. Learn how to create a drawing and apply dimensions and notes to it.
Learning objectives:
Create a dimensioned drawing of a component.
Create the base view in a new detailed drawing.
Create a dimensioned view.
Apply appropriate dimensioning techniques.
The completed exercise

## Slide 2
1. Open the MyTumbler assembly and close the Data Panel to provide more workspace. From the Workspace menu, select Drawing > From Design.
Figure 1. Accessing the Drawing workspace.
2. In the Contents drop-down list, choose Select. This allows you to choose a single component in the assembly. Select the Tumbler component. Choose ASME for the Dimensioning Standard and click OK.
Figure 2. Setting up the drawing.

## Slide 3
3. Fusion will load the drawing and automatically select the base view. This is known as the front view. Place the tumbler toward the lower-left corner. Be sure to leave some space as you will add dimensions.
For Style, choose Visible and Hidden Edges. Fusion chooses a scale that will fit the drawing size, however, you can change it later if you decide to. When possible, try to scale at 1:1. Click all the icons for Center Marks so that these features are included in dependent views as well. Click OK.
Figure 3. Placing the base view.
4. Now you will project the other views. You can project views in eight different directions. Typically, however, there is a front, top, isometric, and right-side view.
In the Create group, click Projected View. Select the parent view (Front) and then move the pointer to the desired location for other views. Click the checkmark or right-click and choose OK to close.
Figure 4. Projecting other views.

## Slide 4
5. It is recommended to shade the isometric view. Double-click the isometric view and click the Shaded icon in the Drawing View dialog. Click Close.
Figure 5. Adding a Shaded style to the isometric view.
6. With this component, you will notice the front and right-side views are identical. Right-click the right-side view and click Delete in the menu.
Figure 6. Deleting the right-side view..

## Slide 5
7. To begin the dimensioning process, select the Dimension tool in the Dimensions group on the toolbar.
On the base/front view, click on the bottom line of the cup. Then click the next horizontal line up (the bottom of the lid). Drag the dimension out. The dimension will be 8. Click on the bottom line again. Click the top line and drag the dimension out. This number should be 9.
Figure 7. Applying dimensions.
8. Click the inside wall of the cup and then the outside wall of the cup. This will be .13". After placing the dimension, double-click it, press the spacebar, and type SHELL. This will let the fabricator know it is a .13” shell.
Figure 8. Adding a shell note.
9. In the top view, you will dimension all three visible circles. In the Dimensions group, click Dimension. Click the inside circle. Move the pointer outward and place the dimension. Repeat this for all three circles.
Click the Fit icon at the bottom of the screen and the dimension drawing will be centered on the screen. When finished, save the file.
Figure 9. Adding dimensions.

## Slide 6
10. A quick way to add dimensions is to use Auto Dimensions.
Delete the dimensions that you added. In the Dimensions group, click Auto Dimensions. You now have a variety of dimension styles that you can choose from in the list of suggestions. It is still useful to know how to add dimensions but this is a great tool to use.
Figure 9. Using Auto Dimensions.