## Slide 1
Step-by-step guide
Render a project environment
Rendering allows you to visualize how products would look in an environment. You’ll learn how to apply different materials to your tumbler as well as change the lighting. You will also change backgrounds and submit a render to the cloud to save resources on your computer.
Learning objectives:
Apply visual settings.
Modify render settings.
Submit a render to the cloud.
The completed exercise
Page 1

## Slide 2
1. Open your MyTumbler assembly and close the Data Panel. From the Workspace menu, select Render. Now you are in the Render workspace.
Figure 1. Entering the Render workspace.
2. Choose the color wheel to change the appearance of the tumbler.
Figure 2. Opening Appearances.

## Slide 3
3. Expand the Plastic folder and then expand Transparent. Select Acrylic (Clear) and drag it to the tumbler lid. While here, apply Acrylic (Clear) to the straw as well.
Figure 3. Applying Acrylic to the Lid and Straw.
4. Expand the Miscellaneous folder and then the Rubber folder. Choose Silicone (White) and drag it to the gasket. If you are unable to drag it to the part in the Canvas, drag it to the Gasket component in the Browser.
Figure 4. Applying Silicone to the gasket.

## Slide 4
5. Expand Metal and then Stainless. Choose Stainless Steel – Brushed Radial and drag it to the tumbler cup. Close the Appearance dialog.
NOTE: Experiment with different appearances. This example is one of many appearances you can choose from.
Figure 5. Adding Stainless Steel to the tumbler.
6. Click the Scene Settings icon in the Setup group.
In the Scene Settings dialog, experiment with the settings available. The first area is the Environment group. You can drag the slider and adjust the Brightness here. If you click the Position icon, you are able to rotate the light source from the environment while keeping the object stationary. Adjust the Ground Scale here as well.
Figure 6. Scene Settings.

## Slide 5
7. Choose between Solid Color and Environment in the Background drop-down list. You can apply a new color or create a custom color if Solid Color is selected.
If you select the Ground Plane checkbox, Flatten Ground and Reflections will appear as options. You can also change the Roughness of the Reflections with the slider bar.
NOTE: Flatten Ground can often skew the image so be careful when selecting this option.
Figure 7. Choosing Settings for Scene Settings.
8. In the Camera group, there are three options to choose from in the drop-down list: Perspective, Ortho, and Perspective with Ortho Faces. You can adjust the Focal Length and the Exposure as well as the Depth of Field if you have Ray Tracing enabled and the Aspect Ratio selected.
Figure 8. Camera settings.

## Slide 6
9. To use the Environment Library, change the Background drop-down list from Solid Color to Environment. In the Environment Library tab, you can choose different 3D environments to place your tumbler in. By default, there are several environment lighting choices. There are also some scenes you will need to download before they can be used. Return to the Settings tab, and if needed, adjust the Focal Length to zoom in and out of the environment. Once completed, click Close.
Figure 9. The Environment Library tab.
10. You can also add decals to your design. In the Setup group, click the Decal icon. In the Insert dialog, click Insert From My Computer and navigate to image files on your computer to use as decals.
Figure 10. Inserting an image to use as a decal.
11. Select the face you would like to apply the decal to and place it according to the design.
Figure 11. Applying a decal to the tumbler.

## Slide 7
12. You can also add a texture map control which allows you to rotate and change the look of the appearance. Change the Project Type settings to see the various controls. Box is used in the example. Click OK.
Figure 12. Applying texture map control to the tumbler.
13. There are a couple of options for rendering: In-canvas and Rendering for the Web, Cloud, and Mobile. In- canvas rendering will utilize your computer hardware to create the rendering. Cloud rendering will utilize resources from the cloud to perform the rendering rather than using your computer resources.
Click the Render icon (it looks like a tea kettle). Choose your desired settings for web, mobile, print, video, or custom, and then whether you want to render in the cloud or locally, as well as quality. Notice the number of cloud credits your setup will cost. There is no cost for Autodesk Education accounts, but each cloud rendering job has a limit of 16.
Figure 13. Choosing Render for the Cloud Renderer.

## Slide 8
14. When you are comfortable with the settings, click Render. The rendering will appear in the bottom of the screen and when finished, will appear in the Rendering Gallery.
Figure 14. The rendered image will appear in the
Rendering Gallery.