## Slide 1
Step-by-step guide
Export, share, and print
Learn how to share your files with others as well as set your files up to be exported for 3D printing.
Learning objectives:
Share a link to a design.
Prepare and export files for 3D printing.
The completed exercise

## Slide 2
1. To share your design, click the File icon in the top-left corner of the Application Bar. Click Share File Link.
Figure 1. One method to share the file.
2. Select the checkbox to share the latest version with anyone using this link. A link will be generated for you to copy and paste. You may also choose to allow the item to be downloaded or password protected.
Figure 2. Creating a shareable link.
3. To 3D print your design, right-click the name of the assembly or component from the Browser and select Save As Mesh.
Figure 3. Save As Mesh.

## Slide 3
4. In the Format drop-down list, there are several options to choose from. The most common is STL (Binary) although 3MF and OBJ are becoming more widely used. Set the Unit Type to Millimeter. This setting is dependent on your 3D printer. Set the Refinement to High and select the Preview Mesh checkbox. Click OK when finished.
You will be prompted to save the file to your computer. Once you do, your STL file will be ready to be imported into the slicer you use for your 3D printer.
NOTE: 3D printing a design allows the creator to see a physical prototype. It is important to note, many 3D printing materials are not food-safe. In the Tumbler lesson, material choice is critical if used for food consumption. If you decide to print and use the tumbler, select an FDA-approved food safe material such as PETG. There is a lesson in the practice exercises in which a drink coaster was designed and can be printed in other material choices.
Figure 4. Save As Mesh settings.