## Slide 1: Feeds and speeds theory

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Understand common terms related to calculating feeds and speeds
Use formulas to calculate things like SFM, RPM, and IPM
Understand basic formulas used to calculate feeds and speeds
Learn the differences between traditional roughing and high efficiency roughing

## Slide 3: Common terms
  Spindle Speed (RPM): Revolutions per Minute or the speeds at which the tool will rotate
  Cutting Feed rate (in/min): The linear speed at which a tool is moving.
  Surface footage (SFM): Linear feet a rotating cutter travels in one minute at a given RPM
  Cutter force: The resistance of the material against the intrusion of the cutting tool.
  Cutter-workpiece engagement (CWE): the instantaneous contact geometry between the cutter and the in-process workpiece during machining. It plays an important role in machining process simulation and directly affects the calculation of the predicted cutting forces and torques.
  Plunge/Lead-in/Lead-out/Ramp: Various types of tool movements that often require a variation to the cutting federate.
  Feed per tooth (in): Amount of material each tooth on a tool will remove per revolution. Also known as Chip Load.
  Inch per revolution (ipr): Sum of material removed by all teeth per revolution.
  Stepdown: The amount a tool will engage material vertically and is typically a ratio of the tool diameter based on specific cutter movements.

## Slide 4: Calculating feeds and speeds
  Tool manufacturers generally don’t provide RPM or cutting feedrates for tools
  Manufacturers provide SFM ranges and IPT values
    SFM ranges are provided because often carbide tools can be run at a faster RPM than spindles are capable of running
  Why? Spindle specifications
    Different spindle tapers (R8, HSK, BT-30, CAT-40, CAT-50, etc.)
    Maximum spindle RPM’s vary between machines
    Horsepower ratings vary from machine to machine
  Rigidity of machine
    Larger machines with higher horsepower spindles can take a bigger cut than a smaller machine with less horsepower
  Rigidity of workholding
    The better stock is held, the easier it is for the stock to be cut
    If stock is not held rigidly, it can’t be cut as aggressively due to factors such as chatter and vibration
Notes: If SFM is higher than a machine spindle is capable of running, use the maximum RPM of spindle and refer to the tooling manufacturers IPT recommendations

## Slide 5: Calculating feeds and speeds
A baseline federate and spindle speed is often acquired from a tool manufacturer. This value will be based on the tool diameter, number of cutting flutes and their geometry, tool coatings, material to be cut, rigidity of the work holding and type of material that is being cut.
  A ½” Diameter 3 flute Endmill might give you a range of values.
    Depth of cut = 2.0 x Diameter
    Side cut = 0.1 x Diameter
    Cutting Speed = 820 – 3250 SFM(surface feet per minute) for Non-ferrous materials
    Feed Per Tooth for side milling = 0.0045 (IPT)
    Feed Per Tooth for slotting = 0.0045 * 0.2 = 0.0009 (IPT)
  General formulas
    SFM: (RPM x Tool Diameter) / 3.82
    RPM: (3.82 / SFM)/ Tool Diameter
    IPM: # of teeth x Inch Per Tooth x RPM
    IPT: (IPM / RPM) / # of teeth
    Inch(in) to millimeter (mm): Inch x 25.4
    Millimeter (mm): to inch(in) : mm/25.4 or mm x 0.03937

## Slide 6: Calculating feeds and speeds (continued)
Baseline values in combination with a specific machine should be used as a starting point and adjusted up/down at the machine control to influence future programs.
Test cuts in the same material will help ensure efficient cutting practices.
  Sample ½” Diameter 3 flute Endmill.
    Depth of cut = 2.0 x Diameter
    Side cut = 0.1 x Diameter
    Cutting Speed = 820 – 3250 SFM(surface feet per minute) for Non-ferrous materials
    Feed Per Tooth for side milling = 0.0045 (IPT)
    Feed Per Tooth for slotting = 0.0045 * 0.2 = 0.0009 (IPT)
Calculating Feed rate to be run at 7500 RPMS:
  IPM = # of teeth x IPT x RPM
  IPM = 3 x 0.0045 x 7500
  IPM = 101.25 Inches per minute feedrate
  Note: The feeds and speeds examples and calculations for this guide are designed for aluminum. If other materials such as steels are used, speeds and feeds calculations will need to be adjusted.

## Slide 7: Cutting Operation Types
Slotting
  Full width of cutter
  Not a preferable cut, but can be necessary at times
Traditional roughing
  Shallow depth of cut/large width of cut
  In tight corners, tool experiences slotting characteristics
  Good toolpath for shallow features and soft materials
  Wears out the bottom portion of the tool while the rest of the cutting flute is still good
High efficiency roughing
  Modern roughing toolpath
  Deep depth of cut/small width of cut
  No sharp loads on tool in tight corners
  Makes use of the entire cutting flute for longer tool life
Notes: Traditional roughing rules of thumb are ½ of the tool diameter for cutting depth and 75% to 90% of the tool diameter for stepover
High efficiency roughing rules of thumb are 2x tool diameter for cutting depth and 20% of the tool diameter for stepover

## Slide 8: High Efficiency Roughing
Traditional
Roughing
Notes: Representation of traditional roughing vs high efficiency roughing showing how the toolpath varies when entering tight corners
Traditional roughing offsets the shape in the amount of stepover the users specified.
High Efficiency Roughing (Adaptive Clearing) maintains a constant cutter engagement and monitors tool engagement angle.
Optimal load is used instead of stepover with adaptive clearing because the stepover may be reduced in tight corners to maintain tool engagement angle

## Slide 9: High Efficiency Roughing
Traditional
Roughing
Notes: Representation showing the cutting path changing from a desired cutter engagement angle to a full slotting toolpath for traditional roughing.
Representation showing how adaptive clearing maintains the constant tool engagement angle instead of becoming a full slotting toolpath

## Slide 10: Traditional Roughing
Load spikes in internal corners
Axial depth is of cut is the only constantly controlled parameter
Notes: Traditional roughing uses wears out the tip of the tool leaving much of the tool unused when the tip of the tool is worn out
The distance from fulcrum of the tool to the tip of the tool leads to increased tool deflection

## Slide 11: High Efficiency Roughing
Use the entire tool!
Full control over Radial and Axial depth of cut
Notes: Adaptive clearing takes a much deeper depth of cut with a smaller width of cut allowing the majority of the cutting flutes to be used
Longer tool life since the entire tool is used
Less tool deflection since the the cutting surfaces of the tool are closer to the fulcrum

## Slide 12: Helpful Links
Haas Tip of the Day video Speed and Feeds: Inch
Haas Tip of the Day Speeds and Feeds video: Metric
Haas Tip of the Day Your Feedrate is wrong!