## Slide 1: Flow of data
Notes: Do we want to animate this ? what is a good transition from the previous slide?
Is Haas ok with this branding?

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Explain the workflow of the engineer/designer
Explain the workflow of the programmer
Explain the workflow of the operator

## Slide 3: Data flow
Programmer receives file
3D Model
2D Print
Programmer determines stock, work holding, order of operations, and tools
File is programmed
Inspection Document created
Setup Sheet Created
NC File Generated
Raw material is prepped
Operator sets up work holding, tools, and stock based on setup sheet
Part is inspected based on print and inspection document
Part moved to shipping if it passes inspection
Part is reworked or started from scratch if it doesn’t pass inspection
Operator runs all setups and NC Programs until part is complete

## Slide 4: Data flow
The programmer programs the part.
Programmer receives file as either a 3D model or a 2D print. If 2D print, programmer will create a 3D model of the 2D print.
Programmer will determine process plan including working holding, tools to be used, and order of operations.
Setups and toolpaths are added to the 3D model as required to fully program the part
Inspection document is created based on drawing and dimensions that need to be inspected.
  Can be CAM inspection document, electronic inspection sheet, or printed inspection sheet
Setup sheet is generated for all the setups showing stock sizes, part orientations, WCS location, and tools used along with relevant information as to how the tool should be set up.
NC File is generated for each setup that needs to be run to complete the part.

## Slide 5: Data flow
The operator runs part.
Stock is cut and prepped based on setup sheet.
Operator reviews setup sheet to install proper work holding in machine and sets up tools to run each setup listed on setup sheet.
Operator runs each setup until the part is complete.
Notes: Video production guidance
Use fade in/out when using these slates in video format.
Opening and closing slides should last no more than 3 seconds.
Practice-based module tutorial videos don't include music;
Tutorial videos are generally 2-10 minutes long. (After 10 there is a drop of student engagement)
Language style guidance
DO use sentence case for module titles.
DO use sentence case for learning objectives.
DO use consistent punctuation at the end of each learning objective.
DO: If it’s necessary to add context by describing the content type, use the word “video”. For example, “Here’s what you’ll be able to do after this video.”
DON’T: As of 2021, we no longer use the word “lesson”.
DON’T: If possible, don’t refer to the content type in video voiceover. If you have to refer to the content type, please use "module".
DON’T include helper text above the learning objectives list.

## Slide 6: Data flow
The operator inspects the part.
Part is inspected
  This can be while on the machine by the operator or moved to a separate inspection station where precision measuring tools such as calipers, micrometers, dial indicators, and even CMM’s (Coordinate Measuring Machine) will be used to verify part meets dimensional tolerances
If the part meets specifications, the part is moved to shipping
If the part doesn’t meet specifications, the part will either be moved back to the machine to be reworked, or the part will be rerun from scratch and the process of inspection will be repeated