## Slide 1: Following part datum

## Slide 2: Learning objectives
After completing this section, you’ll be able to:
Determine datum and critical dimensions
Identify datums and critical dimensions
Understand best practices for datums and critical dimensions

## Slide 3: Determining datums and critical dimensions
  Refer to print or model-based dimensions on 3D model for critical dimensions
  First OP WCS location is not critical because the part is inside of the raw stock that has not been machined yet
  Once features have been machined in OP1, the WCS location will follow the datums that represent the critical features listed on the print
  After reviewing the print or model-based dimensions of the 3D model, determine the order of operations of how the part should be machined to meet the given tolerances

## Slide 4: Determining datums and critical dimensions
  Below is the print for a part that is to be machined.
  Critical dimensions have been circled to note their importance (typically intended for inspection)
Notes: Take some time to review the print to determine an order of operations before jumping into the process
Note critical dimensions called out or tight tolerances
Determine a plan as to how those features will be machined to achieve part is within tolerance when complete

## Slide 5: Determining datums and critical dimensions
  Examine the 3D model to determine the order of operations
  This part could best be machined in the first operation in one of two orientations
  Note that there are tapped hole features that have location dimensions which have been indicated as critical on the print
  Machining this part with the tapped holes in OP1 will ensure that tolerances will be met since those features will be machined at the same time as the other features that can be accessed in this orientation of the setup
Notes: View showing both the top and the bottom of the part at the same time
The print has critical dimensions shown for location of the two tapped holes.
Machining all of the features in one operation as opposed to starting in the orientation without the tapped holes and then flipping the part to add those holes to ensure tolerances are met

## Slide 6: Determining datums and critical dimensions
  Setup for first operation to machine the cylinder
  Note the WCS is located based on the stock and doesn’t match any datum information shown on the print
  There are no critical surfaces to pick up as a starting point on raw stock
  Boundary of part and holes will be machined in this setup
Notes: WCS is placed on the top center of the stock.
All of the material will be roughed and finished around the inner and outer boundary of the part cutting past the bottom model surface followed by the holes being drilled and tapped

## Slide 7: Determining datums and critical dimensions
  Setup for second operation to machine the central bore
  Only one critical datum for this setup (Z)
  Z datum is set off top of parallels
  Machined top face from OP1 seated on ground faces of parallels in OP2
  This operation only removes the excess stock material above the part
  Precise X and Y datum not critical
Notes: This setup only removes the hat of excess material from the top of the part
Z datum is set off of top of parallels before placing the part in the vise ensuring the part will come out to the proper thickness
X and Y locations are not critical as there are no machining operations that will be applied to the part. X and Y could even be set off corner of raw stock hat. However, this requires more steps to locate that point when creating the setup in Fusion 360
Only the hat of material will be removed. The shape of the part was completely cut out in the first setup

## Slide 8: Determining datums and critical dimensions
  Setup for third operation to machine the bores on top face
  WCS set off datums from the print that match the original faces machined from OP1 and OP2
  As part is oriented for different setups, these datums will be followed
Notes: Hole features are machined based on the callout of the print using the datums referenced on the print

## Slide 9: Determining datums and critical dimensions
  Setup for fourth operation to machine the holes on the opposite side
  WCS set off datums from the print that match the original faces machined from OP1 and OP2
  Part is rotated 180 degrees clockwise from OP3
  X datum follows X datum from OP3
Notes: As the part is rotated 180 degrees, note how the X datum is moved to right hand side of the part to match the same X datum that was used for Op3

## Slide 10: Datum theory best practices
  Refer to print or model-based dimensions as a starting point to determine how the part will be machined to meet listed tolerances or critical features
  Once datums have been established on a part, follow and use those datums for following operations
  Each time a part is reoriented to machine a new setup, there is a chance accuracy can be compromised in the new setup
  Machine as many features as possible in a setup to ensure accuracy between features
    Multi-axis machines (4-axis, 5-axis) help with this by machining almost all features in a single setup using the accuracy of the machine instead of the potential error that can be incorporated by creating multiple setups on a 3-axis machine.