## Slide 1: Post Processing

## Slide 2: Learning objectives
After completing this section, you’ll be able to:
Describe post processing.
Explain the theory of G and M codes.

## Slide 3: G and M codes
A CAM program generates toolpaths from part geometry.
Toolpath generation in CAM program is the same regardless of what machine tool the program will be run on.
A CAM program doesn’t know what machine will be used at the time of toolpath generation.
Machine tools run specific controllers that read G and M codes.
G codes primarily tell the machine what type of motion is wanted
  G00: Rapid move
  G01: Linear move
M codes are miscellaneous codes for the controller
  M03: Spindle on clockwise rotation
  M06: Automatic tool change

## Slide 4: Post processing
A CAM program generates CAM toolpaths the same regardless of what machine tool control will be used.
A word processing program doesn’t know what printer the user will want output for. Printer driver is used to convert word processing text to an output the printer can read.
A post processing file is used to convert CAM toolpath to G and M code formatted in the correct way for a machine tool to read.
Post Processing files can be edited to change the order that code is output for the machine tool control.
At the end of a program machine table can be brought to front center of the machine to make it easier for the operator to remove the parts.
Coolant can be programmed to turn on when the tool reaches the feed height plane.

## Slide 5: Post processing
NC output from a CAM program typically generates a much longer NC program when compared to a NC program written by hand.
A CAM program can automate mundane tasks that would be too difficult or tedious to write by hand such as horizontal and vertical lead in/lead out radii or maintaining a constant tool angle engagement for a roughing operation
G and M Code Examples
N60 G41 G00 X1.1 Z1.1 T0303 M08:Enable cutter radius compensation mode, rapid position to 0.55" above axial centerline (1.1" in diameter) and 1.1 in positive from the work offset in Z, activate flood coolant.
N70 G01 Z1.0 F.05:Feed in horizontally at rate of 0.050" per revolution of the spindle until the tool is positioned 1" positive from the work offset.
N120 G00 X1.1 M05 M09: Clear the part, stop the spindle, turn off the coolant.

## Slide 6: NC program examples
Graphical representation of a facing toolpath generated by Autodesk Fusion 360

## Slide 7: NC program comparison
Different machine controllers generate NC programs in different formats.
The format of each program is output in a way that each machine control can properly read the G and M codes.
Two different machines can generate NC programs that are formatted completely different for the same part, but the machined part outcomes will be the same.
Comparison of NC programs for the same part generated from two different controllers