## Slide 1: Theory of tool and work offsets

## Slide 2: Learning objectives
After completing this video, you’ll be able to:
Understand tool length offsets
Understand the relationship of WCS, tool length offsets, and machine coordinates
Learn different methods for locating the WCS

## Slide 3: What are Work/WCS Offsets?
WCS (Work Coordinate Systems) Offsets exist to let the CNC Machine know the location of the G-Code program’s origin
Without WCS Offsets, the machine does not know where the part is within the work envelope of the machine
Why not use G28 as the WCS?
  G28: Return to Home Position. Also known as Machine Reference Point
  G28 is inconsistent from one machine to another, as machines have different work envelopes

## Slide 4: Where to set Work/WCS Offsets?
WCS Offsets can be set anywhere, but best practice is to, whenever possible, set them in a consistent location that does not move/change so that it does not have to be reset from one part to another.
  Raw unmachined surfaces are typically bad WCS reference locations as they change once machined and therefore are no longer referenceable or consistent.
  Workholding features, work stops, and fixturing can provide consistent reference locations for your WCS offsets.

## Slide 5: Why Tool Offsets?
Tool Offsets exist to let the CNC Machine know the cutting location of the Tool Tip (Tool Height Offset), as well as the cutting location of the tool’s edges (Tool Diameter/Radius Offset)
Without Tool Offsets, the machine does not know the length or diameter of the tools it uses to cut parts.
  Most of the time this results in the CNC machine alarming due to programmed movements exceeding the travel limits of the machine.
  In the worst-case scenarios, this can result in tool/part/fixture/machine crashes.

## Slide 6: Where to Set Tool Offsets?
Tool Length Offsets can be set anywhere on the machine, the location of which is called the “Tool Height Offset Reference Location” (THORL)
CRITICAL: All Tool Height Offsets must be set at the EXACT SAME THORL
Best practice is to pick a THORL that is consistent & unchanging from part-to-part, program-to-program, etc.
  Raw unmachined surfaces are typically bad THORL’s as they change once machined and are inconsistent part-to-part.
  When setting manual offsets, the most consistent & accessible location is often the top of the machine table base.
    Rather than touch tool tips off at the top of the machine table, you touch-off on something sitting on top of the table, such as a tool height probe or 1-2-3 block
  When using Tool Height Pre-setting Machines (Zoller, Haas, etc.), the THORL is located at Machine Z0.0

## Slide 7: Tool & Work Offsets Are Related
WCS Z Offset can be defined as the difference between the WCS Z Origin & the THORL (shown in formula below)
  This formula works for all CNC Machines (Mills, Lathes, Millturns, Verticals, Horizontals, etc.)
  This formula also works when setting Tool/WCS offsets either manually or with tool/work probes
WCS Z Offset =
WCS Z Origin – THORL

## Slide 8: Spindle Gauge Line Representation
(G28/G53) Machine Z0
Notes: Image showing where spindle gauge line (machine Z0) is located.
Spindle gauge line locations vary between spindle types (HSK, BT-30, CAT-30, CAT-40, etc.)

## Slide 9: Visual Key
Machine Spindle
Toolholder (BT, CT, HSK, etc.)
Tool (End Mill, Probe, etc.)
Workpiece (Billet, Casting, etc.)
Fixture (Vise, Pallet, etc.)
Machine Table/Base
Machine (G28/G53) Z0, AKA “Gauge Line”
Tool Touch-Off Indicator /
1-2-3 Block
↑ = Z+
↓ = Z-
THORL
WCS Z Origin

## Slide 10: Example A: Top of Workpiece
WCS = G54
WCS Z Origin = Top of Fixture
  Machine Z Position = -10.0”
THORL = Top of Part
  Machine Z Position = -10.0”
Formula:
  WCS Z Offset = (-10.0”) – (-10.0”)
  WCS Z Offset = 10”= 0.0”
Z-10.0
Z-10.0
G28 Z0
↑ = Z+
↓ = Z-

## Slide 11: Example B: Top of Fixture
WCS = G54
WCS Z Origin = Top of Fixture
  Machine Z Position = -13.0”
THORL = Top of Part
  Machine Z Position = -10.0”
Formula:
  WCS Z Offset = (-13.0”) – (-10.0”)
  G54 Z Offset = 7” = -3.0”
Z-10.0
Z-13.0
G28 Z0
↑ = Z+
↓ = Z-

## Slide 12: Example C: THORL on Touch-Off Block/Indicator
WCS = G54
WCS Z Origin = Top of Fixture
  Machine Z Position = -13.0”
THORL = Top of Block/Indicator
  Machine Z Position = -15.5”
Formula:
  WCS Z Offset = (-13.0”) – (-15.5”)
  G54 Z Offset = 2.5””
G28 Z0
Z-15.5
Z-13.0
↑ = Z+
↓ = Z-

## Slide 13: Example D: THORL on Machine table top
WCS = G54
WCS Z Origin = Top of Fixture
  Machine Z Position = -13.0”
THORL = Machine table top
  Machine Z Position = -17.5”
Formula:
  WCS Z Offset = (-13.0”) – (-17.5”)
  G54 Z Offset = 4.5”
G28 Z0
Z-17.5
Z-13.0
↑ = Z+
↓ = Z-

## Slide 14: Tool Presetters
Tool Presetters Measure Tool Offsets outside the machine reducing machine downtime.
To measure Tool Height Offsets, Presetters replicate a machine spindle taper in order to measure the “True” Tool Length/Height from the Gauge Line.
The resulting Tool Height Offset value ends up being a positive value.
https://www.haascnc.com/haas-tooling/tool_management/tool_presetting_mach/08-1200.html

## Slide 15: Example E: Tool Height Presetter
The tool and holder are inserted in the presetter with the tooling pointing up
THORL = Distance from Gauge Line (G28 Z0) to Tool Tip
  Tool Height Offset = 6.25”
G28 Z0
↑ = Z+
↓ = Z-
Z6.25