## Slide 1: Types of 2D toolpaths

## Slide 2: Toolpath types
Face: Finish the top face of a part.
2D Pocket: Rough and finish open and closed pockets with an offset strategy.
2D Adaptive Clearing: Rough parts with a consistent chip load/constant cutter engagement strategy.
2D Contour: Rough and Finish selected chains/edges of a part.
Drill: Spot, drill, and tap blind and through holes in a part.

## Slide 3: Face
Facing removes all material from the top of stock to the top of part for a finished machined face.
Can be done with large endmills or specific shell mills and face mills.
Will use the stock definition or selected area.
No tool containment options. All toolpaths will enter/exit from outside of stock or selection.

## Slide 4: 2D Pocket
Creates a roughing operation that uses toolpaths parallel to selected geometry.
Can be used on open or closed pockets at multiple depths in the same operation.
Great option to finish the floor and sides of pockets where material has been left from roughing operations.
Poor option for deep pockets or geometry with multiple tight corners. Tool loads will not be consistent.

## Slide 5: 2D Adaptive Clearing
Creates a roughing operation that uses a consistent chip load/constant engagement angle.
Can be used on open or closed pockets at multiple depths in the same operation.
Great option for deep and complex pockets. Tools can generally cut their full flute depth at higher feedrates as compared to a 2D Pocket toolpath.
Poor option for finishing walls and floors. Should be used as a roughing operation only.

## Slide 6: 2D Contour
Creates a toolpath based on selected 2D contours.
Can be used on open/closed pockets or open/closed chains/contours at multiple depths in the same operation, but each selection must be in 2D/flat relatives to the XY plane.
Has options for roughing, finishing, multiple depths, ramps and leads and can use stock contours to reduce non-cutting feed motions.
Great option for finishing walls and profiles of parts.
Poor options for roughing and mass material removal.

## Slide 7: Drill/Tap
Creates a toolpath based on selected points, hole faces, or diameter ranges.
Commonly used to spot drill, drill, and tap holes.
Offers multiple cycle types such as pecking and dwelling to aid in chip removal and hole clearing.
Offers drilling specific options such as “drill tip through bottom” when specifying heights.
Can be used on counter-sunk and counter-bore holes and will merge hole segments to calculate drill depth.

## Slide 8: Additional Toolpaths
Thread: Creates spiraling helical cuts for milling threads.
Bore: Creates a spiraling helical cut that maintains tool contact with selection.
Circular: Creates circular cuts at multiple heights on selected faces with included lead-in/lead-out movements.
Engrave: Creates a cut along a selected path using a V shaped tool.
2D Chamfer: Creates cuts along edges with a V shaped tool. Note: 2D Chamfer offers collision avoidance with part features.
Slot: Mills a slot following a centerline path.
3D Adaptive Clearing: 3D Adaptive motion roughing toolpath that is model aware and can quickly remove material from simple or complex parts.

## Slide 9: Common Workflow
When programming most parts there will be a common workflow and set of toolpaths used. This is going to vary based on part geometry, but in general you will notice the following:
  Face: Remove the rough stock from the top of the part down to the highest machined face using a large face mill.
  2D Adaptive: Rough the entire part with the largest endmill. Use semi-roughing passes with smaller tools as needed leaving a small amount of material to be finished.
  2D Pocket: Finish cut walls and floors of pockets at the same time removing the small amount of material left from roughing.
  2D Contour: Finish edges of geometry with a finish or multiple finish passes as required.
  Drill: Spot, drill, and tap holes as required.
  2D Chamfer: Deburr sharp edges of part with a small chamfer as specified in the design or detailed drawing.