## Slide 1
Step-by-step guide
Create a digital twin
Create a digital twin to ensure that you can cut a physical part without colliding into other objects.
Learning objectives:
Create a stock body.
Import and locate workholding.
The completed exercise

## Slide 2
1. Open a new Untitled tab in Fusion. Expand the Data Panel and use the New Folder button to create a folder structure for this course. For the purposes of this documentation, a main folder named 25 Learn Fusion CAM in 90 was created. Then an Imperial subfolder was created and a 1
- Setup subfolder was created inside that.
Upload the two supplied files shown in the image on the right into your folder structure. These two supplied files will be used to help create a digital twin. This digital twin will help clarify where the tool can machine without colliding into any other objects.
Figure 1. Create the course’s folder structure and
upload files

## Slide 3
2. Inside the Data Panel, double-click the Cell Phone Stand - Inch Assembly.f3d file to open it in the Canvas area. This is a two-piece cell phone holder.
Figure 2. Open the supplied file
3. Click Hide Data Panel to close the Data Panel.
Figure 3. Hide the Data Panel

## Slide 4
4. Sometimes it makes sense to move individual components into separate files before creating machining operations. You can use the Derive tool to make a copy that is linked back to the original file. Expand the Bodies folder and select the Main Body.
Figure 4. Select the Main Body
5. With the Main Body selected, click Create> Derive.
Figure 5. Open the Derive tool

## Slide 5
6. In the Derive dialog, make sure the Place Objects at Origin option is checked, then OK the dialog.
Figure 6. OK the dialog
7. The Main Body is copied into a new Untitled tab. The Browser’s arrow icon indicates that this part is derived from an external file. If the original external design is modified, those changes will automatically cascade to this derived design.
Figure 7. Note the Derive icon

## Slide 6
8. In the Browser, click the Origin’s eyeball icon to make it visible in the Canvas area.
Figure 8. Show the origin
9. Note the part is not ideally oriented for machining.
Figure 9. Note the part’s orientation

## Slide 7
10. Since the part is a body and not a component, the Align tool should be used. Click Modify> Align.
Figure 10. Open the Align tool

## Slide 8
11. In the Align dialog, choose the Bodies option from the Object menu.
Figure 11. Choose the Bodies option
12. For the dialog’s From selection, choose the large hole’s center point. You can select this point by clicking the edge shown in the image on right.
Figure 12. Select the hole’s center point

## Slide 9
13. For the dialog’s To selection, choose the origin’s center point. Make sure the origin’s small white icon lies flat on the XY plane.
Figure 13. Select the origin
14. The part will snap into place after making the dialog’s To selection. OK the Align dialog after you’re satisfied.
Figure 14. Inspect the result

## Slide 10
15. Notice the Align feature is added to the timeline.
Figure 15. Note the feature added to the timeline
16. Dragging the timeline marker backwards will revert the part to its original position.
Figure 16. Note how to revert the part’s position
17. You can create a custom body to represent the stock material that will be machined. Select the part’s bottom face shown in the image on the right.
Figure 17. Select the face

## Slide 11
18. Click Create> Create Sketch.
Figure 18. Create a new sketch
19. Double-click the edge shown in the image on the right to select the entire edge loop.
Figure 19. Select the edge loop

## Slide 12
20. Convert the selected edge loop into construction geometry by choosing the dialog’s Construction option. Repeat this process to convert all of the existing sketch geometry into construction geometry.
Figure 20. Convert to construction geometry
21. Open the Rectangle tool by clicking Create> 2-Point Rectangle.
Figure 21. Open the Rectangle tool

## Slide 13
22. Choose the dialog’s Center Rectangle
option.
Figure 22. Choose the Center Rectangle option
23. Click the origin to place the rectangle’s center point at the sketch’s origin, then click again to create a rectangle larger than the part.
Figure 23. Draw a rectangle

## Slide 14
24. Open the Sketch Dimension tool by clicking Create> Sketch Dimension.
Figure 24. Open the Sketch Dimension tool
25. Click the rectangle’s top edge to apply a dimension to it. Enter 4in into the dimension box and press Enter.
Figure 25. Dimension the top edge

## Slide 15
26. Add a dimension of 4.125 in to the
rectangle’s vertical edge.
Figure 26. Dimension the vertical edge
27. Finish the current sketch by clicking Finish Sketch> Finish Sketch.
Figure 27. Finish the sketch

## Slide 16
28. Open the Extrude tool by clicking Create> Extrude.
Figure 28. Open the Extrude tool
29. Select the rectangle you drew and pull the on-screen manipulator up -0.25 in.
Figure 29. Extrude the rectangle

## Slide 17
30. Choose the New Body option from the Operation menu. OK the dialog
Figure 30. Change the operation type
31. You can organize your project by renaming the Browser’s bodies. Click Body2 and rename it as Stock.
Figure 31. Rename the new body

## Slide 18
32. You can adjust the Stock’s opacity so you can see the underlying original model. In the Browser, right-click the Stock body and choose Opacity Control> 30%.
Figure 32. Adjust the stock’s opacity
33. You can now see the original model through the stock body.
Figure 33. Inspect the result

## Slide 19
34. Open the Data Panel and locate the supplied Vise.f3d project.
Figure 34. Locate the supplied file

## Slide 20
35. Click and drag the Vise.f3d project into the Canvas area.
Figure 35. Click and drag the vise

## Slide 21
36. Use the on-screen manipulator’s arrow to drag the vise below the Stock body.
Figure 36. Move the vise

## Slide 22
37. Use the on-screen manipulator’s rotation handle to rotate the vise -90 degrees.
Figure 37. Rotate the vise
38. Deactivate the dialog’s Ground to Parent option, then OK the dialog.
Figure 38. OK the dialog

## Slide 23
39. Open the Align tool by clicking Modify> Align.
Figure 39. Open the Align tool
40. Choose the dialog’s Components
option from the Object menu.
Figure 40. Change the object type

## Slide 24
41. Being careful to avoid any of the small white square icons, select the vise’s face as shown in the image on the right. You might need to zoom in to the vise to make sure you are not selecting the parallel’s face.
Figure 41. Select the face

## Slide 25
42. For the dialog’s To selection, choose the stock body’s face that will contact the vise face you selected in the previous step.
Figure 42. Select the stock’s face

## Slide 26
43. Notice the vise moves into the correct position. OK the dialog.
Figure 43. Inspect the progress
44. Right-click in an open area of the canvas and choose the Repeat Align option from the right-click menu.
Figure 44. Reopen the Align tool

## Slide 27
45. Use the Align tool to make sure the stock body’s bottom face is aligned with the parallel’s top face. OK the dialog.
Figure 45. Continue to align the vise to the stock
46. Repeat the Align tool to align the stock’s left face with the vise’s left face. OK the dialog.
Figure 46. Align the stock to the left

## Slide 28
47. Select the vise jaw’s top face shown in
the image on right.
Figure 47. Select the jaw’s face
48. In the Browser, expand the Vise component and notice that one of the components is highlighted with a dashed underline.
Figure 48. Inspect the Browser

## Slide 29
49. Right-click the highlighted component
and choose the menu’s Pin option.
Figure 49. Pin the selected component
50. Click the dialog’s Capture Position
option.
Figure 50. Capture the component’s position
51. The vise will stay stationary but the component’s joints are allowed to move. Click and drag the sliding vise jaw and notice that it can move.
Figure 51. Move the vise jaw

## Slide 30
52. Click Position> Revert.
Figure 52. Revert the component’s position
53. Open the Align tool and align the
sliding jaw’s face to the stock.
Figure 53. Align the sliding jaw

## Slide 31
54. Activate the Align dialog’s Capture
Position option, then OK the dialog.
Figure 54. OK the dialog
55. Now that the digital twin is complete, you can ensure that tools will not collide with other objects during the machining process.
Figure 55. Inspect the result

## Slide 32
56. Save the design by clicking Save in the Application Bar.
Figure 56. Click Save