## Slide 1
Step-by-step guide
Create a Setup Sheet
Collect all of a job’s information into a convenient Setup Sheet so the machine operator understands the job’s parameters.
Learning objectives:
Create a Setup Sheet.
The completed exercise

## Slide 2
1. Continue with the file from the previous video or open the supplied Cell Phone INCH – Simulate.f3z file.
Figure 1. Open the file
2. A Setup Sheet can be created so that a machine operator correctly prepares for the job. Select the NC Programs folder’s Setup Stand, right-click it, then choose Setup Sheet from the menu.
Figure 2. Create a Setup Sheet

## Slide 3
3. Choose the sheet’s name and save
location.
Figure 3. Name the setup sheet
4. Click the dialog’s Save.
Figure 4. Click Save

## Slide 4
5. By default, the sheet opens in the Detailed configuration. This Detailed configuration does not omit any information. You can use the menu at the sheet’s top to customize the types of information that the sheet displays.
Figure 5. Configure the sheet’s information
6. The Summary section displays the number of operations, the tools, the maximum spindle speed, the estimated cycle time, and more.
Figure 6. Inspect the Summary section

## Slide 5
7. The Tools section describes each tool in detail. For example, you can learn about the diameter, number of flutes, vendor, estimated cycle time, holder information, and much more.
Figure 7. Inspect the Tools section
8. The Setup section describes the setup and the stock. You can learn about the WCS location, the stock’s dimensions, and more.
Figure 8. Inspect the Setup section

## Slide 6
9. The Operations section gives a detailed description of each operation. You can learn the operation’s name, operation type, maximum spindle speed, the required tool, the coolant setting, and more.
Figure 9. Inspect the Operations section
10. The printer icon in the sheet’s top right corner allows you to save the sheet as a PDF or print a physical copy. It is important to note that these setup sheets can be accessed by anyone that has access to your project; this allows you to easily share the information with other users.
Figure 10. Note how to print the sheet

## Slide 7
11. The Configuration drop-down menu at the top of the sheet can be used to customize the sheet’s information. After you finish exploring the setup sheet, click the X icon in the top right corner. The Setup Sheet was saved when you created it and does not need to be saved again.