## Slide 1: Tool holders and work holding

## Slide 2: Learning objectives
After completing this lecture, you’ll be able to:
Identify different tool holding options
Identify different types of work holding options
Understand the pros and cons of different work holding options

## Slide 3
Standard solid body cutting tool holder are used in various machining operations. This toolholder incorporates a set screw to prevent cutting tool pull out.
  Pros
    Economical
    Rigid
    Durable
Cons
Made for one size tool, multiples needed
Runout can be excessive shortening tool life
Most are not balanced, spindle speed limited
Standard solid body cutting tool holder

## Slide 4
Projected solid body cutting tool holder used in various machining operations where reach or tool holder interference is a concern. This toolholder incorporates a set screw to prevent cutting tool pull out.
Pros
Economical
Durable
Increased rigidity and accuracy
Cons
Made for one size tool, multiples needed
Runout can be excessive shortening tool life
Most are not balanced, spindle speed limited
Difficult to cool, shortening tool life
Projected solid body cutting tool holder

## Slide 5
ER Collet chucks: ER Collet chucks are used in various machining operations and offer great versatility holding tools of various sizes by means of a collet.
Pros
Economical
Collets are cheaper than toolholders
Better run out than solid body
High cylindrical clamping force
Cons
Requires operator training to use properly
Tool can slip in the collet
ER collet chucks

## Slide 6
Project shrink fit tool: Projected shrink fit tool holders are used in high volume and highly accurate machining operations. The tool holders also excel where reach or tool holder interference is a concern. This toolholder incorporates the principal of thermal expansion to hold the cutting tool in the bore.
Pros:
Highly accurate, less than .0001 runout
Rigid
Small nose diameter
Balanced for high RPM’s
Cons:
Made for one size tool, multiples needed
Tool holder cost
Requires adding a special machine to heat and cool the holder for tool installation
Shrinking machines: Power Clamp Comfort NG i4.0 - HAIMER (haimer-usa.com)
Projected shrink fit tool holders

## Slide 7
Keyless drill chucks: Keyless drill chucks are used in drilling operations. This tool holder incorporates a set of jaws that are adjusted by hand to close and grip the shank of the cutting tool.
Pros
Economical
Adjustable to grip size within the range
Cons
Runout can be excessive shortening tool life
Not recommended for carbide tool shanks
This tool holder is not to be used as an end mill holder. Lateral cutting forces should never be applied to this holder.
Keyless drill chucks

## Slide 8
Milling chucks are used in various milling operations. This tool holder uses collets and a specially designed collet nut to provide high clamping forces.
Pros:
Economical
Collets designed for superior clamping force over ER collets
Cons:
Tool holder has a higher projection length which can reduce Z travel
Milling chucks

## Slide 9
Hydraulic chucks: Hydraulic chucks are used in are used in high volume and highly accurate machining operations. This tool holder uses hydraulic fluid compressed via a set screw to provide high cylindrical clamping forces.
Pros
Superior clamping force over ER collets and solid body holders
Balanced
Reduced runout less than .0001 in optimal conditions
Cons
Holders are specifically sized with no range
Price
CAT40 Hydraulic Holders - metal milling - Techniks CNC Machine Tooling (techniksusa.com)
Hydraulic chucks

## Slide 10
Value Collection - 20 Piece, 6 Inch Long x 1/8 Inch Thick, Alloy Steel
Thin Parallel Set – 06820898 - MSC Industrial Supply (mscdirect.com)
Most of the jobs on a mill can be held in a vise.
There are many different types depending on
the exact need, but most will require the
use of parallels, soft jaws, or other work
holding device.
Work holding

## Slide 11
Traditional single station fixed jaw vise: Rear jaw is stationary while the front jaw opens and closes to grip work piece.
Pros
WCS can be located on fixed jaw to allow for running of different jobs without having to reset WCS
Cons
Not as useful for multi-axis work
Requires more than one vise for one piece flow operations to complete Op2
Traditional single station fixed jaw vise

## Slide 12
Dual station vise: This vise allows for a work piece to be held in each
Pros
Allows for multiple ops to be completed in a single cycle.
Good for production runs
Cons
Not as useful for multi-axis work
WCS needs to be set for each new job run in the vise for different size stock
Dual station vise.

## Slide 13
Self centering vise: Both jaws open and close equal amount when screw is rotated
Pros
Useful for multi-axis work
Often used in combination with other workholding items like pyramids and tombstones
Cons
Higher price
Both jaws move to grip stock making it difficult to set WCS on jaws for different jobs
WCS typically located on a ”Zero” point so work holding needs to be used in CAM digital twin to accurately set a WCS
Self centering vise

## Slide 14
Creative solutions to hold your work piece
Talongrip™ Long Length Serrated Grip This grip is used for holding on to minimal amounts of material allowing for heavy metal removal rates
Heavy-Duty VersaGrip™
This grip offers another method for griping edges of a work piece to secure in a non-traditional method.
All images sourced from Products | Mitee-Bite Products LLC. (miteebite.com)
Modular XYZ Xpansion® Pins
These pins can be used to accurately locate the bores of parts or fixtures for quick and accurate locating.
In most instances when planning a job, Setup 1 is usually the simplest because it comes out of traditionally round or flat stock. The complication begins as you move into Setup 2 and sometimes Setups 3 and 4. The industry is constantly evolving to help provide economical turnkey solutions such as the ones below.

## Slide 15
Sometimes it makes sense to use multiple vises to hold a longer work piece. In this photo we are using 2 Kurt vises with Mitee-bite Talon Grip Jaws to hold on to longer stock.
Mechanical Technology: Milling Machine Work Holding Devices (4mechtech.blogspot.com)
In some situations, you may not have any flat edges to grip or clamp on. Thinking outside the box and using strap clamps can take a job from problem to completed.