## Slide 1
Step-by-step guide
Copy and paste tools
Populate a tool library by copying, pasting, and modifying existing tools.
Learning objectives:
Use the tool library filter.
Copy and paste a tool from the Sample Library.
Edit a tool.
The completed exercise

## Slide 2
1. Open a new Untitled design and navigate to the Manufacture workspace. Open the Tool Library dialog by clicking Manage> Tool Library. | Figure 1. Open the Tool Library dialog
2. Click the Learn CAM Sample – MM library to open it. | Figure 2. Open the tool library
3. A common practice for populating tool libraries is to copy and paste existing tools. These can come from either the Fusion Library or Vendor tool libraries. The Fusion Library’s tools are preloaded with general feeds and speeds, cutting presets, and more. | Figure 3. Explore the Fusion Library

## Slide 3
4. Tools in the Vendor library are organized by manufacturer and are configured to precisely match existing tools. | Figure 4. Explore the Vendor libraries

## Slide 4
5. You can filter the visible tools by using the options in the dialog’s Filters tab. For example, activate the Milling option in the Tool category section, then activate the Flat endmill option in the Type section. | Figure 5. Filter the results

## Slide 5
6. Open a tool library and notice that the visible tools match these filter criteria. | Figure 6. Open a tool library
7. Select one of the library’s tools. | Figure 7. Select a tool

## Slide 6
8. Notice that the Cutting data section has customized feeds and speeds for various materials. | Figure 8. Inspect the Cutting data section
9. Activate the Fusion Library and notice the filters are still active. | Figure 9. Navigate to the Fusion Library

## Slide 7
10. In the Filters tab, activate the Inches option in the Unit section. Choose the Range option from the Diameter section’s drop-down menu, then enter a range of 6 mm to 25 mm. Alternately, you could enter the range using inch values by entering 0.25 in to 1 in. | Figure 10. Continue to filter the tools
11. To copy an existing tool, right-click it and choose Copy tool from the menu. Locate and copy the ¼” Flat Endmill. | Figure 11. Copy the tool

## Slide 8
12. Navigate to the Learn CAM Sample- MM tool library, right-click in an open section, then choose Paste tool from the menu. | Figure 12. Paste the copied tool
13. Copying and pasting a tool does not clear the active filters. Clear all the active filters by clicking each section’s X icon. | Figure 13. Clear the filters

## Slide 9
14. After clearing the active filters, all of the tool library’s tools will be visible. In this case, there is only a single tool so no additional tools are visible. | Figure 14. Inspect the tool library
15. To edit the library’s tool, right-click it and choose Edit tool from the menu. | Figure 15. Edit the tool

## Slide 10
16. Navigate to the dialog’s Cutter tab and notice that you can customize the tool’s parameters. For example, you could increase the number of flutes to 4 and change the tool’s material to Carbide. It is always important to remember that every tool in the digital tool library needs to precisely match a physical tool in your tool chest; this will help create successful toolpaths. | Figure 16. Customize the tool’s parameters
17. Navigate to the dialog’s Cutting data tab and choose the Aluminum – Slotting preset. | Figure 17. Choose the cutting preset

## Slide 11
18. The 12,000 RPM Spindle speed value might be well above a machine’s capabilities. You can modify this value, but it is important to understand your specific machine’s capabilities. | Figure 18. Note ways to customize the preset
19. Continue to the Post processor tab and enter 1 into the Number box. This identifies that the current tool is in the tool changer’s number 1 slot. Click the dialog’s Accept. | Figure 19. Change the tool’s number

## Slide 12
20. Navigate to the Fusion Library> Milling Tools (Metric) tool library and open it. Locate the 6mm Flat Endmill tool, right-click it, then choose Copy tool from the menu. | Figure 20. Copy the 6 mm tool
21. Navigate back to the Learn CAM Sample – MM tool library, right-click in an open section, then choose Paste tool from the menu. Notice that the tool library can simultaneously have both metric and standard tools. | Figure 21. Paste the 6 mm tool

## Slide 13
22. Right-click the new tool and choose Edit tool from the menu. | Figure 22. Edit the 6 mm tool
23. Navigate to the Post processor tab, enter 2 into the Number box, then click the dialog’s Accept. | Figure 23. Change the tool’s number

## Slide 14
24. Inspect the library’s tools and note their tool changer slots. The Imperial tool is in the 1 slot and the metric tool is in the 2 slot. | Figure 24. Inspect the tool library
25. Close the Tool Library dialog by clicking Close. The tools are automatically saved when you close the dialog. | Figure 25. Close the dialog