## Slide 1
Step-by-step guide
Create a custom tool
Populate a digital tool library by creating a custom tool from scratch.
Learning objectives:
Create a new milling tool.
Edit tool parameters.
Create cutting presets.
The completed exercise

## Slide 2
1. Open a new Untitled design and navigate to the Manufacture workspace. Open the Tool Library dialog by clicking Manage> Tool Library. | Figure 1. Open the Tool Library dialog
2. Navigate to and open the Learn CAM Sample – MM tool library you created in a previous module. | Figure 2. Open the tool library
3. In the previous module, you copied and pasted two existing tools into this tool library. However, you can also create new tools from scratch. Click the plus icon to create a new tool. | Figure 3. Create a new tool

## Slide 3
4. Select the Flat end mill option in the dialog’s Milling section. | Figure 4. Select the tool type
5. In the dialog’s General tab, enter 10 mm Flat Endmill into the Description box. Because the details need to match a specific physical tool, make sure you enter the appropriate vendor, product ID, and product link information. | Figure 5. Customize the general information

## Slide 4
6. Continue to the Cutter tab and enter 10 mm into the Diameter box. Press Enter. Notice that the Shaft diameter value automatically updates to match the Diameter value because it is driven by an equation. The FX icon in the Shaft diameter box indicates that this value is driven by an equation until you override it. Continue to customize the information in the Cutter tab so that the digital tool matches a physical tool. | Figure 6. Customize the tool’s geometry
7. Continue to the Holder tab, then locate the CT40 – 0.250 x 1.38 End Mill Holder in the left column. Click the holder to highlight it. | Figure 7. Choose a holder

## Slide 5
8. Click Select holder to add it to the tool. If you want to extract the holder and save it to your tool library, you can click Extract holder. | Figure 8. Click Select holder

## Slide 6
9. Continue to the Cutting data tab and notice that you can create cutting presets. Click the plus icon to create a new preset. | Figure 9. Click the plus icon
10. Name the new preset as AL Rough to indicate that it will be used to rough aluminum. | Figure 10. Name the preset

## Slide 7
11. Enter 8000 RPM into the Spindle speed box and notice that several other parameters automatically update because they are driven by equations that include the Spindle speed value. | Figure 11. Enter the Spindle speed value
12. Enter 1200 mm/min into the Cutting feedrate box and notice the other values that automatically update. | Figure 12. Adjust the Cutting feedrate value

## Slide 8
13. You can manually override an equation by typing a value into the box. In the image on the right, the Lead-in feedrate was reduced from 1200 to 1000. After you press Enter, the fx icon disappears to indicate that it is not driven by an equation anymore. | Figure 13. Modify an equation-driven value
14. Continue to the Post processor tab and notice that the tool is automatically given the tool changer’s next available slot number. In this case, this new tool is added to slot number 3. | Figure 14. Verify the tool’s number

## Slide 9
15. Click the dialog’s Accept. | Figure 15. Click Accept
16. Notice the tool you created is added to the tool library. If you extracted any tool holders in Step 8, these will also be displayed inside the tool library. | Figure 16. Inspect the tool library
17. The tool library is automatically saved to the Cloud. Close the Tool Library dialog. | Figure 17. Close the dialog