## Slide 1
Step-by-step guide
Use roughing toolpaths to remove material
Compare a couple of different methods for roughing out a part’s geometry.
Learning objectives:
Create a 2D Adaptive toolpath.
Create a 2D Pocket toolpath.
The completed exercise

## Slide 2
1. Continue with the file from the previous module or upload the supplied Cell Phone Metric – Rough.f3d file. In the supplied file, the links to the external parent files are broken. It is better to use your own file if possible. | Figure 1. Open the file
2. Now that the stock has been faced, the part’s pocket geometry needs to be roughed out. Two common options are the 2D Adaptive Clearing and 2D Pocket operations. The 2D Adaptive Clearing operation is a roughing-only operation but the 2D Pocket could be used to rough or finish. Click 2D> 2D Adaptive Clearing. | Figure 2. Create a 2D Adaptive Clearing operation

## Slide 3
3. Make sure the 12 mm flat endmill tool is selected for this operation. If this tool is not selected, click Select and navigate to the Learn CAM 90 – Metric tool library and select Tool 7. | Figure 3. Select the correct tool for the operation
4. Continue to the dialog’s Geometry tab and select the face shown in the image on the right. The blue area indicates that the operation is trying to cut inside the selection; this is correct. If you need to machine outside the selection, you could flip the operation by clicking the red arrow. Also note that the blue area does not pass over the large hole, which means the operation might try to avoid this feature. | Figure 4. Select the face

## Slide 4
5. Explore the 2D Adaptive dialog’s other tabs, then click OK to accept all the default options. | Figure 5. OK the dialog
6. Inspect the toolpath preview and note that the large hole was not completely avoided. However, there is a small amount of material remaining in that area. This adaptive clearing operation optimizes the toolpath to maintain a consistent cutting load. | Figure 6. Inspect the toolpath preview

## Slide 5
7. Right-click the 2D Adaptive operation and choose Edit from the menu. | Figure 7. Edit the operation
8. Clear the current selection by clicking the X. | Figure 8. Clear the selection

## Slide 6
9. Select the edge shown in the image on the right and notice the blue area includes the large hole. OK the 2D Adaptive dialog. | Figure 9. Select the edge
10. Inspect the toolpath preview and notice that the pocket is correctly roughed. Selecting the pocket’s edge was the better choice in this instance but might not be the correct choice in every situation. | Figure 10. Inspect the toolpath preview

## Slide 7
11. Create a 2D Pocket operation by clicking 2D> 2D Pocket. | Figure 11. Create a 2D Pocket operation
12. Click the dialog’s Select to choose an appropriate tool for the operation. | Figure 12. Click Select

## Slide 8
13. Navigate to the Learn CAM 90 – Metric tool library and select Tool 6. Click the Select Tool dialog’s Select. | Figure 13. Select the tool
14. Navigate to the dialog’s Geometry tab and select the edge shown in the image on right. | Figure 14. Select the edge

## Slide 9
15. Continue to the Heights tab and enter -2 mm into the Bottom Height section’s Offset box. This will make sure the pocket passes all the way through the part by cutting 2mm below the selected contour. | Figure 15. Adjust the Bottom Height
16. Continue to the Passes tab and notice that the Stock to Leave option is activated. OK the dialog. | Figure 16. OK the dialog

## Slide 10
17. Inspect the toolpath preview and notice how the operation ramps down to the final cutting depth. This toolpath uses a different strategy than the 2D Adaptive toolpath. The 2D Adaptive toolpath is the better choice when you need to maintain a consistent tool load and use a faster feedrate. | Figure 17. Inspect the toolpath preview
18. Viewing the stock from the side makes it easier to see how deeply the operation machines. The final cutting depth is easily below the model’s bottom face. | Figure 18. Note the operation’s cutting depth

## Slide 11
19. Right-click the 2D Pocket operation, then choose Suppress from the menu. Click the dialog’s Yes to suppress the operation. | Figure 19. Suppress the 2D Pocket operation
20. A new operation needs to be created to replace the suppressed 2D Pocket operation. Click 2D> 2D Adaptive Clearing. | Figure 20. Create a 2D Adaptive Clearing operation

## Slide 12
21. Navigate to the Geometry tab and select the edge shown in the image on right. | Figure 21. Select the edge
22. Continue to the Heights tab and enter -2 mm into the Bottom Height section’s Offset box. | Figure 22. Adjust the bottom height

## Slide 13
23. Continue to the Passes tab and activate the Use Slot Clearing option. OK the dialog to generate the toolpath. | Figure 23. Activate the Use Slot Clearing option
24. The toolpath is not generated, and an orange warning icon is shown next to the operation. The toolpath cannot be generated using the operation’s current settings. | Figure 24. Note the warning

## Slide 14
25. Edit the new 2D Adaptive operation by right-clicking it and choosing Edit from the menu. Navigate to the Passes tab and deactivate the Use Slot Clearing option. OK the dialog. | Figure 25. Deactivate the Use Slot Clearing option
26. Notice that the toolpath issue is not resolved and the tool is too large to use an adaptive motion to cut the geometry. | Figure 26. Inspect the result

## Slide 15
27. Right-click the new 2D Adaptive operation and select Delete from the menu. | Figure 27. Delete the operation
28. Unsuppress the 2D Pocket operation by right-clicking it and toggling off the menu’s Suppress option. Note that the orange icon indicates the operation needs to be regenerated. | Figure 28. Unsuppress the 2D Pocket operation

## Slide 16
29. Select the 2D Pocket operation, then click Actions> Generate. | Figure 29. Regenerate the operation
30. The orange icon is replaced by a green checkmark after the operation is regenerated. Save the file. | Figure 30. Inspect the Browser