## Slide 1
Step-by-step guide
Use finishing toolpaths to finalize a model
Create and customize several toolpaths to cut a part’s geometry.
Learning objectives:
Create a 2D Pocket Finishing toolpath.
Create a 2D Bore toolpath.
Create tapped holes.
Create a 2D Contour toolpath with tabs.
The completed exercise

## Slide 2
1. Continue with the file from the previous module or upload the supplied Cell Phone Metric – Finish.f3d file. It is important to note that the supplied file will not have active links to the external parent files, so use your own file if possible. | Figure 1. Open the file
2. A Bore operation can be used to cut the large pocket’s hole. Click 2D> Bore. | Figure 2. Create a Bore operation

## Slide 3
3. Verify that the operation is using the 6mm flat endmill. If this tool is not displayed in the dialog, click Select. Navigate to the Learn CAM 90 – Metric tool library and select Tool 6. | Figure 3. Select the operation’s tool
4. Continue to the Bore dialog’s Geometry tab and select the face shown in the image on right as the dialog’s Circular Face Selection. | Figure 4. Select the face

## Slide 4
5. Continue to the Heights tab and enter -2 mm into the Bottom Height section’s Offset box. OK the dialog. | Figure 5. Adjust the bottom height
6. Inspect the toolpath and notice that a small chunk of material is left in the center. This could be a problem because it could be thrown through the machine. | Figure 6. Inspect the toolpath

## Slide 5
7. The existing 2D Pocket operation could be adjusted to eliminate the problem you noted in the previous step. Right-click the 2D Pocket operation and choose Edit from the menu. | Figure 7. Edit the 2D Pocket operation
8. Navigate to the Geometry tab and select the bottom edge shown in the image on right. This edge will be added to the current pocket selection. OK the dialog. | Figure 8. Add to the pocket selection

## Slide 6
9. Inspect the toolpath and notice that the 2D Pocket operation now cuts both holes. | Figure 9. Inspect the toolpath
10. In the Browser, select the Bore operation and notice that the tweaks to the 2D Pocket operation have resolved the issue that you noticed in Step 6. | Figure 10. Inspect the updated Bore operation

## Slide 7
11. Create a new 2D Pocket operation by clicking 2D> 2D Pocket. | Figure 11. Create a new 2D Pocket operation
12. Navigate to the 2D Pocket dialog’s Geometry tab and select the edge shown in the image on the right. | Figure 12. Select the edge

## Slide 8
13. Continue to the Passes tab and activate the Finishing Passes option. Deactivate the Stock to Leave option, then OK the dialog. | Figure 13. Configure the Passes tab

## Slide 9
14. Inspect the toolpath and notice that the final pass removes the last 0.6 mm of material because of the Finishing Passes option. | Figure 14. Inspect the toolpath
15. Create a new 2D Pocket operation by clicking 2D> 2D Pocket. Navigate to the Geometry tab and select the edge shown in the image on the right. | Figure 15. Create a new 2D Pocket operation

## Slide 10
16. Continue to the Heights tab and enter -2 mm into the Bottom Height section’s Offset box. | Figure 16. Adjust the bottom height
17. Continue to the Passes tab and deactivate the Stock to Leave option. OK the dialog to generate the toolpath. | Figure 17. Deactivate the Stock to Leave option

## Slide 11
18. Inspect the toolpath to make sure the geometry is correctly cut. A chamfer feature is needed to finish the pocket and the slot; this chamfer will be covered in a different module. | Figure 18. Inspect the toolpath
19. To begin creating the model’s tapped holes, create a Drill operation. Click Drilling> Drill. | Figure 19. Create a Drill operation

## Slide 12
20. Click the dialog’s Select to choose an appropriate tool for the operation, then navigate to the Learn CAM 90 – Metric tool library. Select Tool 1 which is a 5 mm Spot Drill. Click the Select Tool dialog’s Select. | Figure 20. Select the operation’s tool
21. Navigate to the Drill dialog’s Geometry tab and select the five hole faces shown in the image on the right. | Figure 21. Select the hole faces

## Slide 13
22. Continue to the Passes tab and notice that the spot drill is trying to plunge too far. This operation is supposed to only dimple the surface. | Figure 22. Notice the preview
23. In the Bottom Height section, select the Hole top option in the From menu. Enter -1mm into the Offset box, then OK dialog. | Figure 23. Adjust the bottom height

## Slide 14
24. Inspect the toolpath preview to make sure the spot drill does not plunge too deep. | Figure 24. Inspect the toolpath
25. You can efficiently create an operation to drill the holes by duplicating and tweaking the existing Drill operation. Select the Drill operation, right-click it, then choose Duplicate from the menu. | Figure 25. Duplicate the Drill operation

## Slide 15
26. Edit the new Drill operation by right- clicking it and choosing Edit from the menu. Click the dialog’s Select to change the operation’s tool. | Figure 26. Edit the new Drill operation
27. Navigate to the Learn CAM 90 – Metric tool library and choose Tool 2. Click the Select Tool dialog’s Select. | Figure 27. Choose the operation’s tool

## Slide 16
28. Continue to the Passes tab. Choose the Hole bottom option in the Bottom Height section’s From menu, then activate the Drill Tip through Bottom option. | Figure 28. Adjust the bottom height
29. Continue to the Passes tab and change the Cycle Type to Chip breaking – partial retract. OK the dialog. | Figure 29. Change the cycle type

## Slide 17
30. Inspect the toolpath to make sure the holes are correctly drilled. | Figure 30. Inspect the toolpath
31. Create a new drilling operation by clicking Drilling> Drill, then click the Drill dialog’s Select to choose the correct tool. | Figure 31. Create a new Drill operation

## Slide 18
32. Navigate to the Learn CAM 90 – Metric tool library and choose Tool 3. Click the Select Tool dialog’s Select. | Figure 32. Choose the operation’s tool
33. Select the five hole faces shown in the image on the right. | Figure 33. Select the hole faces

## Slide 19
34. Continue to the Passes tab and choose the Tapping option from the Cycle Type menu. | Figure 34. Change the cycle type
35. Navigate to the Heights tab and enter -2 mm into the Bottom Height section’s Offset box so that the tap fully threads the entire hole. OK the dialog to generate the toolpath. | Figure 35. Adjust the bottom height

## Slide 20
36. The next operation needs to cut the model’s perimeter but also needs to leave some tabs so the part doesn’t fall out of the stock. Click 2D> 2D Contour. | Figure 36. Create a 2D Contour operation
37. Click the 2D Contour dialog’s Select to choose the operation’s tool. Navigate to the Learn CAM 90 – Metric tool library and select Tool 6. Click the Select Tool dialog’s Select. | Figure 37. Select the operation’s tool

## Slide 21
38. Continue to the Geometry tab, then select the edge shown in the image on right as the Contour Selection. | Figure 38. Select the edge
39. Activate Tabs option, then enter 10 mm into the Tab Width box. Enter 3 mm into the Tab Height box, then enter 110 mm into the Tab Distance box. | Figure 39. Activate the Tabs option

## Slide 22
40. You can also manually place tabs on the part. For the Manual Tabs selection, click the perimeter in 4 places to add additional tabs. These tabs will allow the part to stay with the stock as the perimeter is machined. | Figure 40. Manually add additional tabs
41. Continue to the Passes tab and activate the Multiple Depths option. Enter 2 mm into the Maximum Roughing Stepdown box, then OK the dialog to generate the toolpath. | Figure 41. Configure the Multiple Depths option

## Slide 23
42. Inspect the toolpath and notice how the tabs keep the part joined with the stock. These tabs could be made smaller to make the part easier to separate from the stock, but a chamfer operation needs finalize the part. Save the file. | Figure 42. Inspect the toolpath