## Slide 1
Step-by-step guide
Stock facing the base
Create a Facing operation to remove a stock body’s extra top material.
Learning objectives:
Create a Facing toolpath with an end mill.
The completed exercise

## Slide 2
1. Upload and open the supplied Cell Phone Metric – Face.f3d file. | Figure 1. Open the file
2. Instead of opening the supplied file, you could use this as an opportunity to practice creating a setup by creating your own file. If you want to do this, open the supplied Cell Phone Stand – Metric Assembly.f3d file, derive the Stand Body into its own file, then create a setup. | Figure 2. Note how to create your own file

## Slide 3
3. A Facing operation is typically a program’s first operation. This operation removes the stock’s extra top material and ensures a high-quality finish. | Figure 3. Notice the stock needs to be faced
4. Create a Facing operation by clicking 2D> Face. | Figure 4. Create a Facing operation

## Slide 4
5. Click the Face dialog’s Select to choose an appropriate tool for the operation. | Figure 5. Click Select
6. Inside the Select Tool dialog, navigate to the Learn Cam 90 – Metric tool library. | Figure 6. Open the tool library

## Slide 5
7. Some machines cannot support a large diameter tool like this library’s 50 mm face mill. Select Tool 7 which is a 12 mm flat endmill. | Figure 7. Select the tool
8. Click the Select Tool dialog’s Select. | Figure 8. Click Select

## Slide 6
9. OK the Face dialog to accept all the default settings and generate the toolpath. | Figure 9. OK the dialog
10. Inspect the toolpath and notice that the operation faces the entire stock body using 10 passes. Save the file. | Figure 10. Inspect the toolpath