## Slide 1
Step-by-step guide
Use roughing toolpaths to remove material from the base
Create and customize 2D and 3D Adaptive Clearing operations to rough a part’s geometry.
Learning objectives:
Create a 2D Adaptive toolpath.
Create a 3D Adaptive toolpath.
The completed exercise

## Slide 2
1. Open the supplied Cell Phone Stand Metric – Rough.f3d file or continue with your file from the previous module. Note that the supplied file does not have active links to the external parent files, so it’s better to use your own file if possible. | Figure 1. Open the file
2. A 2D Adaptive Clearing operation could begin roughing this part’s geometry. Click 2D> 2D Adaptive Clearing. | Figure 2. Create a 2D Adaptive Clearing operation

## Slide 3
3. Make sure that the 12 mm flat endmill is displayed in the 2D Adaptive dialog. If you need to change the tool, click Select, navigate to the Learn CAM 90 – Metric tool library and select Tool 7. | Figure 3. Verify the operation’s tool
4. Continue to the 2D Adaptive dialog’s Geometry tab and select the face shown in the image on the right. Notice that there is only a single dark blue edge which indicates that Fusion will treat this selection like an open pocket. Verify the default settings in the dialog’s other tabs, then OK the dialog. | Figure 4. Select the face

## Slide 4
5. Inspect the toolpath and notice that it focuses on cutting the face you selected. A different type of operation might be more suitable for roughing this part. | Figure 5. Inspect the toolpath
6. The 2D Adaptive operation can be suppressed because a new operation will replace it. Right-click the 2D Adaptive operation and choose Suppress from the menu. | Figure 6. Suppress the operation

## Slide 5
7. Click the dialog’s Yes to confirm that you want to suppress the operation. | Figure 7. Click Yes
8. Create a new operation by clicking 3D> Adaptive Clearing. This operation is considered model aware because it analyzes the entire part’s geometry instead of a specific face or chain. | Figure 8. Create a 3D Adaptive Clearing operation

## Slide 6
9. Continue to the Adaptive dialog’s Geometry tab and notice that the bodies are colored either green or gold. The vise jaws and parallels were identified as fixtures in the setup, so Fusion knows to avoid them; that’s why these bodies are gold. Instead, the operation will focus on the green body. Verify the default settings in the dialog’s other tabs, then OK the dialog. | Figure 9. Inspect the default selection
10. Inspect the toolpath and notice that it uses the current tool to rough as much as it can. | Figure 10. Inspect the toolpath

## Slide 7
11. Also notice that the Browser has a warning icon next to the operation. Click this icon to learn more about the warning. | Figure 11. Note the warning
12. Fusion has lifted the operation’s Retract height to the Safe height. Close the dialog. | Figure 12. Inspect the warning

## Slide 8
13. Right-click the Adaptive operation and choose Edit from the menu. | Figure 13. Edit the operation
14. Navigate to the Heights tab and increase the Retract Height section’s Offset value to 10 mm. OK the dialog to update the toolpath. | Figure 14. Adjust the Retract height

## Slide 9
15. Inspect the Browser and notice that Fusion removed the warning icon. | Figure 15. Inspect the Browser
16. In the Browser, right-click the Adaptive operation and choose Duplicate from the menu. | Figure 16. Duplicate the operation

## Slide 10
17. Edit the new Adaptive operation by right-clicking it and choosing Edit from the menu. | Figure 17. Edit the new operation
18. Click Select to choose a smaller tool for the new operation. | Figure 18. Click Select

## Slide 11
19. Navigate to the Learn CAM 90 – Metric tool library and select Tool 6. This 6 mm flat endmill will be able to remove some of the material that the 12 mm end mill could not reach. Click the Select Tool dialog’s Select. | Figure 19. Select the tool
20. Continue to the Adaptive dialog’s Geometry tab and make sure the Remaining stock option is selected in the Define Stock By menu. This option allows the operation to ignore the material removed by previous operations. OK the dialog to accept the default values and generate the toolpath. | Figure 20. Make sure Remaining stock is selected

## Slide 12
21. Inspect the toolpath and notice that the stock more closely matches the modeled shape. | Figure 21. Inspect the toolpath
22. However, notice the operation left an extremely thin section on the bottom of the part. This is not thick enough to stabilize the part during future operations. | Figure 22. Notice the thin section

## Slide 13
23. Edit the newest Adaptive operation and navigate to the Heights tab. Choose the Selection option in the Bottom Height section’s From menu. | Figure 23. Adjust the bottom height
24. For the dialog’s Bottom Reference selection, choose the edge shown in the image on the right. OK the dialog to update the toolpath. | Figure 24. Select the bottom reference

## Slide 14
25. Inspect the result and notice that the thicker section will better stabilize the part during future operations. Save the file. | Figure 25. Inspect the toolpath