## Slide 1
Step-by-step guide
Use finishing toolpaths to finalize a base model
Create and compare several operations to finish a part’s geometry.
Learning objectives:
Create a 3D Scallop toolpath.
Create a 2D Contour toolpath with tabs.
Create a 3D Contour toolpath.
The completed exercise

## Slide 2
1. Continue with your file from the previous module or open the supplied Cell Phone Stand Metric – Finish.f3d file. If you decide to open the supplied file, notice the links to the external parent files are broken. For this reason, it is better to use your own file if possible. | Figure 1. Open the file
2. A 2D Pocket operation could begin finishing this part. Click 2D> 2D Pocket. | Figure 2. Create a new 2D Pocket operation

## Slide 3
3. Click the 2D Pocket dialog’s Select to choose an appropriate tool for this operation. Choose Tool 7, which is a 12 mm flat endmill. You might have to source this tool from the Learn CAM 90 – Metric tool library. Click the Select Tool dialog’s Select. | Figure 3. Select the tool
4. Continue to the dialog’s Geometry tab and select the face shown in the image on the right. The dark blue line highlights only a single edge which means the operation will treat the selection as an open pocket. | Figure 4. Select the face

## Slide 4
5. Continue to the Passes tab and deactivate the Stock to Leave option. OK the dialog to generate the toolpath. |  | Figure 5. Deactivate the Stock to Leave option
6. Notice the strategy the operation uses for machining this open pocket. Each pass is allowed to extend beyond the sides of the modeled geometry. | Figure 6. Inspect the toolpath | 

## Slide 5
7. Now that the part’s flat face is fully machined, some 3D operations can be used to cut the fillet geometry. Click 3D> Contour. | Figure 7. Create a 3D Contour operation
8. Click the Contour dialog’s Select to choose the operation’s tool. Navigate to the Learn CAM 90 – Metric tool library and select Tool 8. This 4 mm ball nose mill will be able to properly cut the model’s fillets. Click the Select Tool dialog’s Select. | Figure 8. Choose the operation’s tool

## Slide 6
9. Continue to the dialog’s Geometry tab. The operation’s attention needs to be focused on a specific area instead of analyzing the entire model. Activate the Model option. | Figure 9. Activate the Model option
10. Select the four faces shown in the image on the right as the dialog’s Model Surfaces selection. OK the dialog to generate the toolpath. | Figure 10. Select the model surfaces

## Slide 7
11. Inspect the toolpath and notice that the operation machines more than the faces you selected. | Figure 11. Inspect the toolpath
12. Edit the Contour operation by right- clicking it and choosing Edit from the menu. Navigate to the Geometry tab and click the plus icon to add a new surface group. | Figure 12. Add a new surface group

## Slide 8
13. Select the same four faces you selected in Step 10. Make sure the Machine surface option is selected in the dialog’s Action section, then OK the dialog. | Figure 13. Create a new surface group
14. The original model group needs to be identified as geometry to avoid. Right-click the Model group and choose Edit from the menu. | Figure 14. Edit the Model group

## Slide 9
15. Select the Avoid surface option in the dialog’s Action section, then OK the dialog. | Figure 15. Choose the Avoid surface option
16. Most of the model has a red color to identify it as Avoid surfaces, but the four faces you selected are green to indicate they are cutting faces. OK the dialog to generate the toolpath. | Figure 16. Inspect the preview

## Slide 10
17. Inspect the toolpath and notice that it machines only the faces you selected. However, the operation could be tweaked to add more passes for a smoother finish. | Figure 17. Inspect the toolpath
18. Edit the Contour operation again, then navigate to the Passes tab. Enter 0.05 mm into the Cusp Height box, then OK dialog. | Figure 18. Edit the operation’s cusp height

## Slide 11
19. Inspect the toolpath and notice that several more passes are added to the operation. | Figure 19. Inspect the toolpath
20. Some other operations could be used to cut this geometry. Select the Contour operation, right-click it, and choose Suppress from the menu. | Figure 20. Suppress the Contour operation

## Slide 12
21. Click the dialog’s Yes to suppress the operation. | Figure 21. Click Yes
22. Create a new operation by clicking 3D> Scallop. | Figure 22. Create a Scallop operation

## Slide 13
23. Navigate to the Scallop dialog’s Heights tab and choose the Selection option in the Bottom Height section’s From menu. | Figure 23. Adjust the bottom height
24. For the dialog’s Bottom Reference selection, choose the point shown in the image on right. | Figure 24. Select the bottom reference

## Slide 14
25. Navigate to the Geometry tab and activate the Slope option. This option can tell the operation to avoid machining perfectly horizontal or vertical surfaces. Enter 1 deg into the From Slope Angle box, then enter 89 deg into the To Slope Angle box. The operation will ignore anything less than 1° or more than 89°. | Figure 25. Configure the Slope option
26. Continue to the Passes tab and enter 0.1 mm into the Stepover box. OK the dialog. | Figure 26. Adjust the stepover value

## Slide 15
27. Notice the operation is using many passes to create a very fine surface finish. However, the perimeter chamfers are also being machined. This is not nearly as efficient as using a Chamfer operation, but is a possible solution. | Figure 27. Inspect the toolpath
28. Create a new 2D Contour operation by clicking 2D> 2D Contour. | Figure 28. Create a new 2D Contour operation

## Slide 16
29. Click the dialog’s Select to choose an appropriate tool for the operation. Choose Tool 6, then click the Select Tool dialog’s Select. | Figure 29. Select the tool
30. Navigate to the Geometry tab and select the edge shown in the image on the right as the Contour Selection. | Figure 30. Select the edge

## Slide 17
31. Activate the Tabs option, then enter 10 mm into the Tab Width box. Enter 2 mm into the Tab Height box, then enter 100 mm into the Tab Distance box. | Figure 31. Configure the Tabs option
32. For the dialog’s Manual Tabs option, click the model’s perimeter to place two additional tabs. The model should now have four tabs total. OK the dialog to generate the toolpath. | Figure 32. Manually add tabs

## Slide 18
33. Notice that the operation leaves a fine finish that closely matches the modeled geometry. Save the file. | Figure 33. Inspect the result