## Slide 1
Step-by-step guide
Chamfer edges on the base model
Create and compare a few 2D options for cutting a part’s 3D chamfer.
Learning objectives:
Create a Chamfer toolpath to deburr edges.
The completed exercise

## Slide 2
1. Continue with your file from the previous module or open the supplied Cell Phone Stand Metric – Debur.f3d file. It’s better to use your file if you can because the supplied file’s links to the external parent file are broken. | Figure 1. Open the file
2. This part’s only remaining feature that needs to be cut is the modeled chamfer. This chamfer will be slightly trickier to cut because it is not a simple 2D shape. Several operations could be used to cut this feature. | Figure 2. Notice the chamfer that needs to be cut

## Slide 3
3. To explore the first option, click 2D> 2D Chamfer. | Figure 3. Create a Chamfer operation
4. Click the dialog’s Select to choose an appropriate tool for this operation. | Figure 4. Click Select

## Slide 4
5. Navigate to the Learn CAM 90 – Metric tool library and select Tool 4. | Figure 5. Choose the tool
6. Click the Select Tool dialog’s Select. | Figure 6. Click Select

## Slide 5
7. Select the edge shown in the image on the right and notice that Fusion previews a flat, planar selection. OK the dialog. | Figure 7. Select an edge
8. Click the Browser’s warning icon to learn about the issue. | Figure 8. Click the warning icon

## Slide 6
9. The warning dialog mentions that the toolpath is empty. Click the dialog’s Close. | Figure 9. Learn about the warning
10. Edit the 2D Chamfer operation by right-clicking it and choosing Edit from the menu. | Figure 10. Edit the operation

## Slide 7
11. Navigate to the Passes tab and enter 0 mm into the Chamfer Clearance box. OK the dialog to generate the toolpath. | Figure 11. Adjust the Chamfer Clearance value
12. Inspect the preview and notice that the operation does not chamfer the full perimeter. Only the flat section can be chamfered using the 2D Chamfer operation. | Figure 12. Inspect the preview

## Slide 8
13. A different tool could be used to cut this feature. Click 2D> Trace. | Figure 13. Create a Trace operation
14. Navigate to the Geometry tab and select the edge shown in the image on right. The highlighted edges are not limited to a 2D plane. OK the dialog to generate the toolpath. | Figure 14. Select the edge

## Slide 9
15. Inspect the toolpath and notice that the tool gouges the stock. A larger section of the tool engages the stock as the geometry ramps towards vertical. | Figure 15. Inspect the toolpath
16. Neither the 2D Chamfer nor the Trace operations are appropriate for this geometry. Right-click them and choose Delete from the menu. | Figure 16. Delete the unnecessary operations

## Slide 10
17. The 3D menu’s Deburr operation could be used if you activate your manufacturing extensions. However, the Scallop operation could be tweaked to cut this feature. Right- click the Scallop operation and choose Edit from the menu. | Figure 17. Edit the Scallop operation
18. Navigate to the Geometry tab and activate the Contact Point Boundary option. OK the dialog. | Figure 18. Activate the Contact Point Boundary option

## Slide 11
19. Notice the tool extends far enough to fully cut the feature. However, this will significantly increase the machining time. | Figure 19. Inspect the toolpath
20. Right-click the Scallop operation and choose Machining Time from the menu. | Figure 20. Inspect the operation’s machining time

## Slide 12
21. Fusion expects the operation to run for more than 26 minutes. Close the Machining Time dialog. | Figure 21. Inspect the operation’s information
22. Edit the Scallop operation again and navigate to the Passes tab. Increase the Stepover value to 0.25 mm, then OK the dialog. | Figure 22. Adjust the Scallop operation

## Slide 13
23. This modification will cut a slightly rougher finish but is expected to run only 10.5 minutes. | Figure 23. Inspect the toolpath

## Slide 14
24. Select the last operation inside the Browser’s Setup1. This will preview all of the material removed from the stock. Inspect the stock to make sure all of the modeled geometry is correctly cut. | Figure 24. Inspect the stock
25. You can temporarily hide the toolpaths to make the model easier to see. To do this, you can toggle the Toolpaths option in the Navigation bar’s Toolpath visibility menu. Alternately, the keyboard shortcut is F7. Save the file. | Figure 25. Toggle the toolpaths