## Slide 1
Step-by-step guide
Use simulation to validate stock removal
Validate an entire setup or individual operations using Fusion’s simulation tool.
Learning objectives:
Simulate toolpaths.
Modify toolpath parameters.
The completed exercise

## Slide 2
1. Continue with one of your fully programmed parts or open the supplied Cell Phone Metric – Final.f3d file. | Figure 1. Open the file
2. Fusion can animate an entire setup or individual operations to verify that the operation correctly cuts the modeled geometry. Select Setup1. | Figure 2. Select Setup1

## Slide 3
3. Open the simulation by clicking Actions> Simulate. | Figure 3. Simulate the setup
4. The stock body is displayed in blue, and the tool, holder, and fixtures have reduced opacity. | Figure 4. Inspect the visible bodies

## Slide 4
5. The Simulate dialog’s options can be used to customize the simulation. Make sure the Comparison option is selected from the Colorization menu so that you can easily tell if each operation removes the proper amount of material. |  | Figure 5. Change the colorization type
6. Click in an open area of the canvas and drag your cursor to the right. Notice the simulation plays as you drag the cursor. | Figure 6. Click and drag your cursor | 

## Slide 5
7. You can also click the timeline at the bottom of the screen to jump to specific points. This timeline is broken into segments representing each of the setup’s operations. | Figure 7. Click the timeline
8. A third way to play the animation is to press Play near the Bottom of the Screen. The slider below the Play button allows you to adjust the animation’s forward or reverse speed. | Figure 8. Press Play

## Slide 6
9. Because you selected the Comparison option in Step 5, Fusion applies a color to each face. Blue faces indicate areas that need more material removed. Green faces indicate that the proper amount of material has been removed, and red faces indicate that too much material has been removed. This model did not have a chamfer feature on the large center hole and the tapped holes’ threads were not modeled. Fusion assumes too much material has been removed in these areas because the machined part does not match the modeled geometry. In this instance, these red faces can be ignored. | Figure 9. Inspect the result
10. After you finish exploring the simulation, click Exit Simulation> Exit Simulation. Alternately, you could click the Simulate dialog’s Exit Simulation. | Figure 10. Exit the simulation

## Slide 7
11. After verifying the simulation, you could edit one of your operations. For instance, Setup1’s final operation is the 2D Chamfer that cuts the large hole’s chamfer. You could edit this operation and reduce the Chamfer Width value to 0.25 mm. | Figure 11. Edit an operation
12. After you OK the dialog, select the operation. | Figure 12. Select the operation

## Slide 8
13. You can simulate the individual operation by clicking Actions> Simulate. | Figure 13. Simulate the selected operation
14. Play the simulation and note your modification’s effects. In this instance, the chamfered edge is much smaller. Exit the simulation after you finish analyzing the part, then save the file. | Figure 14. Analyze the simulation