## Slide 1
Step-by-step guide
Post process toolpaths
Convert an NC program to machine-readable G-Code so that a machine can cut the parts.
Learning objectives:
Post process toolpaths.
Review G-Code.
The completed exercise

## Slide 2
1. Continue with the file from the previous module or open the supplied Cell Phone Metric – Final.f3d file. | Figure 1. Open the file
2. You can convert your NC programs to machine-readable G-Code by post processing them. Right-click the Setup Stand, then choose Post Process from the menu. | Figure 2. Post process an NC code

## Slide 3
3. Fusion uses the selected post to convert all of the NC program’s selected toolpaths to machine-readable G-Code. This G-Code will open inside an external code editor app. | Figure 3. Inspect the G-Code
4. The program name and number are displayed on Line 2. The comment is displayed on Line 3, and the tools are described on Lines 4 through 9. | Figure 4. Notice the name, comment, and tools

## Slide 4
5. The first operation’s name is on Line 14, the tool is on Line 15, the spindle speed is on Line 16, and the WCS location is on Line 18. Explore the code to make sure everything looks appropriate, then save the file. This file can be sent to the machine that will cut the parts. | Figure 5. Inspect the G-Code